## Slide 1: Ints (cont)

## Slide 2: Lesson plan
2’s complement
  The negation trick
History of technology
  From 8-bit to 64-bit machines
Byte ordering
  Big vs. small endian
Floating points

## Slide 3: Two’s complement
11011000
= 1*(-27) +1*26 +0*25 +1*24 +1*23 +0*22 +0*21+0*20 = -40
11111111
= 1*(-27) +1*26 +1*25 +1*24 +1*23 +1*22 +1*21+1*20 = -1

## Slide 4: 2’s complement: find a number’s negation
00101000
(40)10
(-40)10
??
A useful trick to do negation
Step-1: flip all bits
00101000
(40)10
11010111
Step-2: add 1
+ 00000001
11011000
(-40)10

## Slide 5: Why does the negation trick work
b with bits flipped

## Slide 6: Negation trick lets us find bit pattern of a negative number more easily
The bit pattern of -33?

## Slide 7: Negation trick helps computers do subtraction
0 0 0 0 0 1 0 1
0 0 0 0 0 1 1 1
-
(5)10
(7)10
Instead of doing this:
0 0 0 0 0 1 0 1
0 0 0 0 0 1 1 1
(5)10
Do this instead:
(7)10
1 1 1 1 1 0 0 0
+ 0 0 0 0 0 0 0 1
1 1 1 1 1 1 1 0
(-2)10
1 1 1 1 1 1 1 0
(-2)10
(-7)10

## Slide 8: Intel 8080 (1974)
CPU
0x4c
0x4c
0x1e
0xaf
0x0f
Memory
0xcb
0xea
0xba
0x00
0xff
0x8c
……
0x4c
Arithmetic Logic
Unit
registers
0xb0
0xa9
…
0xa1
0xa2
0xa3
0xa4
0xa5
0xa6
0xa7
0xa8
8 bits machine – 8 bits length of
Memory – processor transfer
CPU Register
Memory Address

## Slide 9: Intel 386 (1985)
CPU
0x4c1eaf0f
0x4c
0x1e
0xaf
0x0f
Memory
0xcb
0xea
0xba
0x00
0xff
0x8c
……
0x4c1eaf0f
Arithmetic Logic
Unit
registers
0x000000b0
0x000000a9
…
0x000000a1
0x000000a2
0x000000a3
0x000000a4
0x000000a5
0x000000a6
0x000000a7
0x000000a8
32 bits machine – 32 bits length of
Memory – processor transfer
CPU Register
Memory Address

## Slide 10: AMD K8 (2000), Intel Pentium 4 and later
CPU
0x00bacbea4c1eaf0f
0x4c
0x1e
0xaf
0x0f
Memory
0xcb
0xea
0xba
0x00
0xff
0x8c
……
0x00bacbea4c1eaf0f
Arithmetic Logic Unit
registers
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
64 bits machine – 64 bits length of
Memory – processor transfer
CPU Register
Memory Address

## Slide 11: C’s Integer data types on 64 bits machine
 | Length | Min | Max
char | 1 byte | -27 | 27 - 1
unsigned char | 1 byte | 0 | 28 - 1
short | 2 bytes | -215 | 215 - 1
unsigned short | 2 bytes | 0 | 216 - 1
int | 4 bytes | -231 | 231 - 1
unsigned int | 4 bytes | 0 | 232 - 1
long | 8 bytes | -263 | 263 - 1
unsigned long | 8 bytes | 0 | 264 - 1

## Slide 12: Your first C program
#include <stdio.h>
int
main()
{
char x = -127;
char y = 0x81;
char z = x + y;
printf(“hello world sum is %d\n”, z);
}
$ gcc helloworld.c
$ ./a.out
1 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
0 0 0 0 0 0 1 0
-127
-127
1
2

## Slide 13: Memory layout for multi-byte integers
CPU
Memory
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address: 0x00…00a2
int a

## Slide 14: Memory layout for multi-byte integers: 2 ways
CPU
Memory
0x78
0x56
0x34
0x12
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address: 0x00…00a2
int a

## Slide 15: Memory layout for multi-byte integers: 2 ways
CPU
Memory
0x12
0x34
0x56
0x78
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address: 0x00…00a2
int a

## Slide 16: Memory layout – Little Endian
CPU
Memory
0x12
0x34
0x56
0x78
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address: 0x00…00a2
int a
  Least significant byte in smallest address,
  e.g, laptops, and server machines

## Slide 17: Advantages of Little Endian
0x12345678
0x12131415
+
Processor performs the calculation
from the least significant bit
Processor can simultaneously
perform memory transfer and
calculation.

## Slide 18: Advantages of Little Endian
CPU
Memory
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address of variable a: 0x00…00a2
int a

## Slide 19: Advantages of Little Endian
CPU
Memory
0x12
0x34
0x56
0x78
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address: 0x00…00a2
int a

## Slide 20: Advantages of Little Endian
CPU
Memory
0x12
0x34
0x56
0x78
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address: 0x00…00a2
int a
short b = (short)a
Directly get the data from
0x00…00a2
short b

## Slide 21: Memory layout – Big Endian
CPU
Memory
0x78
0x56
0x34
0x12
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address: 0x00…00a2
int a
  Most significant byte in smallest address,
  e.g, ARM architecture >v3 (cellphones, ipads)

## Slide 22: Advantages of Big Endian
Test whether the number is positive or negative by looking at the byte at offset zero.