## Slide 1: Integers (continued) Floating point
Jinyang Li

## Slide 2: Lesson plan
2’s complement
  The negation trick
A short history of processors:
  from 8-bit to 64-bit machines
Byte ordering
  Big vs. small endian
Intro to floating points

## Slide 3: Two’s complement: 8-bit signed integer
11011000
= 1*(-27) +1*26 +0*25 +1*24 +1*23 +0*22 +0*21+0*20 = -40
11111111
= -1
01011000
= 0*(-27) +1*26 +0*25 +1*24 +1*23 +0*22 +0*21+0*20 = 88
00000000
= 0
10000000
= -27= -128
01111111
= 27-1= -127

## Slide 4: 2’s complement: find a number’s negation
00101000
(40)10
(-40)10
??
A useful trick to do negation:
Step-1: flip all bits
Step-2: add 1
00101000
(40)10
11010111
+00000001
11011000
(-40)10
Step-1: flip bits
Step-2:

## Slide 5: Why does the negation trick work
b with bits flipped

## Slide 6: Negation trick lets us find bit pattern of a negative number more easily
The bit pattern of 8-bit signed integer -33?

## Slide 7: Negation trick lets us find bit pattern of a negative number more easily
Answer:
33 = (00010001)2
Apply negation trick: (11101110)2+1=(11101111)2
The bit pattern of 8-bit signed integer -33?

## Slide 8: Negation trick helps computers do subtraction
(-7)10
0 0 0 0 0 1 0 1
0 0 0 0 0 1 1 1
-
(5)10
(7)10
Instead of doing this:
0 0 0 0 0 1 0 1
(5)10
Do this instead:
0 0 0 0 0 1 1 1
(7)10
1 1 1 1 1 0 0 0
0 0 0 0 0 0 0 1
1 1 1 1 1 1 1 0
(-2)10
1 1 1 1 1 1 1 0
(-2)10
+
Works for both signed and unsigned subtraction

## Slide 9: The evolution of integer sizes in processors

## Slide 10: 8-bit processors: e.g. Intel 8080 (1974)
CPU
0x4c
0x4c
0x1e
0xaf
0x0f
Memory
0xcb
0xea
0xba
0x00
0xff
0x8c
……
0x4c
Arithmetic Logic
Unit
registers
0xb0
0xa9
…
0xa1
0xa2
0xa3
0xa4
0xa5
0xa6
0xa7
0xa8
8 bits machine: 8 bits length of
Memory – processor transfer
CPU register
Nowadays: 8-bit processor (microcontroller)
Is used for embedded systems

## Slide 11: 32-bit processors: Intel 386 (1985)
CPU
0x4c1eaf0f
0x4c
0x1e
0xaf
0x0f
Memory
0xcb
0xea
0xba
0x00
0xff
0x8c
……
0x4c1eaf0f
Arithmetic Logic
Unit
registers
0x000000b0
0x000000a9
…
0x000000a1
0x000000a2
0x000000a3
0x000000a4
0x000000a5
0x000000a6
0x000000a7
0x000000a8
32 bits machine: 32 bits length of
Memory – processor transfer
CPU register
Memory address
Most commonly used desktop/server processors
in the latest 80s to early 00s

## Slide 12: 64-bit processors: Intel Pentium 4 (2000)
CPU
0x00bacbea4c1eaf0f
0x4c
0x1e
0xaf
0x0f
Memory
0xcb
0xea
0xba
0x00
0xff
0x8c
……
0x00bacbea4c1eaf0f
Arithmetic Logic Unit
registers
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
64 bits machine: 64 bits length of
Memory – processor transfer
CPU register
Memory address
Nowadays: Intel/AMD 64-bit x86 processors used for servers/laptops
Mobile phones/tablets: 64-bit ARM processors (made by Apple/Qualcomm/Samsung etc)

## Slide 13: C’s Integer data types on 64 bits machine
 | Length | Min | Max
char | 1 byte | -27 | 27 - 1
unsigned char | 1 byte | 0 | 28 - 1
short | 2 bytes | -215 | 215 - 1
unsigned short | 2 bytes | 0 | 216 - 1
int | 4 bytes | -231 | 231 - 1
unsigned int | 4 bytes | 0 | 232 - 1
long | 8 bytes | -263 | 263 - 1
unsigned long | 8 bytes | 0 | 264 - 1

## Slide 14: Your first C program
#include <stdio.h>
int
main()
{
char x = -127;
char y = 0x81;
char z = x + y;
printf(“hello world sum is %d\n”, z);
}
$ gcc helloworld.c
$ ./a.out
1 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
0 0 0 0 0 0 1 0
-127
-127
1
2

## Slide 15: Memory layout for multi-byte integers
CPU
Memory
……
Arithmetic Logic Unit
registers
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
4-byte

## Slide 16: Memory layout: Little Endian
CPU
Memory
0x12
0x34
0x56
0x78
……
Arithmetic Logic Unit
registers
int x = 0x12345678
x:
  Little endian:
  Least significant byte stored at smallest address
  Used in x86 processors (servers/laptops) and most ARM (phones/tablets) implementation
0x12 | 0x34 | 0x56 | 0x78
address of x
addr+1
addr
addr+2
addr+3

## Slide 17: Advantage of Little Endian
0x12345678
0x12131415
+
Processor performs the calculation
from the least significant bit
Processor can simultaneously
perform memory transfer and
calculation.

## Slide 18: Another advantage of Little Endian
CPU
Memory
0x12
0x34
0x56
0x78
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678;
…
short b = (short)a;
Casting a larger integer to a smaller one requires no explicit conversion.
a:
b:
addr+1
addr
addr+2
addr+3

## Slide 19: Memory layout: Big Endian
CPU
Memory
0x78
0x56
0x34
0x12
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678;
…
  Big Endian:
  Most significant byte stored at smallest address
  ARM processors (phones/tablets) in principle support both endian
0x12 | 0x34 | 0x56 | 0x78
a:
addr+1
addr
addr+2
addr+3

## Slide 20: Advantages of Big Endian
Quick to test whether the number is positive or negative
  Examine byte stored at the address offset zero.

## Slide 21: Breakout time!

## Slide 22: Breakout exercises
2's complement of -15 (8-bit, in hex)
Computers use different hardware circuitry to perform addition vs subtraction.
Computers use different hardware circuitry to perform unsigned addition vs. signed addition.
long x = 0xdeadbeef01234567 Assume a Little Endian machine, and x is stored in memory starting at address a. What 1-byte value is stored at address a+3?

## Slide 23: Breakout exercises
2's complement of -15 (8-bit, in hex)
  0xf1
Computers use different hardware circuitry to perform addition vs subtraction.
  False
Computers use different hardware circuitry to perform unsigned addition vs. signed addition.
  False
long x = 0xdeadbeef01234567 Assume a Little Endian machine, and x is stored in memory starting at address a. What 1-byte value is stored at address a+3?
  0x01

## Slide 24: Lesson plan
2’s complement
  The negation trick
A short history of processors:
  From 8-bit to 64-bit machines
Byte ordering
  Big vs. small endian
Intro to floating points

## Slide 25: Representing Real Numbers using bits
-
+
1
2
-3
-2
-1
3
2n-1-1
2n-1
0
2n-1
Unsigned n-bit integers
Signed n-bit integers
What about real numbers?

## Slide 26: Decimal Representation
Real Numbers | Decimal Representation (Expansion)
11 / 2 | (5.5)10
1 / 3 | (0.3333333...)10
√2 | (1.4128…)10

## Slide 27: Decimal Representation
Real Numbers | Decimal Representation (Expansion)
11 / 2 | (5.5)10
1 / 3 | (0.3333333...)10
√2 | (1.4128…)10
(5.5)10 = 5 * 100+ 5 * 10-1
(0.333333...)10 = 3 * 10-1 + 3 * 10-2 + 3 * 10-3 + ...
(1.4128...)10 = 1 * 100 + 4 * 10-1 + 1 * 10-2 + 2 * 10-3 + ...

## Slide 28: Decimal Representation
Real Numbers | Decimal Representation (Expansion)
11 / 2 | (5.5)10
1 / 3 | (0.3333333...)10
√2 | (1.4128…)10
(1.4128...)10 = 1 * 100 + 4 * 10-1 + 1 * 10-2 + 2 * 10-3 + ...

## Slide 29: Binary Representation
(5.5)10 =
= (101.1)2

## Slide 30: Binary Representation
(0.333333...)10 = 1 / 4 + 1 / 16 + 1 / 64 + ...
= (0.01010101...)2

## Slide 31: Binary Representation
2p
2p-1
2
1
1/2
1/4
1/2q
.

## Slide 32: Binary representation
What’s the decimal value of (10.01)2

## Slide 33: Binary representation
What’s the decimal value of (10.01)2
Answer: 2.25

## Slide 34: Strawman representation: fixed point
s | b14 | b13 | b12 | … | b1 | b0 | b-1 | b-2 | b-3 | … | b-14 | b-15 | b-16
sign
15 bits
Fixed position e.g. middle
16 bits

## Slide 35: Fixed point representation
s | b14 | b13 | b12 | … | b1 | b0 | b-1 | b-2 | b-3 | … | b-14 | b-15 | b-16
sign
15 bits
16 bits
Example: ( 10.011 )2
0 | 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 | 0 1 1 0 0 0 0 0 0 0 0 0 0 0 0

## Slide 36: Problems of Fixed Point
s | b14 | b13 | b12 | … | b1 | b0 | b-1 | b-2 | b-3 | … | b-14 | b-15 | b-16
15 bits
16 bits
Range?
Precision?
-
+
0

## Slide 37: Problems of Fixed Point
  Limited range and precision: e.g., 32 bits
    Range: [-215+2-16,215-2-16 ]
    Highest precision: 2-16
Rarely used (No built-in hardware support)
s | b14 | b13 | b12 | … | b1 | b0 | b-1 | b-2 | b-3 | … | b-14 | b-15 | b-16
15 bits
16 bits

## Slide 38: Floating point: key idea
Limitation of fixed point:
  Even spacing results in hard tradeoff between high precision and high magnitude
How about un-even spacing between numbers?
-
+
0

## Slide 39: Floating Point: decimal
Based on exponential notation (aka normalized scientific notation)
r10 = +M * 10E, where 1 <= M < 10
M: significant (mantissa), E: exponent

## Slide 40: Floating Point: decimal
Example:
365.25 = 3.6525 * 102
0.0123 = 1.23 * 10-2
Decimal point floats to the position immediately
after the first nonzero digit.

## Slide 41: Floating Point: binary
Binary exponential representation
(5.5)10 = (101.1)2 = (1.011)2 * 22
r10 = +M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…bn )2
M: significant, E: exponent

## Slide 42: Floating Point
Binary exponential representation
(5.5)10 = (101.1)2 = (1.011)2 * 22
Normalization: give a number r, obtain its normalized representation
Normalized
representation
of r
r10 = +M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…bn )2
M: significant, E: exponent

## Slide 43
Normalized representation of (10.25)10?

## Slide 44
Normalized representation of (10.25)10 ?
Answer: (10.25)10 = (1010.01)2 = (1.01001)2 * 23

## Slide 45: Normalized representation in computer
31
+M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…b23 )2
exponent
significant
s
30
23
exp (E)
0
22
fraction (F)
(b1b2b3…b23)2

## Slide 46: Normalized representation
0 | 0000 0010 | 0110 0000 0000 0000 0000 000
31
30
23
22
0
Example: (5.5)10 = (101.1)2 = (1.011)2 * 22
( b1b2b3…b23 )2
+M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…b23 )2
exponent
significant

## Slide 47: Summary
2’s complement
  The negation trick, and its use for subtraction
What are 32-bit or 64-bit processors?
Byte ordering
  Big vs. small endian
Intro to floating points