## Slide 1: Memory hierarchy: caching
Jinyang Li
Based on Patterson and Hennessy’s slides

## Slide 2: What we’ve learnt so far
Single cycle RISC-V CPU design
5 stage pipelined RISC-V CPU
  Pipelining challenges: hazards
    Must stall (bubble) to ensure correctness
  3 types of hazards:
    Structure (To mitigate, add resources)
    Data (To mitigate, do forwarding/bypassing)
    Control (Predict/speculate)

## Slide 3: Today’s lesson plan
Memory hierarchy
Caching
  Performance
  Design

## Slide 4: Programmers want fast and unlimited memory, but…
Processor
Memory
Memory
Memory
SRAM
DRAM
Flash
Memory
Magnetic
disk
speed
smallest
biggest
size
Flip-flop
0.5-2.5ns
50-70ns
5-50𝜇s
5-20ms
< 0.5ns
$500-$1000/GB
$7-$15/GB
$0.75-$1/GB
$0.05-$0.1/GB
Integrated on chip
fastest
slowest

## Slide 5: DRAM Technology
Data stored as a charge in a capacitor
  Single transistor used to access the charge
  Must periodically be refreshed
    Read contents and write back
Double data rate (DDR) DRAM
  Transfer on rising and falling clock edges
2666 *106 transfers/sec
8 bytes per transfer

## Slide 6: Flash Storage
Nonvolatile semiconductor storage
  Compared to DRAM
    100x – 1000x slower
  Compared to magnetic disk
    100× – 1000× faster than magnetic disk
    Smaller, lower power, more robust
Flash bits wears out after 1000’s of accesses
  Wear leveling: remap data to less used blocks

## Slide 7: Magnetic disk
Nonvolatile, rotating magnetic storage
Data is stored in sectors
  512 bytes in size
Data access time includes:
  Seek time: move the heads to the right track
    Typically, 4-5ms
  Rotational time: wait till head is over the right sector
    = ½ /rotation frequency, e.g. ½/(15000/60)=2ms
  Data transfer time
    E.g. 512B/ 100MB/s = 0.005ms
e.g. Transfer 512Bytes

## Slide 8: How to give programmers the illusion of fast and vast memory? Caching!
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
This lecture: focus on cache memory only
Referred to as
main memory
Referred to as
cache memory (integrated on CPU chip)
Done at the granularity
of a block or line

## Slide 9: Why caching works? Principle of locality
Programs access a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data

## Slide 10: Direct Mapped Cache
Direct mapped: each mem block can only be cached at one location
  (Block address) modulo (#Blocks in cache)
…
00000000
11111111
00000001
11111110
…
…
Memory Addr:
1 | 1 | 1 | 1 | 0 | 1 | 1 | 1
00000111
00001000
11110111
11111000
Byte offset within a block
Block address
#Blocks =TotalMem/BlockSize =28/23
Suppose cache has 8 blocks
(00000)2 % 8 = (000)2
(01000)2 % 8 = (000)2
(11000)2 % 8 = (000)2
8-byte data
000
001
010
011
100
101
110
111

## Slide 11: Direct Mapped Cache
Direct mapped: each mem block can only be cached at one location
  (Block address) modulo (#Blocks in cache)
…
00000000
11111111
00000001
11111110
…
…
Memory Addr:
1 | 1 | 1 | 1 | 0 | 1 | 1 | 1
00000111
00001000
11110111
11111000
Byte offset within a block
Block address
#Blocks =TotalMem/BlockSize =28/23
Suppose cache has 8 blocks or 8 “lines”
Use lower-order x-bits of block address
to index into the cache with 2x blocks.
8-byte data
000
001
010
011
100
101
110
111

## Slide 12: Tags and Valid Bits
How to track which mem block is stored in a cache location?
  Store tag
What if there is no data in a location?
  Store a valid-bit
Memory Addr:
1 | 1 | 1 | 1 | 0 | 1 | 1 | 1
Byte offset
Block address
8-byte data
000
001
010
011
100
101
110
111
10
1
Tag
Data
Valid?
Cache index
Tag
Suppose cache has 8 blocks or 8 “lines”

## Slide 13: Cache Example
8-blocks, 8-bytes/block, direct mapped
Initial state
N |  | 
N |  | 
N |  | 
N |  | 
N |  | 
N |  | 
N |  | 
N |  | 
Tag
Data
Valid?
111
110
101
100
011
010
001
000

## Slide 14: Cache Example
N |  | 
N |  | 
N |  | 
N |  | 
N |  | 
N |  | 
N |  | 
N |  | 
Tag
Data
Valid?
111
110
101
100
011
010
001
000
Memory addr accessed: 10110xxx

## Slide 15: Cache Example
N |  | 
Y | 10 | 8-bytes starting at mem[10110]
N |  | 
N |  | 
N |  | 
N |  | 
N |  | 
N |  | 
Tag
Data
Valid?
111
110
101
100
011
010
001
000
Memory addr accessed: 11010xxx

## Slide 16: Cache Example
N |  | 
Y | 10 | 8-bytes starting at mem[10110]
N |  | 
N |  | 
N |  | 
Y | 11 | 8-bytes starting at mem[11010]
N |  | 
N |  | 
Tag
Data
Valid?
111
110
101
100
011
010
001
000
Memory addr accessed: 10110xxx

## Slide 17: Cache Example
N |  | 
Y | 10 | 8-bytes starting at mem[10110]
N |  | 
N |  | 
N |  | 
Y | 11 | 8-bytes starting at mem[11010]
N |  | 
N |  | 
Tag
Data
Valid?
111
110
101
100
011
010
001
000
Memory addr accessed: 00010xxx

## Slide 18: Cache Example
N |  | 
Y | 10 | 8-bytes starting at mem[10110]
N |  | 
N |  | 
N |  | 
Y | 00 | 8-bytes starting at mem[00010]
N |  | 
N |  | 
Tag
Data
Valid?
111
110
101
100
011
010
001
000

## Slide 19: Another example: Larger Block Size
64-bit memory address
64 cache blocks, 16 bytes/block
Tag
Index
Offset
0
3
4
9
10
63
4 bits
6 bits
22 bits
??
??
??

## Slide 20: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them
    More competition  increased miss rate
  Larger blocks  pollution
Larger miss penalty
  Can override benefit of reduced miss rate

## Slide 21: Hardware of direct mapped cache

## Slide 22: Cache Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access
Very expensive: usually 20~100 cycles

## Slide 23: Write-Through vs write-back
Write-through: On write hit, update memory upon write
Write-back: On write hit, update cache only
  Keep track of whether a block in cache is dirty
  When a dirty block is replaced, write it back to memory

## Slide 24: Measuring Cache Performance

## Slide 25: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
Miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI = 2 + 2 + 1.44 = 5.44
  Ideal CPU is 5.44/2 =2.72 times faster

## Slide 26: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 27: Reducing cache miss: Associative Cache
Fully associative
  Allow a given block to go in any cache entry
  Require all entries to be searched at once
    Need a comparator per cache entry (expensive)
n-way set associative
  Divide cache into sets each of which contains n entries
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Fully-associative within the set: search n entries of a set at once
    n comparators (less expensive)

## Slide 28: Associative Cache Example
Cache locations of a memory block with block address 12

## Slide 29: Associativity Example
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 
Direct mapped
  Block access sequence: 0, 8, 0, 6, 8

## Slide 30: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000 benchmark
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 31: 4-way set Associative Cache Organization

## Slide 32: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Hardware implementation: simple for 2-way, manageable for 4-way, too hard beyond that

## Slide 33: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
High-end systems include L-3 cache

## Slide 34: Software Optimization via Blocking
Goal: maximize accesses to data before it is replaced
Example: Naïve matrix multiplication (DGEMM)
for (int i = 0; i < n; i++) {
for (int j = 0; j < n; j++) {
double cij = 0;
for( int k = 0; k < n; k++ )
cij += A[i+k*n] * B[k+j*n];
C[i+j*n] = cij;
}
}

## Slide 35: DGEMM access pattern
older accesses
new accesses
C
A
B
Cache hit?
Cache hit?

## Slide 36: Blocked DGEMM
#define BLOCKSIZE 32
void do_block (int n, int si, int sj, int sk, double *A, double*B, double *C)
{
for (int i = si; i < si+BLOCKSIZE; ++i)
for (int j = sj; j < sj+BLOCKSIZE; ++j)
{
double s = 0;
for( int k = sk; k < sk+BLOCKSIZE; k++ )
s += A[i+k*n] * B[k+j*n];
C[i+j*n] += s; //accumulate s to C[i][j] */
}
}
void dgemm (int n, double* A, double* B, double* C)
{
for ( int sj = 0; sj < n; sj += BLOCKSIZE )
for ( int si = 0; si < n; si += BLOCKSIZE )
for ( int sk = 0; sk < n; sk += BLOCKSIZE )
do_block(n, si, sj, sk, A, B, C);
}

## Slide 37: Blocked DGEMM Access Pattern
Unoptimized
Blocked
C
A
B

## Slide 38: Summary
Memory hierarchy
Caching works due to principles of locality
Direct mapped vs. set-associate cache
Software optimization via blocking