## Slide 1: CSO-Recitation 13 CSCI-UA 0201-007
R13: Assessment 11

## Slide 2: Assessment 11

## Slide 3: Q1 Boolean laws
Which of the following Boolean laws hold? Below, A, B, C could refer to either a Boolean variable or a Boolean expression
R1: A+0=A
R2: A+0=0
R3: A+1=1
R4: A+1=A
R5: A⋅(B+C)=A⋅B + A⋅C
R6: A + =1
R7: A ⋅ = 0
Basic law:
A ⋅0 =0, A ⋅1=A
A+0=A, A+1=1
Distribution law
Inverse law

## Slide 4: Q2 Simplify boolean expression
Simplify boolean expression (A+B) ⋅(+ ).
You may write `*` for ⋅, and write `barA` for (or `barB` or )
(A+B)*(barA+barB)
=(A+B)*barA + (A+B)*barB
=barA*A + barA*B + barB*A + barB*B
=0+barA*B+barB*A+0
=barA*B+barB*A
Distribution law
Distribution law
Inverse law
Basic law

## Slide 5: Q3 Simplify boolean expression
When simplifying the Boolean expression in Q2, which of the Boolean laws in shown Q1 are needed?
R1
R2
R3
R4
R5
R6
R7

## Slide 6: Q4 Boolean circuit
If you are to use a single logic gate to implement the simplified expression in Q2. Which gate should you use?
AND
OR
NOR
NAND
XOR
None of the above
XOR(A,B) = A*barB + B*barA
NAND(A,B) = bar(A*B) = barA+barB

## Slide 7: Q5 Combinatorial circuit
In this question, you are asked to implement a combinatorial circuit that takes a 4-bit input and outputs a single bit indicating whether the unsigned 4-bit integer represented by b3​b2​b1​b0​ is a prime number or not.
Q5.1 Truth table
How many total rows does the truth table corresponding to the 4-bit prime number detector circuit have?
16
#row of truth table:
have 4 input signals, each represents 1 bit
how many bit patterns?
2^4 = 16

## Slide 8: Q5.2 Truth Table
How many of the rows in the truth table of Q5.1 corresponds to the output bit value o=1?
6
Prime: 2, 3, 5, 7, 11, 13

## Slide 9: Q5.3 Product of terms
The prime number detector circuit can be built as a sum of products where each product term corresponds to a row in Q5.2. Please write the product term that corresponds to the input b3b2b1b0 = (1011)2
B3 Barb2 b1 b0
(1011)2 = 11, is a prime
  output = 1
b3, b1, b0 = 1, remain the same
b2 = 0, => Barb2

## Slide 10: Q5.4 ROM
If you are to using a ROM to implement the prime number detector circuit. What is the minimal size of the ROM required?
4 variables
h = 2^4 = 16
  i.e. #input bit patterns
w = 1 (one bit to indicate whether this is a prime number or not)

## Slide 11: Q5.4 ROM
Following Q5.4, what is the value of the ROM entry at index or address (1010)2​?
0
(1010)2 = 10, not a prime
  output = 0

## Slide 12: Q6 Ripple carry
If a 1-bit adder's gate delay is 2, then what is the gate delay of a 32-bit ripple carry?
64
ready at t=0
ready at t=2
ready at t=4
ready at t=6
ready at t=2*32
a32
b32
ALU32
Result 32

## Slide 13: Q6 Ripple carry
If a 1-bit adder's gate delay is 2, then what is the gate delay of a 32-bit ripple carry?
64
ripple carry:
compute carry-bit sequentially
gate delay = (1-bit adder’s gate_delay) * #adders
= 2* 32 =64

## Slide 14: Lab 4 Optimization

## Slide 15: Simple implicit list implementation
First-fit algorithm
Simply optimized realloc function (3 cases):
  Shrink: directly decrease the size
  Expand:
    Next chunk is a free chunk, and the size is sufficient: utilize the next chunk
    Otherwise, free the current chunk and allocate a new one

## Slide 16: Simple implicit list implementation
Utilization is low.
Even though the utilization is high, performance is low

## Slide 17: Simple implicit list implementation

## Slide 18: Simple implicit list implementation
First try to optimize these two traces (realloc trace)

## Slide 19: realloc trace

## Slide 20: realloc trace
512, a
128, a
Heap start
512, f
640, a
128, a
384, f
128, f

## Slide 21: realloc trace
512, a
128, a
Heap start
512, f
640, a
128, a
384, f
128, f
640, f
768, a

## Slide 22: realloc trace
640, a
…
768, a
768, f
896, a

## Slide 23: realloc trace - optimization
512, a
128, a
Heap start
512, f
640, a
128, a
384, f
128, f
128, a
Ask for os for the remaining size (768 – 640)

## Slide 24: realloc trace - optimization
512, a
128, a
Heap start
512, f
640, a
128, a
384, f
128, f
128, a
Ask for os for the remaining size (768 – 640)
768, a

## Slide 25: realloc trace - optimization
512, a
128, a
Heap start
512, f
640, a
128, a
384, f
128, f
128, a
768, a
All malloc(128) will be put near the start of the heap

## Slide 26: realloc trace - optimization
512, a
128, a
Heap start
512, f
640, a
128, a
384, f
128, f
128, a
768, a
All realloc will just increase the size of the last chunk
Increase when realloc

## Slide 27: realloc trace - optimization
Before:
After:

## Slide 28: binary trac
a 0 64
a 1 448
a 2 64
a 3 448
a 4 64
a 5 448
…
f 1
f 3
f 5
…
a 4000 512
a 4001 512
a 4002 512
a 4003 512
…
64, a
448, a
64, a
448, a
…

## Slide 29: binary trace
a 0 64
a 1 448
a 2 64
a 3 448
a 4 64
a 5 448
…
f 1
f 3
f 5
…
a 4000 512
a 4001 512
a 4002 512
a 4003 512
…
64, a
448, f
64, a
448, f
…

## Slide 30: binary trace
a 0 64
a 1 448
a 2 64
a 3 448
a 4 64
a 5 448
…
f 1
f 3
f 5
…
a 4000 512
a 4001 512
a 4002 512
a 4003 512
…
64, a
448, f
64, a
448, f
…
Too small for 512
512, a
Too small for 512
512, a
…

## Slide 31: binary trace - optimization
We can separate the memory allocation for small and large chunks
  Try to put the small chunks together
JRockit JVM follows this principle (https://docs.oracle.com/cd/E13150_01/jrockit_jvm/jrockit/geninfo/diagnos/garbage_collect.html)
a 0 64
a 1 448
a 2 64
a 3 448
a 4 64
a 5 448
…
f 1
f 3
f 5
…
a 4000 512
a 4001 512
a 4002 512
a 4003 512
…
64, a
448, a
64, a
448, a
…
…
Small chunks
Large chunks

## Slide 32: binary trace - optimization
Before:
After:

## Slide 33: Other optimization
To optimize utilization:
  Add footer to fully utilize the free chunks (coalesce adjacent free chunks is possible)
To optimize the performance:
  Use segregated and explicit list to find a suitable chunk faster
  Use next fit instead of first fit

## Slide 35: Adders

## Slide 36: Faster adder: carry lookahead
Ripple carry
  Delay: 64*1BitAdderGateDelay,☹️, Gate count: 64*c 🙂
Brute-force (truth table->PLA)
  Delay: 2 🙂, Gate count: O(2^(64+64)) ☹️
In between: Carry lookahead
  Long delay in ripple carry caused by carry bits dependency!
  Idea: compute all carry bits at a time

## Slide 37: Faster adder: carry lookahead (4-bit)
to get rid of ci+1’s dependency on ci, plug in the expr for ci

## Slide 38: Faster adder: carry lookahead (4-bit)
CarryIn CarryOut
a0
b0
CarryIn CarryOut
a1
b1
CarryIn CarryOut
a2
b2
CarryIn CarryOut
a3
b3
carryIn (c0)
carryOut (c4)
c1
c2
c3
CarryIn CarryOut
a0
b0
CarryIn CarryOut
a1
b1
CarryIn CarryOut
a2
b2
CarryIn CarryOut
a3
b3
Carry Lookahead
carryOut (c4)
carryIn (c0)
p0 g0
c3
c1
c2
p1 g1
p2 g2
p3 g3
Ripple carry
Carry Lookahead
Delay of c0=>c4 is 3
Delay of c0=>c4 is 2*4=8
How many gates asymptotically do we need?
ci needs i multi-input AND gates
at least 1+2+…+N=O(N^2) gates
Not so good with large N

## Slide 39: Time && space comparison
 | Time (Delay) | Space (# gates)
Ripple carry | O(N) | O(N)
Carry lookahead | O(1) | O(N^2)
chaining N/M M-bit carry lookahead | O(N/M) | O(M^2*N/M)=O(NM)
Hierarchical M-bit carry lookahead | O(log_M N) | O(NM)

## Slide 40: 16-bit adder
Strawman: : chaining 4-bit carry lookahead
CarryIn CarryOut
a0
b0
CarryIn CarryOut
a1
b1
CarryIn CarryOut
a2
b2
CarryIn CarryOut
a3
b3
Carry Lookahead
carryOut (c4)
carryIn (c0)
p0 g0
c3
c1
c2
p1 g1
p2 g2
p3 g3
4-bit adder with carry lookahead
CarryIn CarryOut
a0..3
b0..3
CarryIn CarryOut
a4..7
b4..7
CarryIn CarryOut
a8..11
b8..11
CarryIn CarryOut
a12..15
b12..15
carryIn (c0)
carryOut (c16)
c4
c8
c12
Problem: high delay (3*4=12)

## Slide 41
CarryIn CarryOut
a0
b0
CarryIn CarryOut
a1
b1
CarryIn CarryOut
a2
b2
CarryIn CarryOut
a3
b3
Carry Lookahead
carryOut (c4)
carryIn (c0)
p0 g0
c3
c1
c2
p1 g1
p2 g2
p3 g3

## Slide 42: 16-bit adder
Similar problem: carry bits dependency
Borrow the idea of carry-lookahead to compute c4 c8 c12 c16 at a time?
CarryIn CarryOut
a0..3
b0..3
CarryIn CarryOut
a4..7
b4..7
CarryIn CarryOut
a8..11
b8..11
CarryIn CarryOut
a12..15
b12..15
carryIn (c0)
carryOut (c16)
c4
c8
c12

## Slide 43: 16-bit adder
Similar problem: carry bits dependency
Borrow the idea of carry-lookahead to compute c4 c8 c12 c16 at a time
  Need to compute “super” propagate (P0…P3) and “super” generate (G0…G3) for each 4-bit adder
CarryIn CarryOut
a0..3
b0..3
CarryIn CarryOut
a4..7
b4..7
CarryIn CarryOut
a8..11
b8..11
CarryIn CarryOut
a12..15
b12..15
carryIn (c0)
c4
c8
c12
Carry Lookahead
carryOut (c16)
p0 g0
p1 g1
p2 g2
p3 g3
P0 G0
P1 G1
P2 G2
P3 G3

## Slide 44: 16-bit adder
Super propagate:
  P0=p0·p1·p2·p3
Super generate:
  G0=g3+ p3·g2 + p3· p2·g1+ p3· p2·p1 ·g0
The carry bits are the same:
CarryIn CarryOut
a0..3
b0..3
CarryIn CarryOut
a4..7
b4..7
CarryIn CarryOut
a8..11
b8..11
CarryIn CarryOut
a12..15
b12..15
carryIn (C0)
C1
C2
C3
Carry Lookahead
carryOut (C4)
p0 g0
p1 g1
p2 g2
p3 g3
P0 G0
P1 G1
P2 G2
P3 G3
CarryIn CarryOut
a0
b0
CarryIn CarryOut
a1
b1
CarryIn CarryOut
a2
b2
CarryIn CarryOut
a3
b3
Carry Lookahead
carryOut (c4)
carryIn (c0)
p0 g0
c3
c1
c2
p1 g1
p2 g2
p3 g3
P0
G0

## Slide 45: Sequential logic
Building Blocks

## Slide 46: Sequential Logic
There is memory
  Outputs depend on prior state as well as the current inputs
  State can be stored and used later
We rely on clock signals
  Clock signals tell us when things should happen
  We should only write to state when the clock is set a certain way

## Slide 47: SR Latch, D Latch and D Flip Flop
Demo

## Slide 48: SR Latch
Constructed from two NOR gates
  You can either Set the latch (make it remember 1), or Reset it (make it remember 0)
Two inputs: S and R
Two outputs: Q and NOT Q
  Q is what it remembers, NOT Q is the opposite
Both S and R cannot be 1 at the same time, or sadness occurs

## Slide 49: D Latch
Constructed from some additional logic and an SR Latch
Two inputs: C and D
You can have the latch remember D as long as C is true
Two outputs: Q and NOT Q
  Q is what the latch remembers, NOT Q is the inverse
Ensures that S and R inputs to the SR Latch aren’t both true

## Slide 50: D Flip Flop
Constructed from some additional logic and two D latches
Same inputs and outputs as D latches
But, the output is only stored on a chosen clock edge

## Slide 51: Lab5
using Logisim Evolution

## Slide 52: Setup
Clone the Lab 5 repository – new link (campuswire)
cd lab5new-<YourGithubUsername>
wget https://nyu-cso.github.io/labs/logisim-evolution-2.15.jar
download the Java runtime environment:
  sudo apt-get install default-jre
Launch Logisim by typing (in your lab5new repo):
  java -jar logisim-evolution-2.15.jar
Save frequently when you work~

## Slide 53: Finite State Machines

## Slide 54: Finite State Machines
There are a number of states, inputs, and outputs
To the beat of the clock, we read in inputs and go to new states, and set the outputs
Both the output and the next state are defined by the current state and the inputs
Can be expressed as a flowchart or a truth table

## Slide 55: An FSM example
There are 4 states
Nodes represent states
  Initial state is 00
“x/y” on the arrow edge is “transition condition”
  when input=x, follow this edge to transit into the pointed state
  set output=y in the meantime

## Slide 56: An FSM example
We are here
read input ”0”

## Slide 57: An FSM example
move to here
set output=1
read input ”1”

## Slide 58: An FSM example
move to here
set output=1

## Slide 59: An FSM example
The corresponding truth table

## Slide 60: Another FSM Example
The NYC Subway Turnstile
There is a lock controlled by the FSM
If the user didn’t pay yet then the lock is active and the user can’t push through
If the user pays, the lock unlocks until they push through
Draw an FSM for this
Write out a truth table
Create the circuit

## Slide 61: Another FSM Example
current state | input | next state
(lock / unlock) | (pay / push) | 
Lock
Unlock
pay
push
push
pay

## Slide 62: Another FSM Example
current state | input | next state
(lock / unlock) | (pay / push) | 
Lock
Unlock
pay
push
push
pay