## Slide 1: Floating point
Jinyang Li

## Slide 2: Floating Point (FP) lesson plan
Normalized binary exponential notation
Strawman 32-bit FP
IEEE FP format
Rounding

## Slide 3: Previously…
-
+
1
2
-3
-2
-1
3
2n-1-1
2n-1
0
2n-1
Unsigned n-bit integers
Signed n-bit integers
What about real numbers?

## Slide 4: Represent real numbers: the decimal way
Real Number | Decimal Representation
11 / 2 | (5.5)10
1 / 3 | (0.3333333...)10
√2 | (1.4128…)10
(1.4128...)10 = 1 * 100 + 4 * 10-1 + 1 * 10-2 + 2 * 10-3 + ...

## Slide 5: Binary Representation
(5.5)10
= (101.1)2
= 4 + 1 + 1/2
= 22 + 20 + 2-1

## Slide 6: Binary Representation
(0.333333...)10 = 1 / 4 + 1 / 16 + 1 / 64 + ...
= (0.01010101...)2

## Slide 7: Binary Representation
2p
2p-1
2
1
1/2
1/4
1/2q
.

## Slide 8: Binary representation
What’s the decimal value of (10.01)2

## Slide 9: Binary representation
What’s the decimal value of (10.01)2
Answer: 2.25

## Slide 10: Making the representation fixed width Strawman: fixed point
s | b14 | b13 | b12 | … | b1 | b0 | b-1 | b-2 | b-3 | … | b-14 | b-15 | b-16
sign
15 bits
Fixed position e.g. middle
16 bits

## Slide 11: Fixed point representation
s | b14 | b13 | b12 | … | b1 | b0 | b-1 | b-2 | b-3 | … | b-14 | b-15 | b-16
sign
15 bits
16 bits
Example: ( 10.011 )2
0 | 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 | 0 1 1 0 0 0 0 0 0 0 0 0 0 0 0

## Slide 12: Problems of Fixed Point
s | b14 | b13 | b12 | … | b1 | b0 | b-1 | b-2 | b-3 | … | b-14 | b-15 | b-16
15 bits
16 bits
Range?
Precision?
-
+
0

## Slide 13: Problems of Fixed Point
  Limited range and precision: e.g., 32 bits
    Range: [-215+2-16,215-2-16 ]
    Highest precision: 2-16
Rarely used (No built-in hardware support)
s | b14 | b13 | b12 | … | b1 | b0 | b-1 | b-2 | b-3 | … | b-14 | b-15 | b-16
15 bits
16 bits

## Slide 14: Floating point: key idea
Limitation of fixed point:
  Even spacing results in hard tradeoff between high precision and high magnitude
How about un-even spacing between numbers?
-
+
0

## Slide 15: Floating Point: decimal
Based on exponential notation (aka normalized scientific notation)
r10 = +M * 10E, where 1 <= M < 10
M: significant (mantissa), E: exponent

## Slide 16: Floating Point: decimal
Example:
365.25 = 3.6525 * 102
0.0123 = 1.23 * 10-2
Decimal point floats to the position immediately
after the first nonzero digit.

## Slide 17: Floating Point: binary
Binary exponential representation
(5.5)10 = (101.1)2 = (1.011)2 * 22
+M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…bn )2
M: significant, E: exponent

## Slide 18: Floating Point
Binary exponential representation
(5.5)10 = (101.1)2 = (1.011)2 * 22
Also called normalized
representation
+M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…bn )2
M: significant, E: exponent

## Slide 19
(Binary) normalized representation of (10.25)10?

## Slide 20
(Binary) normalized representation of (10.25)10 ?
Answer: (10.25)10 = (1010.01)2 = (1.01001)2 * 23

## Slide 21: Strawman FP: normalized representation in 32-bit
31
+M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…b23 )2
exponent
significant
s
30
23
exp (E)
0
22
fraction (F)
(b1b2b3…b23)2

## Slide 22: Strawman 32-bit FP: Example
0 | 0000 0010 | 0110 0000 0000 0000 0000 000
31
30
23
22
0
Example: (5.5)10 = (101.1)2 = (1.011)2 * 22
( b1b2b3…b23 )2
+M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…b23 )2
exponent
significant

## Slide 23: More Strawman 32-bit FP Examples
0 | 0000 0110 | 0000 0100 0000 0000 0000 000
31
30
23
22
0
Example: (65)10 = (1000001)2 = (1.000001)2 * 26
Another example: (10.25)10 = (1010.01)2 = (1.01001)2 * 23
0 | 0000 0011 | 0100 1000 0000 0000 0000 000
31
30
23
22
0

## Slide 24: Strawman FP on a number line
s | exp (E) | frac (F)
31
30
23
22
0
0 0….0 0…01
0 0….0 0…10
0 0….0 0…00
1
1+2*2-23
0 0….0 1…11
1+(223-1)*2-23
0 0….1 0…00
2
0 0….1 0…01
1+2-23
2+2-22
…
0 0….1 0…01
2+2*2-22
0 1….1 1…11
0 1….1 1…10
2255+(223-1)*2232
2255+(223-2)*2232
…
2-23
2-22
2232

## Slide 25: Strawman 32-bit FP: pros and cons
1
2
4
8
1 0….01 0…00
0 0….01 0…00
0 0…10 0…00
0 0…11 0…00
223 evenly spaced numbers in each interval
The good 👍
  Large range [1, 2255+(223-1)*2232], [-2255-(223-1)*2232 ,-1]
  Allows easy comparison: compare FPs by bit patterns
The bad 👎
  No 0!
  No [-1, 1]
  Max precision (2-23 ) not high enough
  No representation of special cases: ∞
-1
-2
0 0….00 0…00
1 0….00 0…00
Max: 0 1…11 1…11
2255+(223-1)*2232

## Slide 26: IEEE Floating Point Standard
Lots of FP implementations in 60s/70s
  Code was not portable across processors
IEEE formed a committee (IEEE.754) to standardize FP format and specification.
  IEEE FP standard published in 1985
  Led by William Kahan
Prof. William Kahan
University of California at Berkeley
Turing Award (1989)

## Slide 27: IEEE Floating Point Standard
This class only covers basic FP materials
A deep understanding of FP is crucial for numerical/scientific computing
  More FP is covered in undergrad/grad classes on numerical methods

## Slide 28: Goals of IEEE Standard
Consistent representation of floating point numbers
  Address the limitation of our FP strawman
Correctly rounded floating point operations, using several rounding modes.
Consistent treatment of exceptional situations such as division by zero

## Slide 29: IEEE FP: Carve out subsets of bit-patterns from normalized representation
+M * 2E M = ( 1.b0b1b2b3…bn )2
s | exp | fraction (F)
31
30
23
22
0
( b0b1b2b3…bn )2
For normalization representation,
exp can not be (1111 1111)2 or (0000 0000)0
expmax = ?
expmin = ?
254, (1111 1110)2
1, (0000 0001)2

## Slide 30: IEEE FP: Represent negative exponents using bias
+M * 2E, M = ( 1.b0b1b2b3…bn )2
s | exp = E + 127 | fraction (F)
31
30
23
22
0
( b0b1b2b3…bn )2
To represent FPs in (-1,1), we must allow negative exponent.
How to represent negative E?
  2’s complement
  use bias
Why? Using bias instead of 2’s complement allows simple comparison of FPs using their bit-patterns

## Slide 31: IEEE FP normalized representation
+M * 2E, M = ( 1.b0b1b2b3…bn )2
s | exp = E + 127 | fraction (F)
31
30
23
22
0
( b0b1b2b3…bn )2
2-126
2-125
2-124
1 0….10 0…00
0 0….10 0…00
0 0…11 0…00
223 evenly spaced numbers in each interval
-2-126
-2-125
0 0….01 0…00
1 0….01 0…00
Max: 0 1…10 1…11
2127+(223-1)*2127-23
The gap [-2-126 , 2-126]
is 2-125

## Slide 32
Represent values close and equal to 0

## Slide 33: IEEE FP denormalized representation: represent values close and equal to 0
+M * 2E
s | exp = E + 127 | fraction (F)
31
30
23
22
0
Normalized Encoding:
1 <= M < 2, M = ( 1.F )2
s | exp =0000 0000 | fraction (F)
31
30
23
22
0
Denormalized Encoding:
0 <= M < 1, M = ( 0.F )2
E = 1 – Bias = -126

## Slide 34: Zeros
0 | 0000 0000 | 0000 0000 0000 0000 0000 000
+0.0
1 | 0000 0000 | 0000 0000 0000 0000 0000 000
-0.0

## Slide 35: Denormalized FP example
0 | 0000 0000 | 1000 0000 0000 0000 0000 000
What’s the IEEE FP format of (1.0)2*2-127?
Smaller than the smallest E (-126)
of normalized encoding
(1.0)2*2-127= (0.1) 2*2-126

## Slide 36: IEEE FP normalized + denormalized
2-126
2-125
2-124
1 0….01 0…00
0 0….10 0…00
0 0…11 0…00
223 evenly spaced numbers in each interval
-2-126
-2-125
0 0….01 0…00
1 0….00 0…00
Max: 0 1…10 1…11
2127+(223-1)*2127-23
s | exp = E + 127 | fraction (F)
1 <= M < 2, M = ( 1.F )2
s | exp =0000 0000 | fraction (F)
0 <= M < 1, M = ( 0.F )2
±0
0 0….00 0…00
1 0….00 0…00
223 evenly spaced denormalized numbers in each of the two intervals

## Slide 37: IEEE FP: special values
s | 1111 1111 | fraction (F)
31
30
23
22
0
Special Value’s Encoding:
values | sign | frac
+ | 0 | all zeros
- | 1 | all zeros
NaN | any | non-zero

## Slide 38: IEEE FP: single vs. double precision
s | E + 127 | frac
31
30
23
22
0
single precision (32 bits)
s | E + 1023 | frac
63
62
52
51
0
double precision (64 bits)
float f = 0.1
double d = 0.1

## Slide 39: single/ double precision
 | Emin | Emax | Nmin | Nmax
Float | -126 | 127 | 2-149 | ≈ 2128
Double | -1022 | 1023 | 2-1078 | ≈ 21024

## Slide 40: FP summary
Normalized binary representation of real numbers
IEEE FP
2-126
2-125
2-124
1 0….01 0…00
0 0….10 0…00
0 0…11 0…00
223 evenly spaced numbers in each interval
-2-126
-2-125
0 0….01 0…00
1 0….00 0…00
Max: 0 1…10 1…11
2127+(223-1)*2127-23
s | exp | fraction (F)
If exp!=0 && exp!=255, (1.F )*2exp-127
0 <= M < 1, M = ( 0.F )2
±0
0 0….00 0…00
1 0….00 0…00
223 evenly spaced denormalized numbers in each of the two intervals
If exp==0, (0.F )*2-126

## Slide 41: A toy 8-bit FP in the spirit of IEEE FP
s | exp = E + 3 | frac (F)
7
6
4
3
0
exponent: 3 bits
fraction: 4 bits
bias: 3
+M * 2E
1 <= M < 2, M = ( 1.F )2
0 <= M < 1, M = ( 0.F )2
s | 0 0 0 | frac (F)
7
6
4
3
0
Normalized encoding
exp ≠ 000, 111
Denormalized encoding
exp = 000
Smallest positive number?
Range?
How many distinct numbers?
Special values encoding
exp = 111
s | 1 1 1 | 
7
6

## Slide 42: A toy 8-bit FP in the spirit of IEEE FP
s | exp = E + 3 | frac (F)
7
6
4
3
0
exponent: 3 bits
fraction: 4 bits
bias: 3
+M * 2E
1 <= M < 2, M = ( 1.F )2
0 <= M < 1, M = ( 0.F )2
s | 0 0 0 | frac (F)
7
6
4
3
0
Normalized encoding
exp ≠ 000, 111
Denormalized encoding
exp = 000 aka E=1-3=-2
0
(00000001)FP8= 2-6
(01101111)FP8= 15.5
28 - 25 -1 distinct numbers: there are 28 total bit-patterns, 25 special values, 0 has 2 bit-patterns.

## Slide 43: Floating Point (FP) lesson plan
Normalized binary exponential notation
Strawman 32-bit FP
IEEE FP format
Rounding

## Slide 44: FP: Rounding
  What if the result of computation is at ?
Values that are represented precisely
Rounding: Use the “closest” representable value x’ for x.
  4 modes:
  Round-down
  Round-up
  Round-toward-zero
  Round-to-nearest (Round-to-even in text book)

## Slide 45: Round down vs. round up
-0.875
-0.75
0.5
0.625
Round(x) = x- (x-<= x)
Round down rounds to the left
0
Round up rounds to the right
Round(x) = x+ (x+>= x)

## Slide 46: Round towards zero
-0.875
-0.75
0.5
0.625
Round(x) = x- if x < 0
Rounds to the left if x >0
Rounds to the right if x < 0
Round(x) = x+ if x < 0
0

## Slide 47: Round to nearest; ties to even
-0.875
-0.75
0.5
0.625
Round to the right if x+ is nearer to x than x-
0
Round to the left if x- is nearer to x than x+
In case of a tie, the one with its least significant bit equal to zero is chosen.

## Slide 48: How does CPU know if it is floating point or integers ?
CPU has separate registers for floating point and integers.
CPU uses different instructions for floating points and integer operations.

## Slide 49: FP summary
FP representation is based on normalized binary exponential notation
IEEE FP format
  Normalized, denormalized, special values
Precision gets higher as numbers approach 0
Rounding

## Slide 50: Floating point operations
Addition, subtraction, multiplication, division etc.
FP Caveats:
  Invalid operation: 0/0, sqrt(-1), +
  Divide by zero: x/0
  Overflows: result too big to fit
  Underflows: 0 < result < smallest denormalized value
  Inexact: round it!

## Slide 51: Why divide by zero = ?
Allow a calculation to continue and produce a valid result
Example:
If R1 or R2 is 0, overall resistance should be 0

## Slide 52: Floating point addition
Commutative? x+y == y+x?
Associative? (x+y)+z = x + (y+z)?
  Rounding:
  (3.14+1e10)-1e10 = 0
  3.14+(1e10-1e10) = 3.14
  Overflow
Every number has an additive inverse?
  Yes except for  and NaN

## Slide 53: Floating point multiplication
Commutative? x* y == y*x?
Associative? (x*y)*z = x * (y*z)?
  Overflow:
  (1e20*1e20)*1e-20= inf, 1e20*(1e20*1e-20)= 1e20
  Rounding
(x+y)*z = x*z + y*z?
  1e20*(1e20-1e20)= 0.0, 1e20*1e20 – 1e20*1e20 = NaN

## Slide 54: Floating point in real world
Storing time in computer games as a FP?
Precision diminishes as time gets bigger
FP value (decimal) | Time value | FP precision | Time precision
1 | 1 sec | 1.19E-07 | 119 nanoseconds
100 | ~1.5 min | 7.63E-06 | 7.63 microseconds
10 000 | ~3 hours | 0.000977 | .976 milliseconds
1000 000 | ~11 days | 0.0625 | 62.5 milliseconds

## Slide 55: Floating point in the real world
Using floating point to measure distances
FP value | Length | FP precision | Precision size
1 | 1 meter | 1.19E-07 | Virus
100 | 100 meter | 7.63E-06 | red blood cell
10 000 | 10 km | 0.000977 | toenail thickness
1000 000 | .16x earth radius | 0.0625 | credit card width
Table source: Random ASCII

## Slide 56: Floating point trouble
Comparing floats for equality is a bad idea!
float f = 0.1;
while (f != 1.0) {
f += 0.1;
}
Notes: You can not represent 0.1 exactly in floating point

## Slide 57: Floating point trouble
Never count using floating points
count = 0;
for (float f = 0.0; f < 1.0; f += 0.1) {
count++;
}
Notes: You can not represent 0.1 exactly in floating point

## Slide 58: Floating point summary
FP format is based on normalized exponential notation
Floating points are tricky
  Precision diminishes as magnitude grows
  overflow, rounding error
Many real world disasters due to FP trickiness
  Patriot Missile failed to intercept due to rounding error (1991)
  Ariane 5 explosion due to overflow in converting from double to int (1996)