## Slide 1: Sequential Logic
Jinyang Li

## Slide 2: What we’ve learnt so far
Combinatorial logic
  Truth table  sum of products circuits
  E.g. Multiplexors (Mux), Decoders
ALU
  Ripple carry
  Carry lookahead

## Slide 3: Two types of logic circuits
Combinatorial circuit
  Truth table  sum of products
  ROM
Sequential circuit
  output is dependent on both input and state (memory elements)
Today’s lesson

## Slide 4: ROM-based implementation of CL
ROM (read-only memory)
00101
11010
11110
00010
00
01
10
11
ROM of 2 address lines and 5 bits per entry
Height 2n
Width

## Slide 5: ROM-based implementation of CL
Example CL : Count # of 1’s in 3-bit inputs
00
01
01
10
01
10
10
11
000:
001:
010:
011:
100:
101:
110:
111:
ROM of height 8 width 2

## Slide 6: ROM vs. PLA (sum of products)
ROM contains more entries than PLA (2n)
A
B
C
00
01
01
10
01
10
10
11
000:
001:
010:
011:
100:
101:
110:
111:
7 products (AND)
8 entries
Easy!
More efficient!

## Slide 7: Two types of logic circuits
Combinatorial circuit
  Truth table  sum of products
  ROM
Sequential circuit
  output is dependent on both input and state (memory elements)

## Slide 8: Sequential logic require clocks
State
element
When should the state element be updated?
Clock signal
Clock
period
Clock frequence = 1/clock_period
Clock
period

## Slide 9: Clocks
Edge-triggered clocking: state content only changes on active clock edge

## Slide 10: Sequential logic require clocks
State
element
State changed to 1
Clock signal
Clock
period
Clock frequence = 1/clock_period
Clock
period
State changed to 0
State changed to 1

## Slide 11: Sequential logic require clocks
Combinatorial logic
State
element 1
State
element 2
Clock cycle
Valid content is read from state element 1
Valid content is written into state element 2
Delay of CL must be less than one clock cycle

## Slide 12: Sequential logic require clocks
Combinatorial logic
State
element
Clock cycle
Valid content is read from state element
Valid content is written into state element

## Slide 13: Memory (state) elements: unlocked S-R Latch
NOR
Stored content
Complement of stored content
S (set) | R (reset) | 
0 | 0 | keeps existing value
1 | 0 | Q=1
0 | 1 | Q=0
1 | 1 | Invalid

## Slide 14: Memory element: clocked D latch
D latch: state is changed as long as clock is asserted
Clock signal
R
S
Clock
State
Input
Latch is open; input is written to state
Latch is closed; state remains unchanged

## Slide 15: Memory element: Flip-flop
Flip-flop: state is changed only on (rising or falling) clock edge
D-flip-flop with a
falling-edge trigger
Q1
1st latch is open Q1=1
2nd latch is open Q=Q1
1st latch is closed

## Slide 16: Memory element: Register file
Register file: a set of registers that can be read and written

## Slide 17: Register file: Read

## Slide 18: Register file: Write
Clock signal is assumed and not drawn

## Slide 19: Register file
What if the same register is read and written in the same clock cycle?
  Return value written in an earlier cycle
  Write of new value occurs on the clock edge (at the end of the current cycle)
Some register file can read value currently being written
  Requires additional logic in the register file

## Slide 20: Finite State Machine
Combinatorial logic  truth table
Sequential logic  F(inite) S(tate) M(achine)
  Input and current state determine next state and outputs

## Slide 21: Finite State Machine
New state is computed every clock cycle
Combinatorial
logic

## Slide 22: FSM example: traffic light control
State:
NSgreen: traffic light is green in N-S (red in E-W)
EWgreen: traffic light is green in E-W (red in N-S)
Inputs:
NScar: car detected in N-S
EWcar: car detected in E-W
Outputs:
NSlite: 1 if state=NSgreen
EWlite: 1 if state=EWgreen

## Slide 23: FSM example: traffic light control
NSgreen
EWgreen
NScar
EWcar
NScar
EWcar
Clock cycles once every 30 seconds

## Slide 24: FSM example: traffic light
FSM is determined by NextState function and Output function
NSg
EWg
NScar
EWcar
NScar
EWcar
How many bits needed to represent state?

## Slide 25: FSM example: traffic light
FSM is determined by NextState function and Output function
0 (Nsgreen)
0 (Nsgreen)
0 (Nsgreen)
0 (Nsgreen)
1 (Ewgreen)
1 (Ewgreen)
1 (Ewgreen)
1 (Ewgreen)
0 (Nsgreen)
1 (Ewgreen)
0 (Nsgreen)
1 (Ewgreen)
1 (Ewgreen)
1 (Ewgreen)
0 (Nsgreen)
0 (Nsgreen)
=
Current State

## Slide 26: FSM traffic light: next state function
State register
EWcar
NScar

## Slide 27: FSM traffic light: output function
0
1
NSLite
EWLite =

## Slide 28: FSM traffic light: output function
State register
NSLite
EWLite