## Slide 1: Virtual memory
Jinyang Li
Some slides are from Patterson and Hennessy

## Slide 2: What we’ve learnt last time
CPU design
  Single cycle
  5 stage pipeline
Memory hierarchy
Caching
  Why it works: principles of locality
  Direct map vs. fully associative vs. n-way associative
fast
small
slow
large

## Slide 3: Today’s lesson plan
Virtual memory
  Why?
  How? Address translation
  Make it fast

## Slide 4: Virtual Memory: goals
Goal #1: Use main memory as a “cache” for disk storage
Goal #2: Allow programs to share main memory safely
  Each process gets a private virtual address space, isolated from other programs
CPU and OS translate virtual addresses to physical addresses
  VM “block” is called a page
  VM translation “miss” is called a page fault

## Slide 5: Sharing memory safely using VM
unused
unused
unused
unused
0x0000
0xffff
0x0000
0xffff
0x0000
0xffff
P1’s address space
P2’s address space
Physical memory
Virtual page number
Physical page number
0
47
Page offset
Page offset
translation
?
?
Suppose page size is 4KB,
how many bits in page offset?
212= 4KB, so 12 bits

## Slide 6: Mapping from Virtual to Physical pages
“Fully associative”
  A virtual page can map to any physical page
Use an index called “page table” to store the mapping
  No need to check all physical pages for a match
OS populates the page table for each process
  Page table is stored in the main memory
CPU (MMU) performs translation using the page table

## Slide 7: Translation using the page table
PTE-0 :
Virtual page number
Physical page number
0
47
Page offset
Page offset
v
W
S
Physical Page #
1
0
0
0x12….34
0
0
0
0x11…56
1
1
0
0x21…36
1
1
0
0x71…80
….
PTE-2 :
PTE-1 :
PTE-3 :
….
writable?
accessible by
OS only?
valid?
Each process has its own page table
A special register, “page table register”
stores the base (physical) address of
the running process’ page table
PTE: Page Table Entry

## Slide 8: Page Fault
PTE-0 :
valid?
writable?
accessible by
OS only?
Virtual page number
Physical page number
0
47
Page offset
Page offset
v
W
S
Physical Page #
1
0
0
0x12….34
0
0
0
0x11…56
1
1
0
0x21…36
1
1
0
0x71…80
….
PTE-2 :
PTE-1 :
PTE-3 :
….
Page fault occurs when
  “v” is invalid
  “w” is invalid for a write access
  “s” is invalid for a non-OS access
OS handles page fault by either
  fix page table or terminate process
PTE: Page Table Entry

## Slide 9: One level page table is impractical
How large is the page table for 48-bit virtual address space?
  Page size 4KB
248/212= 236 pages
Page Table size = 236 pages * 8 byte-PTE/page = 239 bytes = 0.5TB!!!

## Slide 10: Multi-level page tables
Problem
how to reduce # of page table entries required?
Solution
Multi-level page table
  A tree of “page tables”

## Slide 11: 2-level Paging Example
6-bit virtual and physical address, 4-byte page

## Slide 12: 2-level Paging Example
6-bit virtual and physical address, 4-byte page
1-level page table
Suppose a process has only two 2 mapped virtual pages
1100 | 1
0000 | 0
... | ..
0000 | 0
0100 | 1
24 PTEs
1-level Page Table
v
PPN

## Slide 13: 2-level Paging Example
6-bit virtual and physical address, 4-byte page
2-level page table
Suppose a process has only two 2 mapped virtual pages
24 PTEs
1-level Page Table
0101 | 1
0000 | 0
0000 | 0
1101 | 1
22 L0
PTEs
1100 | 1
0000 | 0
0000 | 0
1100 | 1
1111 | 1
0000 | 0
0000 | 0
0100 | 1
0101
is PPN of L1
page table
22 L1
PTEs
1100 | 1
0000 | 0
... | ..
0000 | 0
0100 | 1

## Slide 14: 2-level Paging Example
1-level Page Table
1 1 1 1
10
Virtual
Page #
Page
offset
Index to
page table
how to perform address translation?
  1-level page table
1100 | 1
0000 | 0
... | ..
0000 | 0
0100 | 1

## Slide 15: 2-level Paging Example
how to perform address translation?
  2-level page table
1-level Page Table
1 1 1 1
10
Virtual
Page #
Page
offset
Index to
page table
1 1
10
Index to
L0 table
Page
offset
1 1
Index to
L1 table
1100 | 1
0000 | 0
... | ..
0000 | 0
0100 | 1
0101 | 1
0000 | 0
0000 | 0
1101 | 1
1100 | 1
0000 | 0
0000 | 0
1100 | 1
1111 | 1
0000 | 0
0000 | 0
0100 | 1

## Slide 16: X86_64 and RISC-V use 4-level page table
63
0
…
…
…
…
…
…
…
…
…
Level 0
Level 1
Level 2
Level 3
48
47
39
38
30
29
21
20
Reserved
L0 Offset
L1 Offset
L2 Offset
Page Offset
L3 Offset
12
11
Page table register
Root Addr
4-level page table
9-bit index per level

## Slide 17: Example translation using a 4-level table
63
0
Level 0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
Page table register
Virtual Address: 0x80801fffa8
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
0x3466001
0x3467001
0x3468001
unused
…
Physical address
of the 1st entry at
level 1
4-level page table

## Slide 18: Example translation using a 4-level table
Virtual Address: 0x80801fffa8
63
0
Level 0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
0x3466001
0x3467001
0x3468001
unused
…
Physical address
of the 1st entry at
level 1
4-level page table
Page table register

## Slide 19: Example translation using a 4-level table
63
0
Level 0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
Virtual Address: 0x80801fffa8
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
0x3466001
0x3467001
0x3468001
unused
…
Level 1
0x3587001
unused
0x3588001
unused
…
Physical address
of the 1st entry at
level 1
Physical address
of the 1st entry at
level 2
4-level page table
Page table register

## Slide 20: Example translation using a 4-level table
Virtual Address: 0x80801fffa8
63
0
Level 0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
0x3466001
0x3467001
0x3468001
unused
…
Level 1
0x3587001
unused
0x3588001
unused
…
Physical address
of the 1st entry at
level 1
Physical address
of the 1st entry at
level 2
4-level page table
Page table register

## Slide 21: Example translation using a 4-level table
63
0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
Virtual Address: 0x80801fffa8
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
Level 1
Physical address
of the 1st entry at
level 1
Physical address
of the 1st entry at
level 2
Level 2
0x3678001
0x3579001
unused
unused
…
Physical address
of the 1st entry at
level 3
4-level page table
Level 0
0x3466001
0x3467001
0x3468001
unused
…
0x3587001
unused
0x3588001
unused
…
Page table register

## Slide 22: Example translation using a 4-level table
Virtual Address: 0x80801fffa8
63
0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
Physical address
of the 1st entry at
level 2
Level 2
Physical address
of the 1st entry at
level 3
4-level page table
Level 1
Physical address
of the 1st entry at
level 1
0x3678001
0x3579001
unused
unused
…
Level 0
0x3466001
0x3467001
0x3468001
unused
…
0x3587001
unused
0x3588001
unused
…
Page table register

## Slide 23: Example translation using a 4-level table
63
0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
Virtual Address: 0x80801fffa8
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
Physical address
of the 1st entry at
level 2
Level 2
Physical address
of the 1st entry at
level 3
Level 3
0x5788001
0x5789001
0x578a001
0x5799001
…
Physical address
of the page
4-level page table
Level 1
Physical address
of the 1st entry at
level 1
0x3678001
0x3579001
unused
unused
…
Level 0
0x3466001
0x3467001
0x3468001
unused
…
0x3587001
unused
0x3588001
unused
…
Page table register

## Slide 24: Example translation using a 4-level table
63
0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
Virtual Address: 0x80801fffa8
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
Physical address
of the 1st entry at
level 2
Level 2
Physical address
of the 1st entry at
level 3
Level 3
0x5788001
0x5789001
0x578a001
0x5799001
…
Physical address
of the page
4-level page table
Level 1
Physical address
of the 1st entry at
level 1
0x3678001
0x3579001
unused
unused
…
Level 0
0x3466001
0x3467001
0x3468001
unused
…
0x3587001
unused
0x3588001
unused
…
Physical Address: 0x5799fa8
Page table register

## Slide 25: Fast translation using a TLB
Address translation is costly
  How many memory accesses per actual data access? (4-level page table)
  4 (page table access) + 1 (data access)
Solution?
  Cache virtualphysical page mappings in a fast small cache
  This cache is called Translation Lookaside Buffer (TLB)

## Slide 26: Address translation with TLB
Valid | Tag (VPN) | Data (PPN)
Virtual page number
Page offset
=
TLB Hit!
If TLB miss, translate using 4-level page table, populate TLB with resulting VPN->PPN
TLB cache can be direct mapped or set associative
Like data cache, there can >1 level of TLB cache

## Slide 27: Summary
Virtual memory allows multiple processes to share memory safely
Address translation uses multi-level page table
  Speed up translation using TLB
Memory hierarchy
  L1 cache  L2 cache  …  DRAM memory  disk
Memory system design is critical for performance