## Slide 1: Floating point
Jinyang Li
Some are based on Tiger Wang’s slides

## Slide 2: Representing Real Numbers using bits
-
+

## Slide 3: Representing Numbers in bits
-
+
1
2
-3
-2
-1
What we have studied
3
2n-1-1
2n-1
0
2n-1

## Slide 4: Representing Numbers in bits
Today: How to represent fractional numbers?
-
+
1
2
-3
-2
-1
3
2n-1-1
2n-1
0
2n-1

## Slide 5: Representing real numbers: decimal
Real Numbers | Decimal Representation (Expansion)
11 / 2 | (5.5)10
1 / 3 | (0.3333333...)10
√2 | (1.4128…)10

## Slide 6: Representing real numbers: decimal
Real Numbers | Decimal Representation (Expansion)
11 / 2 | (5.5)10
1 / 3 | (0.3333333...)10
√2 | (1.4128…)10
(5.5)10 = 5 * 100+ 5 * 10-1
(0.333333...)10 = 3 * 10-1 + 3 * 10-2 + 3 * 10-3 + ...
(1.4128...)10 = 1 * 100 + 4 * 10-1 + 1 * 10-2 + 2 * 10-3 + ...

## Slide 7: Representing real numbers: decimal
Real Numbers | Decimal Representation (Expansion)
11 / 2 | (5.5)10
1 / 3 | (0.3333333...)10
√2 | (1.4128…)10
(5.5)10 = 5 * 100+ 5 * 10-1
(0.333333...)10 = 3 * 10-1 + 3 * 10-2 + 3 * 10-3 + ...
(1.4128...)10 = 1 * 100 + 4 * 10-1 + 1 * 10-2 + 2 * 10-3 + ...
r10 = (dmdm-1…d1d0.d-1d-2…d-n)10
=

## Slide 8: Binary Representation
(5.5)10 = 4 + 1 + 1 / 2
= 1 * 22 + 0 * 21 + 1 * 20 + 1 * 2-1

## Slide 9: Binary Representation
(5.5)10 = 4 + 1 + 1 / 2
= 1 * 22 + 0 * 21 + 1 * 20 + 1 * 2-1
= (101.1)2

## Slide 10: Binary Representation
(5.5)10 = 4 + 1 + 1 / 2
= 1 * 22 + 0 * 21 + 1 * 20 + 1 * 2-1
= (101.1)2
(0.333333...)10 = 1 / 4 + 1 / 16 + 1 / 64 + ...
= (0.01010101...)2

## Slide 11: Binary Representation
r10 = (dmdm-1d1d0.d-1d-2…d-n)10
= (bpbp-1b1b0.b-1b-2…b-q)2
2p
2p-1
2
1
1/2
1/4
1/2q
.

## Slide 12: Exercise
Binary Expansion | Formula | Decimal
10.0112 |  | 
 | 2-3 + 2-4 + 2-6 | 
 | 2-1 + 2-2 + 2-3 + 2-4 | 

## Slide 13: Exercise
Binary Expansion | Formula | Decimal
10.0112 | 21 + 2-2 + 2-3 | 2.37510
0.0011012 | 2-3 + 2-4 + 2-6 | 0.20312510
0.11112 | 2-1 + 2-2 + 2-3 + 2-4 | 0.937510

## Slide 14: How to represent real numbers in fixed # of bits?
Fixed point
s | b14 | b13 | b12 | … | b1 | b0 | b-1 | b-2 | b-3 | … | b-14 | b-15 | b-16
sign
15 bits
Fixed position e.g. middle
16 bits

## Slide 15: Naive idea: Fixed point
Fixed point
s | b14 | b13 | b12 | … | b1 | b0 | b-1 | b-2 | b-3 | … | b-14 | b-15 | b-16
sign
15 bits
Fixed position e.g. middle
16 bits
( 10.011 )2
0 | 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 | 0 1 1 0 0 0 0 0 0 0 0 0 0 0 0

## Slide 16: Problems of Fixed Point
  Limited range and precision: e.g., 32 bits
  Largest number:
  Highest precision:
Rarely used (No built-in hardware support)
2-16
215 (011...111)2

## Slide 17: The idea
Limitation of fixed point notation:
  Represents evenly spaced fractional numbers
     hard tradeoff between high precision and high magnitude
How about un-even spacing between numbers?
-
+
0

## Slide 18: Floating Point: decimal
Based on the normalized scientific notation
r10 = +M * 10E, where 1 <= M < 10
M: significant (mantissa), E: exponent

## Slide 19: Floating Point: decimal
Example:
365.25 = 3.6525 * 102
0.0123 = 1.23 * 10-2
Decimal point floats to the position immediately
after the first nonzero digit.

## Slide 20: Floating Point: binary
Binary (normalized) scientific notation:
(5.5)10 = (101.1)2 = (1.011)2 * 22
r10 = +M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…bn )2
M: significant, E: exponent

## Slide 21: Exercises
The scientific notation of (10.25)10 is ?

## Slide 22: Exercises
The scientific notation of (10.25)10 is ?
(10.25)10 = (1010.01)2 = (1.01001)2 * 23

## Slide 23: How to represent a binary scientific notation in fixed # of bits?
s | exp (E) | sig (M)
31
30
23
22
0
( 1.b1b2b3…bn )2
r10 = +M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…bn )2
M: significant, E: exponent

## Slide 24: How to represent a binary scientific notation in fixed # of bits?
s | exp (E) | fraction (F)
31
30
23
22
0
( b1b2b3…b23 )2
r10 = +M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…b23 )2
M: significant, E: exponent

## Slide 25: How to represent a binary scientific notation in fixed # of bits?
0 | 0000 0010 | 0110 0000 0000 0000 0000 000
31
30
23
22
0
(5.5)10 = (101.1)2 = (1.011)2 * 22
( b1b2b3…b23 )2
r10 = +M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…b23 )2
M: significant, E: exponent

## Slide 26: Exercise
What’s the normalized representation of (71)10 and (10.25)10

## Slide 27: Exercise
What’s the normalized representation of (71)10 and (10.25)10
0 | 0000 0110 | 0001 1100 0000 0000 0000 000
31
30
23
22
0
(71)10 = (1000111)2 = (1.000111)2 * 26
(10.25)10 = (1010.01)2 = (1.01001)2 * 23
0 | 0000 0011 | 0100 1000 0000 0000 0000 000
31
30
23
22
0

## Slide 28: Toy Number System
s | exp (E) | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
Largest positive number ?

## Slide 29: Toy Number System
s | exp (E) | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
Largest positive number ?
0 | 1 1 1 | 1 1
( 1.11 )2 * 27 = 224

## Slide 30: Toy Number System
s | exp (E) | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
Largest positive number: 224
Smallest positive number ?

## Slide 31: Toy Number System
s | exp (E) | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
Largest positive number: 224
Smallest positive number: 1
0 | 0 0 0 | 0 0
( 1.00 )2 * 20 = 1

## Slide 32: Toy Number System
s | exp (E) | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
Positive number: 1 to 224
Negative number: -224 to -1
No more bit patterns left to represent numbers
(-1, 1)

## Slide 33: Questions
How to represent
numbers close or equal to 0?
special cases:
  the result of dividing by 0, e.g. 1/0 ?
Lots of different implementations around 1950s!

## Slide 34: IEEE Floating Point Standard
Prof. William Kahan
University of California at Berkeley
Turing Award (1989)
IEEE p754
A standard for binary
floating point representation

## Slide 35: The Only Book Focuses On IEEE Floating Point Standard
https://cs.nyu.edu/overton/NumericalComputing/protected/NumericalComputingSIAM.pdf
With you nyu netid/password. You can also search the pdf with google.

## Slide 36: What we have learnt so far
normalized representation of floating point
0 | 0000 0010 | 0110 0000 0000 0000 0000 000
31
30
23
22
0
(5.5)10 = (101.1)2 = (1.011)2 * 22
how to represent numbers in range (-1,1)
how to represent special cases? e.g.
r10 = +M * 2E M = ( 1.b1b2b3…b23 )2

## Slide 37: Goals of IEEE Standard
Consistent representation of floating point numbers
Correctly rounded floating point operations, using several rounding modes.
Consistent treatment of exceptional situations such as division by zero

## Slide 38: Restrictions on Normalized Representation
r10 = +M * 2E M = ( 1.b0b1b2b3…bn )2
s | exp (E) | fraction (F)
31
30
23
22
0
( b0b1b2b3…bn )2
E can not be (1111 1111)2 or (0000 0000)0
Emax = ?
Emin = ?
254, (1111 1110)2
1, (0000 0001)2

## Slide 39: Exponential Bias
r10 = +M * 2E, M = ( 1.b0b1b2b3…bn )2
s | exp (E) + 127 | fraction (F)
31
30
23
22
0
( b0b1b2b3…bn )2
Bias: 127
To represent (-1,1), we must allow negative exponent.
How to represent negative E?
  2’s complement
  use bias

## Slide 40: IEEE normalized representation
r10 = +M * 2E, M = ( 1.b0b1b2b3…bn )2
s | exp (E) + 127 | fraction (F)
31
30
23
22
0
( b0b1b2b3…bn )2
Bias: 127
Emax = ?
Emin = ?
254 – 127 = 127
1 – 127 = -126
Smallest positive number: ?
Negative number with smallest absolute value: ?
2-126
-2-126

## Slide 41: Questions
Q1. Why using bias?
Q2. Why is bias 127?

## Slide 42: Questions
Q1. Why using bias instead of 2’s complement?
Answer: easier circuitry for comparison.
Notes: Circuitry for handling 2’s complement is more complex than handling unsigned only.
Although 2’s complement has the same addition/substraction logic as unsigned, its comparison logic is different.
(1000 0000) in 2’s complement is less than (0000 0001) but
(1000 0000) in unsigned is more than (0000 0001) but

## Slide 43: Questions
Q2. Why is bias 127?
A2. Balance positive exponents (magnitude) and negative exponents (precision)

## Slide 44: Toy 6-bit Floating Point
s | exp (E) + 3 | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
bias: 3
Smallest positive number ?

## Slide 45: Toy 6-bit Floating Point
s | exp (E) + 3 | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
bias: 3
Smallest positive number: 0.25
0 | 0 0 1 | 0 0
( 1.00 )2 * 2-2 = 0.25
Smallest number >0.25?
( 1.01 )2 * 2-2 = 0.25+0.0625

## Slide 46: Toy 6-bit Floating Point
s | exp (E) + 3 | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
bias: 3
Chart: 
| 0.25 | 0.3125 | 0.375 | 0.4375 | 0.5 | 0.625 | 0.75 | 0.875 | 1.0 | 1.25 | 1.5 | 1.75 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 10.0 | 12.0 | 14.0 | -0.25 | -0.3125 | -0.375 | -0.4375 | -0.5 | -0.625 | -0.75 | -0.875 | -1.0 | -1.25 | -1.5 | -1.75 | -2.0 | -2.5 | -3.0 | -3.5 | -4.0 | -5.0 | -6.0 | -7.0 | -8.0 | -10.0 | -12.0 | -14.0
Normalized | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
?

## Slide 47
represent values which are
close and equal to 0

## Slide 48: IEEE denormalized representation
r10 = +M * 2E
s | exp (E) + 127 | fraction (F)
31
30
23
22
0
Normalized Encoding:
1 <= M < 2, M = ( 1.F )2
s | 0000 0000 | fraction (F)
31
30
23
22
0
Denormalized Encoding:
0 <= M < 1, M = ( 0.F )2
E = 1 – Bias = -126

## Slide 49: Zeros
0 | 0000 0000 | 0000 0000 0000 0000 0000 000
+0.0
1 | 0000 0000 | 0000 0000 0000 0000 0000 000
-0.0

## Slide 50: Examples
0 | 0000 0000 | 1000 0000 0000 0000 0000 000
(0.1)2 * 2-126
1 | 0000 0000 | 0101 0100 0000 0000 0000 000
-(0.010101)2 * 2-126

## Slide 51: Toy 6-bit Floating Point
s | exp (E) | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
bias: 3
Denormalized encoding

## Slide 52: Special Values
s | 1111 1111 | fraction (F)
31
30
23
22
0
Special Value’s Encoding:
values | sign | frac
+ | 0 | all zeros
- | 1 | all zeros
NaN | any | non-zero

## Slide 53: Exercises
representation | E | M | V
0100 1001 0101 0000 0000 0000 0000 0000 |  |  | 
 |  |  | 2.5 * 2-127
 |  |  | -1.25 * 2-111
1111 1111 1111 1111 0000 0000 0000 0000 |  |  | 
1111 1111 1000 0000 0000 0000 0000 0000 |  |  | 
 |  |  | 1.5 * 2-127

## Slide 54: Exercises
representation | E | M | V
0100 1001 0101 0000 0000 0000 0000 0000 | 146 – 127 = 19 | (1.101)2 = 1.625 | 1.625 * 219
0000 0000 1010 0000 0000 0000 0000 0000 | 1 – 127 = -126 | (1.01)2 = 1.25 | 2.5 * 2-127 = (1.01)2 * 2-126
1000 1000 0010 0000 0000 0000 0000 0000 | 16 – 127 = -111 | (1.01)2 = 1.125 | -1.25 * 2-111
1111 1111 1111 1111 0000 0000 0000 0000 | - | - | Nan
1111 1111 1000 0000 0000 0000 0000 0000 | - | - | -
0000 0000 0110 0000 0000 0000 0000 0000 | -126 | (0.11)2 | (0.11)2 * 2-126 = 1.5 * 2-127

## Slide 55: Distribution of Representable Values
NaN
NaN
+

0
+Denorm
+Normalized
-Denorm
-Normalized
+0

## Slide 56: Distribution of Representable Values
NaN
NaN
+

0
+Denorm
+Normalized
-Denorm
-Normalized
+0
  What if the result of computation is at ?

## Slide 57: Rounding
Goal
  Use the “closest” representable value x’ to represent x.
Round modes
  Round-down
  Round-up
  Round-toward-zero
  Round-to-nearest (Round to even in text book)

## Slide 58: Round down in toy 6-bit FP
-0.875
-0.75
0.5
0.625
Round(-0.86) = ?
Round(0.55) = ?
Round(x) = x- (x-<= x)

## Slide 59: Round down in toy 6-bit FP
-0.875
-0.75
0.5
0.625
Round(-0.86) = -0.875
Round(x) = x- (x-<= x)
Round(0.55) = 0.5

## Slide 60: Round up in toy 6-bit FP
Round(x) = x+ (x+>= x)

## Slide 61: Round up in toy 6-bit FP
-0.875
-0.75
0.5
0.625
Round(-0.86) = ?
Round(0.55) = ?
Round(x) = x+ (x+>= x)

## Slide 62: Round up in toy 6-bit FP
-0.875
-0.75
0.5
0.625
Round(-0.86) = -0.75
Round(0.55) = 0.625
Round(x) = x+ (x+>= x)

## Slide 63: Round towards zero in toy 6-bit FP
Round(x) = x+ if x < 0
Round(x) = x- if x > 0

## Slide 64: Round towards zero in toy 6-bit FP
-0.875
-0.75
0.5
0.625
Round(x) = x+ if x < 0
Round(x) = x- if x > 0
Round(-0.86) = ?
Round(0.55) = ?

## Slide 65: Round towards zero in toy 6-bit FP
-0.875
-0.75
0.5
0.625
Round(-0.86) = -0.75
Round(x) = x+ if x < 0
Round(x) = x- if x > 0
Round(0.55) = 0.5

## Slide 66: Round to nearest in toy 6-bit FP
Round(x) either x+ or x- , whichever is nearer to x.

## Slide 67: Round to nearest in toy 6-bit FP
Round(x) either x+ or x- , whichever is nearer to x.
-0.875
-0.75
0.5
0.625
Round(-0.86) = ?
Round(0.55) = ?

## Slide 68: Round to nearest in toy 6-bit FP
Round(x) either x+ or x- , whichever is nearer to x.
-0.875
-0.75
0.5
0.625
Round(-0.86) = -0.875
Round(0.55) = 0.5

## Slide 69: Round to nearest; ties to even
Round(x) either x+ or x- , whichever is nearer to x.
-0.875
-0.75
0.5
0.625
Round(-0.86) = -0.875
Round(0.55) = 0.5
In case of a tie, the one with its least significant bit equal to zero is chosen.

## Slide 70: single/ double precision
s | E + 127 | frac
31
30
23
22
0
single precision (32 bits)
s | E + 1023 | frac
63
62
52
51
0
double precision (64 bits)
float f = 0.1
double d = 0.1

## Slide 71: single/ double precision
 | Emin | Emax | Nmin | Nmax
Float | -126 | 127 | ≈ 2-126 | ≈ 2128
Double | -1022 | 1023 | ≈ 2-1022 | ≈ 21024

## Slide 72: How does CPU know if it is floating point or integers ?
By having specific instruction for floating points operation.

## Slide 73
CPU
decoder
Memory
……
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
add $1, $2
IU
FPU
int d = 1 + 2

## Slide 74
CPU
decoder
Memory
……
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
addss $1, $2
IU
FPU
float f = 0.1 + 0.2