## Slide 1: Pipelined CPU
Jinyang Li
Based on the slides of Patterson and Hennessy

## Slide 2: Today’s lesson plan
Pipeline control path
Handling pipeline hazard
  Structure
  Data
  Control

## Slide 3: What we’ve learnt: basic 5-stage pipeline (datapath)

## Slide 4: Pipelined Control (Simplified)
Set in EX
Set in MEM
Set in WB

## Slide 5: Pipelined Control
ALUSrc
ALUOp
MemWrite
Branch
PCSrc
MemToReg
RegWrite
Control signals derived from instruction, same as
in single-cycle implementation

## Slide 6: Today’s lesson plan
Pipeline control path
Handling pipeline hazard
  Structure (solution: add resources)
  Data (solution: forwarding or stall)
  Control

## Slide 7: Data Hazards in ALU Instructions
Example instruction sequence:
  sub x2, x1,x3 and x12,x2,x5 or x13,x6,x2 add x14,x2,x2 sd x15,100(x2)

## Slide 8: Data hazard in ALU instructions
Data hazards

## Slide 9: Data Hazards in ALU Instructions
Solution: forwarding (aka bypassing)
  Use the result after it’s computed
  Aka, don’t wait for the result to be stored in register

## Slide 10: Using forwarding to resolve data hazard (cycle-4)
sub x2,x1,x3
and x12,x2,x5
or x13,x6,x2
add x14,x2,x2
Notes: Draw lines

## Slide 11: Using forwarding to resolve data hazard (cycle-5)
sub x2,x1,x3
and x12,x2,x5
or x13,x6,x2
add x14,x2,x2
sd x15,100(x2)
Notes: Draw lines

## Slide 12: Forwarding Paths
EX-hazard
MEM-hazard

## Slide 13: Detecting when to use forwarded data
Pass register numbers along pipeline
  e.g., ALU operand register numbers (in EX stage) are:
    ID/EX.RegisterRs1, ID/EX.RegisterRs2
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs1
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRs2
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs1
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRs2
EX-hazard:
Fwd from EX/MEM pipeline reg
Mem-hazard: Fwd from MEM/WB pipeline reg

## Slide 14: Detecting when to use forwarded data
If forwarding instruction will write to a register!
  EX/MEM.RegWrite, MEM/WB.RegWrite
if destination register (Rd) for that instruction is not x0
  EX/MEM.RegisterRd ≠ 0, MEM/WB.RegisterRd ≠ 0
X0 is always 0 in RISC-V
AND

## Slide 15: Double Data Hazard
Consider the sequence:
  add x1,x1,x2 add x1,x1,x3 add x1,x1,x4
Both EX- and Mem-hazards occur
  use the most recent
  aka, only fwd Mem-hazard if EX hazard condition isn’t true
MEM hazard
EX hazard

## Slide 16: Load-Use Data hazard Detection
Load-use hazard cannot be resolved using forwarding alone
Check load-use hazard using condition
  ID/EX.MemRead and ((ID/EX.RegisterRd = IF/ID.RegisterRs1) or (ID/EX.RegisterRd = IF/ID.RegisterRs1))
If detected, stall and insert bubble
ld x2, 20(x1)
and x4, x2, x5
Cannot be forwarded

## Slide 17: How to Stall the Pipeline (aka insert bubble)
Force control values in ID/EX register to 0
  EX, MEM and WB do nop (no-operation)
Prevent update of PC and IF/ID register
  Current instruction is decoded again
  Following instruction is fetched again
  1-cycle stall allows MEM to read data for ld
    Can subsequently forward to EX stage

## Slide 18: Load-Use Data Hazard
Stall inserted here

## Slide 19: Datapath with Hazard Detection
If hazard is detected, set WB/MEM/EX controls to zero (so no registers/memory is written)

## Slide 20: Today’s lesson plan
Pipeline control path
Handling pipeline hazard
  Structure (solution: add resources)
  Data (solution: forwarding or stall)
  Control (solution: stall, branch prediction)

## Slide 21: Branch Hazard
If branch outcome is determined in MEM
PC
Flush 3 instructions (set controls to 0)
Instruction address
If x1==x0
Pc = pc+16*2

## Slide 22: Reducing Branch Delay
Add hardware to determine branch outcome earlier (e.g. ID instead of MEM)  fewer instructions to flush
36: sub x10, x4, x8 40: beq x1, x3, 16 // PC-relative branch // to 40+16*2=72 44: and x12, x2, x5 48: or x13, x2, x6 52: add x14, x4, x2 56: sub x15, x6, x7 ... 72: ld x4, 50(x7)
How many instructions to flush
if branch outcome is known in ID?
IF
ID
EXE
MEM
WB
44: and
IF
ID
EXE
MEM
WB
IF
ID
EXE
MEM
WB
72: ld
clock-1
clock-2
clock-3
40: beq
clock-4
clock-5

## Slide 23: Branch determined in ID and is taken
Clock 2
Additional comparator
to determine branch outcome
Additional adder for
calculating target address
If branch is taken, set IF/ID.Flush
IF/ID.Flush

## Slide 24: Branch determined in ID and is taken
Clock 3
If IF/ID.Flush is set, zero out controls so
memory/register won’t be written in MEM and WB

## Slide 25: Dynamic Branch Prediction
Our simple 5-stage pipeline’s branch penalty is 1 bubble, but
  In deeper pipelines, branch penalty is more significant
Solution: dynamic prediction
  Branch prediction buffer (aka branch history table)
    Indexed by recent branch instruction addresses
    Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 26: 1-Bit Predictor: Shortcoming
Inner loop branches mispredicted twice!
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer
  Mispredicted as taken on last iteration of inner loop
  Then mispredicted as not taken on first iteration of inner loop next time around
for (i = 0; i != 10; i++) {
for (j = 0; j != 100; j++) {
…
}
}

## Slide 27: 2-Bit Predictor
Only change prediction on two successive mispredictions

## Slide 28: Calculating Branch Target (needed if branch is predicted taken)
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately

## Slide 29: Exceptions and Interrupts
“Unexpected” events requiring change in flow of control
Exception
  Arises within the CPU
    e.g., undefined opcode, syscall, memory permission error, divide by zero, …
Interrupt
  From an external I/O controller
Dealing with them without sacrificing performance is hard

## Slide 30: Handling Exceptions
Save PC of offending (or interrupted) instruction
  In RISC-V: Supervisor Exception Program Counter (SEPC)
Save indication of the problem
  In RISC-V: Supervisor Exception Cause Register (SCAUSE)
Jump to handler (aka code in OS kernel)
  Assume at 0000 0000 1C09 0000hex
OS’s handler does either of the following:
  Take corrective action; restart offending instruction
  Terminate program; report cause

## Slide 31: An Alternate Mechanism
Vectored Exception/Interrupts (x86)
Vector index (interrupt descriptor) specifies cause of exception
  E.g. in x86, 0 (divide by zero), 6 (invalid opcode), …
OS sets up the Interrupt Descriptor Table
  IDT[i] contains handler address, where I is vector index.

## Slide 32: Exceptions in a Pipeline
Another form of control hazard
Consider malfunction on add in EX stage
  add x1, x2, x1
  Prevent x1 from being clobbered
  Complete previous instructions
  Flush add and subsequent instructions
  Save PC (of offending instruction) in SEPC and set SCAUSE with cause
  Transfer control to handler
Similar to mispredicted branch
  Use much of the same hardware

## Slide 33: Exception Example
Exception on add in
  40 sub x11, x2, x4 44 and x12, x2, x5 48 orr x13, x2, x6 4c add x1, x2, x1 50 sub x15, x6, x7 54 ld x16, 100(x7) …
Handler
  1C090000 sd x26, 1000(x10) 1c090004 sd x27, 1008(x10) …

## Slide 34: Exception Example
These signals are set
if add malfunctioned
Handler address is used for IF in next cycle

## Slide 35: Exception Example
Offending instruction (add x1, x2, x1) becomes a bubble (so it won’t clobber registers)
Instructions in exception handler

## Slide 36: Summary
Pipeline increases throughput by overlapping execution of multiple instructions
Pipeline hazard
  Structure (solution: add resources)
  Data (solution: forwarding, bubble)
  Control (solution: bubble, branch prediction)