## Slide 1: Sequential Logic
Jinyang Li

## Slide 2: What we’ve learnt so far
Combinatorial logic
  E.g. Multiplexors (Mux), Decoders
  Two ways of building a CL
    Truth table  sum of products circuits
    ROM
ALU
  Compute all operations (+, OR, AND, NOR), multiplexer picks the result
  Building a 64-bit adder
    Ripple carry chains together 1-bit adders
    Carry lookahead

## Slide 3: Today’s lesson plan
Sequential circuit: Memory (state) elements
Sequential circuit: Finite State Machine

## Slide 4: Downside of ripple carry?
a63
b63
Result63
ALU63
Must wait for sequential evaluation of all 64 1-bit adders

## Slide 5: In search of a faster adder
Ripple carry:
  Delay: 64*1BitAdderGateDelay, Gate count: 64*c
Brute-force (truth table->PLA)
  Delay: 2, Gate count: O(264+64)
Clever designs in between?
Idea #1: (Carry lookahead) compute multiple carry-bits at a time

## Slide 6: Faster adder: carry lookahead
Idea #1: (Carry lookahead) compute multiple carry-bits at a time
ci+1 = aibi + (ai + bi)ci
CarryIn to i-th bit
= CarryOut of (i-1)-th bit
CarryOut of i-th bit
= CarryIn of (i+1)-th bit
ci+1 = gi + pici
gi = aibi , pi= ai + bi
gi
Generate
generates carryOut
regardless of carryIn
pi
Propagate
propagates carryIn
to carryOut

## Slide 7: Faster adder: carry lookahead
Idea #1: (Carry lookahead) compute multiple carry-bits at a time
Computing all carry-bits of a 4-bit adder:
Delay?
4-bit ripple carry delay: 2 * 4
3

## Slide 8: Faster adder: carry lookahead
Idea #1: (Carry lookahead) compute multiple carry-bits at a time
Computing all result bits in a 4-bit adder:

## Slide 9: Faster adder: carry lookahead
Build a 16-bit adder with carry-ahead 4-bit adders
carryIn (C0)
ALU0
a[0:3]
b[0:3]
ALU1
ALU2
ALU3
a[4:7]
b[4:7]
a[8:11]
b[8:11]
a[12:15]
b[12:15]
C1
C2
C3
carry
lookahead
carryOut (C4)
p0
g0
p1
g1
p2
g2
p3
g3
P0
G0
P1
G1
P2
G2
P3
G3
P0 = p3· p2· p1· p0
P1 = p7· p6· p5· p4
P2 = p11· p10· p9· p8
P3 = p15· p14· p13· p12
G0 = g3+ p3·g2 +
p3· p2·g1+ p3· p2·p1 ·g0
G1 = g7+ p7·g6 +
p7· p6·g5+ p7· p6·p5 ·g4
G2 = g11+ p11·g10 +
p11· p10·g9+ p11· p10·p9·g8
G3 = g15+ p15·g14 +
p15·p14·g13+ p15·p14·p13·g12
C1=G0+P0 ·C0
C2=G1+P1·G0+ P1· P0 ·C0
C3= G2+ P2·G1 + P2· P1· G0
+ P2· P1· P0 ·C0
C3= G3+ P3·G2 + P3· P2· G1
+ P3· P2· P1· G0
+ P3· P2· P1· P0 ·C0

## Slide 10: Two types of logic circuits
Combinatorial circuit
  PLA: Truth table  sum of products PLA circuit
  ROM (read-only memory): Addresses (inputs) contents (outputs)
Sequential circuit
  output is dependent on both input and state (memory elements)
Today’s lesson

## Slide 11: Sequential logic requires clock
When should the state element be updated?
Clock signal
Clock frequence = 1/clock_period
Clock
period
Clock
period
State element

## Slide 12: Clocks
Edge-triggered clocking: state content only changes on active clock edge

## Slide 13: Sequential logic requires clock
State
element
State changed to 1
Clock signal
Clock
period
Clock frequence = 1/clock_period
Clock
period
State changed to 0
State changed to 1

## Slide 14: Sequential logic requires clock
Combinatorial logic
State
element 1
State
element 2
Clock cycle
Valid content is read from state element 1
Valid content is written into state element 2
Delay of CL must be less than one clock cycle

## Slide 15: Sequential logic requires clock
Combinatorial logic
State
element
Clock cycle
Valid content is read from state element
Valid content is written into state element

## Slide 16: Memory (state) elements: unlocked S-R Latch
NOR
Stored content
Complement of stored content
S (set) | R (reset) | 
0 | 0 | keeps existing value
1 | 0 | Q=1
0 | 1 | Q=0
1 | 1 | Invalid

## Slide 17: Memory element: clocked D latch
Clock
State
Input
D latch: state is changed as long as clock is asserted
Clock signal
R
S
Latch is open; input is written to state
Latch is closed; state remains unchanged

## Slide 18: Memory element: Flip-flop
Flip-flop: state is changed only on (rising or falling) clock edge
D-flip-flop with a
falling-edge trigger
Q1
1st latch is open Q1=1
2nd latch is open Q=Q1
1st latch is closed

## Slide 19: Finite State Machine
Combinatorial logic  truth table
Sequential logic  F(inite) S(tate) M(achine)
  Input and current state determine next state and outputs

## Slide 20: Finite State Machine
New state is computed every clock cycle
Combinatorial
logic

## Slide 21: FSM example: traffic light control
State:
NSgreen: traffic light is green in N-S (red in E-W)
EWgreen: traffic light is green in E-W (red in N-S)
Inputs:
NScar: car detected in N-S
EWcar: car detected in E-W
Outputs:
NSlite: 1 if state=NSgreen
EWlite: 1 if state=EWgreen
How many bits needed to represent state values?

## Slide 22: FSM example: traffic light control
NSgreen
EWgreen
NScar
EWcar
NScar
EWcar
Clock cycles once every 30 seconds
Clock speed?

## Slide 23: FSM example: traffic light
FSM is determined by NextState function and Output function
NSg
EWg
NScar
EWcar
NScar
EWcar

## Slide 24: FSM example: traffic light
FSM is determined by NextState function and Output function
0 (Nsgreen)
0 (Nsgreen)
0 (Nsgreen)
0 (Nsgreen)
1 (Ewgreen)
1 (Ewgreen)
1 (Ewgreen)
1 (Ewgreen)
0 (Nsgreen)
1 (Ewgreen)
0 (Nsgreen)
1 (Ewgreen)
1 (Ewgreen)
1 (Ewgreen)
0 (Nsgreen)
0 (Nsgreen)
=
Current State

## Slide 25: FSM traffic light: next state function
State element
EWcar
NScar
Next

## Slide 26: FSM traffic light: output function
0
1
NSLite
EWLite =

## Slide 27: FSM traffic light: output function
State register
NSLite
EWLite

## Slide 28: Another FSM example: Electronic eye
FSM
left
middle
right
Lights are lit from left to right, then right to left and so on
State transition diagram?

## Slide 29: Memory element: Register file
Register file: a set of registers that can be read and written
😕Why reading two registers at a time?

## Slide 30: Register file: Read
Clock signal is assumed and not drawn

## Slide 31: Register file: Write
Clock signal is assumed and not drawn

## Slide 32: Register file
What if the same register is read and written in the same clock cycle?
  Return register value written in an earlier cycle
  Write of new value occurs on the clock edge (at the end of the current cycle)
Some register file can read value currently being written
  Requires additional logic in the register file

## Slide 33: Summary
Memory (state) elements
  Requires a clock signal to know when to update state value
  Unclocked S-R latch  Clocked D latch  Flip-flop
Sequential logic
  Finite state machine
  Decompose into two CL functions
    Next state function: compute next state value based on current state value and inputs
    Output function: compute output based on current state value and inputs