## Slide 1: Floating point
Jinyang Li
based on Tiger Wang’s slides

## Slide 2: Representing Real Numbers using bits
-
+

## Slide 3: Representing Real Numbers using bits
-
+
1
2
-3
-2
-1
What we have studied
3
2n-1-1
2n-1
0
2n-1

## Slide 4: Representing Real Numbers using bits
Today: How to represent fractional numbers?
-
+
1
2
-3
-2
-1
3
2n-1-1
2n-1
0
2n-1

## Slide 5: Decimal Representation
Real Numbers | Decimal Representation (Expansion)
11 / 2 | (5.5)10
1 / 3 | (0.3333333...)10
√2 | (1.4128…)10

## Slide 6: Decimal Representation
Real Numbers | Decimal Representation (Expansion)
11 / 2 | (5.5)10
1 / 3 | (0.3333333...)10
√2 | (1.4128…)10
(5.5)10 = 5 * 100+ 5 * 10-1
(0.333333...)10 = 3 * 10-1 + 3 * 10-2 + 3 * 10-3 + ...
(1.4128...)10 = 1 * 100 + 4 * 10-1 + 1 * 10-2 + 2 * 10-3 + ...

## Slide 7: Decimal Representation
Real Numbers | Decimal Representation (Expansion)
11 / 2 | (5.5)10
1 / 3 | (0.3333333...)10
√2 | (1.4128…)10
(5.5)10 = 5 * 100+ 5 * 10-1
(0.333333...)10 = 3 * 10-1 + 3 * 10-2 + 3 * 10-3 + ...
(1.4128...)10 = 1 * 100 + 4 * 10-1 + 1 * 10-2 + 2 * 10-3 + ...
r10 = (dmdm-1…d1d0.d-1d-2…d-n)10
=

## Slide 8: Binary Representation
(5.5)10 = 4 + 1 + 1 / 2
= 1 * 22 + 1 * 20 + 1 * 2-1

## Slide 9: Binary Representation
(5.5)10 = 4 + 1 + 1 / 2
= 1 * 22 + 0 * 21 + 1 * 20 + 1 * 2-1

## Slide 10: Binary Representation
(5.5)10 = 4 + 1 + 1 / 2
= 1 * 22 + 0 * 21 + 1 * 20 + 1 * 2-1
= (101.1)2

## Slide 11: Binary Representation
(5.5)10 = 4 + 1 + 1 / 2
= 1 * 22 + 0 * 21 + 1 * 20 + 1 * 2-1
= (101.1)2
(0.333333...)10 = 1 / 4 + 1 / 16 + 1 / 64 + ...
= (0.01010101...)2

## Slide 12: Binary Representation
r10 = (dmdm-1d1d0.d-1d-2…d-n)10
= (bpbp-1b1b0.b-1b-2…b-q)2
2p
2p-1
2
1
1/2
1/4
1/2q
.

## Slide 13: Exercise
Binary Expansion | Formula | Decimal
10.0112 |  | 
 | 2-3 + 2-4 + 2-6 | 
 | 2-1 + 2-2 + 2-3 + 2-4 | 

## Slide 14: Exercise
Binary Expansion | Formula | Decimal
10.0112 | 21 + 2-2 + 2-3 | 2.37510
0.0011012 | 2-3 + 2-4 + 2-6 | 0.20312510
0.11112 | 2-1 + 2-2 + 2-3 + 2-4 | 0.937510

## Slide 15: Intuitive Idea
Fixed point
s | b14 | b13 | b12 | … | b1 | b0 | b-1 | b-2 | b-3 | … | b-14 | b-15 | b-16
sign
15 bits
Fixed position e.g. middle
16 bits

## Slide 16: Intuitive Idea
Fixed point
s | b14 | b13 | b12 | … | b1 | b0 | b-1 | b-2 | b-3 | … | b-14 | b-15 | b-16
sign
15 bits
Fixed position e.g. middle
16 bits
( 10.011 )2
0 | 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 | 0 1 1 0 0 0 0 0 0 0 0 0 0 0 0

## Slide 17: Problems of Fixed Point
  Limited range and precision: e.g., 32 bits
  Largest number:
  Highest precision:
Rarely used (No built-in hardware support)
2-16
215 (011...111)2

## Slide 18: The idea
Limitation of fixed point notation:
  Represents evenly spaced fractional numbers
     hard tradeoff between high precision and high magnitude
How about un-even spacing between numbers?
-
+
0

## Slide 19: Floating Point: decimal
Based on exponential notation (aka normalized scientific notation)
r10 = +M * 10E, where 1 <= M < 10
M: significant (mantissa), E: exponent

## Slide 20: Floating Point: decimal
Example:
365.25 = 3.6525 * 102
0.0123 = 1.23 * 10-2
Decimal point floats to the position immediately
after the first nonzero digit.

## Slide 21: Floating Point: binary
Binary exponential representation
(5.5)10 = (101.1)2 = (1.011)2 * 22
r10 = +M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…bn )2
M: significant, E: exponent

## Slide 22: Floating Point
Binary exponential representation
(5.5)10 = (101.1)2 = (1.011)2 * 22
Normalization: give a number r, obtain its normalized representation
Normalized
representation
of r
r10 = +M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…bn )2
M: significant, E: exponent

## Slide 23: Exercises
The normalized representation of (10.25)10 is ?

## Slide 24: Exercises
The normalized representation of (10.25)10 is ?
(10.25)10 = (1010.01)2 = (1.01001)2 * 23

## Slide 25: Floating Point
Binary exponential representation
(5.5)10 = (101.1)2 = (1.011)2 * 22
How to represent a normalized number in a fixed-length format?
Normalized
representation
of r
r10 = +M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…bn )2
M: significant, E: exponent

## Slide 26: Normalized representation
s | exp (E) | sig (M)
31
30
23
22
0
( 1.b1b2b3…bn )2
r10 = +M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…bn )2
M: significant, E: exponent

## Slide 27: Normalized representation in computer
s | exp (E) | fraction (F)
31
30
23
22
0
( b1b2b3…b23 )2
r10 = +M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…b23 )2
M: significant, E: exponent

## Slide 28: Normalized representation
0 | 0000 0010 | 0110 0000 0000 0000 0000 000
31
30
23
22
0
(5.5)10 = (101.1)2 = (1.011)2 * 22
( b1b2b3…b23 )2
r10 = +M * 2E, where 1 <= M < 2
M = ( 1.b1b2b3…b23 )2
M: significant, E: exponent

## Slide 29: Exercise
Given the normalized representation of (71)10 and (10.25)10

## Slide 30: Exercise
Given the normalized representation of (71)10 and (10.25)10
0 | 0000 0110 | 0001 1100 0000 0000 0000 000
31
30
23
22
0
(71)10 = (1000111)2 = (1.000111)2 * 26
(10.25)10 = (1010.01)2 = (1.01001)2 * 23
0 | 0000 0011 | 0100 1000 0000 0000 0000 000
31
30
23
22
0

## Slide 31: Toy Number System
s | exp (E) | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
Largest positive number ?

## Slide 32: Toy Number System
s | exp (E) | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
Largest positive number ?
0 | 1 1 1 | 1 1
( 1.11 )2 * 27 = 224

## Slide 33: Toy Number System
s | exp (E) | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
Largest positive number: 224
Smallest positive number ?

## Slide 34: Toy Number System
s | exp (E) | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
Largest positive number: 224
Smallest positive number: 1
0 | 0 0 0 | 0 0
( 1.00 )2 * 20 = 1

## Slide 35: Toy Number System
s | exp (E) | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
Positive number: 1 to 224
Negative number: -224 to -1
No more bit patterns left to represent 0!

## Slide 36: Questions
How to represent
numbers close or equal to 0?
special cases:
  the result of dividing by 0, e.g. 1/0 ?
Lots of different implementations around 1950s!

## Slide 37: IEEE Floating Point Standard
Prof. William Kahan
University of California at Berkeley
Turing Award (1989)
IEEE p754
A standard for binary
floating point representation

## Slide 38: The Only Book Focuses On IEEE Floating Point Standard
https://cs.nyu.edu/overton/NumericalComputing/protected/NumericalComputingSIAM.pdf
With you nyu netid/password. You can also search the pdf with google.

## Slide 39: What we have learnt so far
normalized representation of floating point
0 | 0000 0010 | 0110 0000 0000 0000 0000 000
31
30
23
22
0
(5.5)10 = (101.1)2 = (1.011)2 * 22
how to represent numbers in range (-1,1)
how to represent special cases? e.g.
r10 = +M * 2E M = ( 1.b1b2b3…b23 )2

## Slide 40: Goals of IEEE Standard
Consistent representation of floating point numbers
Correctly rounded floating point operations, using several rounding modes.
Consistent treatment of exceptional situations such as division by zero

## Slide 41: Restrictions on Normalized Representation
r10 = +M * 2E M = ( 1.b0b1b2b3…bn )2
s | exp (E) | fraction (F)
31
30
23
22
0
( b0b1b2b3…bn )2
E can not be (1111 1111)2 or (0000 0000)0
Emax = ?
Emin = ?
254, (1111 1110)2
1, (0000 0001)2

## Slide 42: Exponential Bias
r10 = +M * 2E, M = ( 1.b0b1b2b3…bn )2
s | exp (E) + 127 | fraction (F)
31
30
23
22
0
( b0b1b2b3…bn )2
Bias: 127
To represent (-1,1), we must allow negative exponent.
How to represent negative E?
  2’s complement
  use bias

## Slide 43: IEEE normalized representation
r10 = +M * 2E, M = ( 1.b0b1b2b3…bn )2
s | exp (E) + 127 | fraction (F)
31
30
23
22
0
( b0b1b2b3…bn )2
Bias: 127
Emax = ?
Emin = ?
254 – 127 = 127
1 – 127 = -126
Smallest positive number: ?
Negative number with smallest absolute value: ?
2-126
-2-126

## Slide 44: Questions
Q1. Why using bias?
Q2. Why is bias 127?

## Slide 45: Questions
Q1. Why using bias instead of 2’s complement?
Answer: easier circuitry for comparison.
Notes: Circuitry for handling 2’s complement is more complex than handling unsigned only.
Although 2’s complement has the same addition/substraction logic as unsigned, its comparison logic is different.
(1000 0000) in 2’s complement is less than (0000 0001) but
(1000 0000) in unsigned is more than (0000 0001) but

## Slide 46: Questions
Q2. Why is bias 127?
A2. Balance positive numbers (magnitude) and negative numbers (precision)

## Slide 47: Example Toy Number System
s | exp (E) + 3 | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
bias: 3
Smallest positive number ?

## Slide 48: Toy Number System
s | exp (E) + 3 | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
bias: 3
Smallest positive number: 0.25
0 | 0 0 1 | 0 0
( 1.00 )2 * 2-2 = 0.25
Smallest number >0.25?
( 1.01 )2 * 2-2 = 0.25+0.0625

## Slide 49: Toy Number System
s | exp (E) + 3 | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
bias: 3
Chart: 
| 0.25 | 0.3125 | 0.375 | 0.4375 | 0.5 | 0.625 | 0.75 | 0.875 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.5 | 3 | 3.5 | 4 | 5 | 6 | 7 | 8 | 10 | 12 | 14 | -0.25 | -0.3125 | -0.375 | -0.4375 | -0.5 | -0.625 | -0.75 | -0.875 | -1 | -1.25 | -1.5 | -1.75 | -2 | -2.5 | -3 | -3.5 | -4 | -5 | -6 | -7 | -8 | -10 | -12 | -14
Normalized | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
?

## Slide 50
represent values which are
close and equal to 0

## Slide 51: IEEE denormalized representation
r10 = +M * 2E
s | exp (E) + 127 | fraction (F)
31
30
23
22
0
Normalized Encoding:
1 <= M < 2, M = ( 1.F )2
s | 0000 0000 | fraction (F)
31
30
23
22
0
Denormalized Encoding:
0 <= M < 1, M = ( 0.F )2
E = 1 – Bias = -126

## Slide 52: Zeros
0 | 0000 0000 | 0000 0000 0000 0000 0000 000
+0.0
1 | 0000 0000 | 0000 0000 0000 0000 0000 000
-0.0

## Slide 53: Examples
0 | 0000 0000 | 1000 0000 0000 0000 0000 000
(0.1)2 * 2-126
1 | 0000 0000 | 0101 0100 0000 0000 0000 000
-(0.010101)2 * 2-126

## Slide 54: What we’ve learnt last time
r10 = +M * 2E
s | E = unsigned field – Bias(127) | fraction (F)
31
30
23
22
0
Normalized Encoding:
1 <= M < 2, M = ( 1.F )2
s | 0000 0000 | fraction (F)
31
30
23
22
0
Denormalized Encoding:
0 <= M < 1, M = ( 0.F )2
E = 1 – Bias = -126

## Slide 55: Toy Number System
s | exp (E) bias=3 | frac (F)
5
4
2
1
0
6-bit floating point representation
exponent: 3 bits
fraction: 2 bits
bias: 3

## Slide 56: Toy Number System
s | exp (E) bias=3 | frac (F)
5
4
2
1
0
∞
-∞
0
000000
100000
What’s the next closest #?
Denormalized vs. normalized?
How many?

## Slide 57: Toy Number System
s | exp (E) bias=3 | frac (F)
5
4
2
1
0
∞
-∞
0
000000
100000
000001
000010
000011
What type is the next number?
All denormalized # have equal spacing

## Slide 58: Toy Number System
s | exp (E) bias=3 | frac (F)
5
4
2
1
0
∞
-∞
0
000000
100000
000001
000010
000011
000100
000101
000110
000111

## Slide 59: Toy Number System
s | exp (E) bias=3 | frac (F)
5
4
2
1
0
∞
-∞
0
000000
100000
000001
000010
000011
000100
000101
000110
000111
001000
001001
001010
001011

## Slide 60: Special Values
s | 1111 1111 | fraction (F)
31
30
23
22
0
Special Value’s Encoding:
values | sign | frac
+ | 0 | all zeros
- | 1 | all zeros
NaN | any | non-zero

## Slide 61: Exercises
representation | E | M | V
0100 1001 0101 0000 0000 0000 0000 0000 |  |  | 
 |  |  | 2.5 * 2-127
 |  |  | -1.25 * 2-111
1111 1111 1111 1111 0000 0000 0000 0000 |  |  | 
1111 1111 1000 0000 0000 0000 0000 0000 |  |  | 
 |  |  | 1.5 * 2-127

## Slide 62: Exercises
representation | E | M | V
0100 1001 0101 0000 0000 0000 0000 0000 | 146 – 127 = 19 | (1.101)2 = 1.625 | 1.625 * 219
0000 0000 1010 0000 0000 0000 0000 0000 | 1 – 127 = -126 | (1.01)2 = 1.25 | 2.5 * 2-127 = (1.01)2 * 2-126
1000 1000 0010 0000 0000 0000 0000 0000 | 16 – 127 = -111 | (1.01)2 = 1.125 | -1.25 * 2-111
1111 1111 1111 1111 0000 0000 0000 0000 | - | - | Nan
1111 1111 1000 0000 0000 0000 0000 0000 | - | - | -
0000 0000 0110 0000 0000 0000 0000 0000 | -126 | (0.11)2 | (0.11)2 * 2-126 = 1.5 * 2-127

## Slide 63: Distribution of Representable Values
NaN
NaN
+

0
+Denorm
+Normalized
-Denorm
-Normalized
+0

## Slide 64: Distribution of Representable Values
NaN
NaN
+

0
+Denorm
+Normalized
-Denorm
-Normalized
+0
  What if the result of computation is at ?

## Slide 65: Rounding
Goal
  Use the “closest” representable value x’ to represent x.
Round modes
  Round-down
  Round-up
  Round-toward-zero
  Round-to-nearest (Round to even in text book)

## Slide 66: Round down
-0.875
-0.75
0.5
0.625
Round(-0.86) = ?
Round(0.55) = ?
Round(x) = x- (x-<= x)

## Slide 67: Round down
-0.875
-0.75
0.5
0.625
Round(-0.86) = -0.875
Round(x) = x- (x-<= x)
Round(0.55) = 0.5

## Slide 68: Round up
Round(x) = x+ (x+>= x)

## Slide 69: Round up
-0.875
-0.75
0.5
0.625
Round(-0.86) = ?
Round(0.55) = ?
Round(x) = x+ (x+>= x)

## Slide 70: Round up
-0.875
-0.75
0.5
0.625
Round(-0.86) = -0.75
Round(0.55) = 0.625
Round(x) = x+ (x+>= x)

## Slide 71: Round towards zero
Round(x) = x+ if x < 0
Round(x) = x- if x > 0

## Slide 72: Round towards zero
-0.875
-0.75
0.5
0.625
Round(x) = x+ if x < 0
Round(x) = x- if x > 0
Round(-0.86) = ?
Round(0.55) = ?

## Slide 73: Round towards zero
-0.875
-0.75
0.5
0.625
Round(-0.86) = -0.75
Round(x) = x+ if x < 0
Round(x) = x- if x > 0
Round(0.55) = 0.5

## Slide 74: Round to nearest
Round(x) either x+ or x- , whichever is nearer to x.

## Slide 75: Round to nearest
Round(x) either x+ or x- , whichever is nearer to x.
-0.875
-0.75
0.5
0.625
Round(-0.86) = ?
Round(0.55) = ?

## Slide 76: Round to nearest
Round(x) either x+ or x- , whichever is nearer to x.
-0.875
-0.75
0.5
0.625
Round(-0.86) = -0.875
Round(0.55) = 0.5

## Slide 77: Round to nearest; ties to even
Round(x) either x+ or x- , whichever is nearer to x.
-0.875
-0.75
0.5
0.625
Round(-0.86) = -0.875
Round(0.55) = 0.5
In case of a tie, the one with its least significant bit equal to zero is chosen.

## Slide 78: single/ double precision
s | E + 127 | frac
31
30
23
22
0
single precision (32 bits)
s | E + 1023 | frac
63
62
52
51
0
double precision (64 bits)
float f = 0.1
double d = 0.1

## Slide 79: single/ double precision
 | Emin | Emax | Nmin | Nmax
Float | -126 | 127 | ≈ 2-126 | ≈ 2128
Double | -1022 | 1023 | ≈ 2-1022 | ≈ 21024

## Slide 80: How does CPU know if it is floating point or integers ?
By having specific instruction for floating points operation.

## Slide 81
CPU
decoder
Memory
……
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
add $1, $2
IU
FPU
int d = 1 + 2

## Slide 82
CPU
decoder
Memory
……
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
addss $1, $2
IU
FPU
float f = 0.1 + 0.2

## Slide 83: Floating point operations
Addition, subtraction, multiplication, division etc.
FP Caveats:
  Invalid operation: 0/0, sqrt(-1), +
  Divide by zero: x/0
  Overflows: result too big to fit
  Underflows: 0 < result < smallest denormalized value
  Inexact: round it!

## Slide 84: Why divide by zero = ?
Allow a calculation to continue and produce a valid result
Example:
If R1 or R2 is 0, overall resistance should be 0

## Slide 85: Floating point addition
Commutative? x+y == y+x?
Associative? (x+y)+z = x + (y+z)?
  Rounding:
  (3.14+1e10)-1e10 = 0
  3.14+(1e10-1e10) = 3.14
  Overflow
Every number has an additive inverse?
  Yes except for  and NaN

## Slide 86: Floating point multiplication
Commutative? x* y == y*x?
Associative? (x*y)*z = x * (y*z)?
  Overflow:
  (1e20*1e20)*1e-20= inf, 1e20*(1e20*1e-20)= 1e20
  Rounding
(x+y)*z = x*z + y*z?
  1e20*(1e20-1e20)= 0.0, 1e20*1e20 – 1e20*1e20 = NaN

## Slide 87: Floating point in real world
Storing time in computer games as a FP?
Precision diminishes as time gets bigger
FP value | Time value | FP precision | Time precision
1 | 1 sec | 1.19E-07 | 119 nanoseconds
100 | ~1.5 min | 7.63E-06 | 7.63 microseconds
10 000 | ~3 hours | 0.000977 | .976 milliseconds
1000 000 | ~11 days | 0.0625 | 62.5 milliseconds

## Slide 88: Floating point in the real world
Using floating point to measure distances
FP value | Length | FP precision | Precision size
1 | 1 meter | 1.19E-07 | Virus
100 | 100 meter | 7.63E-06 | red blood cell
10 000 | 10 km | 0.000977 | toenail thickness
1000 000 | .16x earth radius | 0.0625 | credit card width
Table source: Random ASCII

## Slide 89: Floating point trouble
Comparing floats for equality is a bad idea!
float f = 0.1;
while (f != 1.0) {
f += 0.1;
}
Notes: You can not represent 0.1 exactly in floating point

## Slide 90: Floating point trouble
Never count using floating points
count = 0;
for (float f = 0.0; f < 1.0; f += 0.1) {
count++;
}
Notes: You can not represent 0.1 exactly in floating point

## Slide 91: Floating point summary
Floating points are tricky
  Precision diminishes as magnitude grows
  overflow, rounding error
Many real world disasters due to FP trickiness
  Patriot Missile failed to intercept due to rounding error (1991)
  Ariane 5 explosion due to overflow in converting from double to int (1996)