## Slide 1: Isolation & Virtual Memory
Jinyang Li

## Slide 2: Layered organization
Hardware
CPU
Memory
I/O
Operating System
User Applications
Software
Goal: Isolation -- failure of one running program must not affect another

## Slide 3: Isolation
Process
Process
Hardware
CPU
Memory
I/O
Operating System
User Applications
Software
Isolation is provided by OS using special hardware primitives
Process
Process
The unit of isolation

## Slide 4: Process
What is a process?
  An instance of a running program
Program vs. Process
  Program: a passive collection of instructions
  Process: the actual execution of those instructions
OS assigns different processes different process id
  getpid() system call returns id of current process
  Command ps lists all processes, kill terminates a process

## Slide 5: Isolation
Process
Hardware
CPU
Memory
I/O
Operating System
User Applications
Software
Upon program startup, OS creates a process. Process asks for OS services through system calls (getpid, read, write).
The unit of isolation
Process
Process
Process
Operating System
create
system call
/services
Syscalls are listed in manual section 2
type “man 2 getpid”

## Slide 6: Our simplified “Mental Model” of program execution
CPU
0x00…0058
PC:
IR:
movq (%rax), %rbx
RAX:
0x38
0x1
…
RBX:
Memory
0x1
……
0x0…058
0x0…050
0x0…010
0x0…018
0x0…020
0x0…028
0x0…030
0x0…038
0x0…040
0x0…048
...
addr: 0x38
data: 0x1
Question: how does a CPU execute >1 programs “simultaneously”?

## Slide 7: Sharing CPU: time multiplexing
CPU
0xfe…0058
PC:
IR:
movq (%rax), %rbx
RAX:
0xee..0038
0x1
…
RBX:
Memory
...
……
1. OS assigns different processes different memory regions

## Slide 8: Sharing CPU: time multiplexing
CPU
PC:
IR:
RAX:
…
RBX:
Memory
...
……
2. OS saves/restores CPU state in memory to switch
execution of one process to another every ~10ms
saved CPU state
0xfe…0058
movq (%rax), %rbx
0xee..0038
0x1

## Slide 9: Sharing CPU: time multiplexing
CPU
PC:
IR:
RAX:
…
RBX:
Memory
...
……
2. OS saves/restores CPU state in memory to switch
execution of one process to another every ~10ms
saved CPU state
saved CPU state
0x00…0028
mov %rax, (%rbx)
0x2
0x00..1234

## Slide 10: Sharing CPU: time multiplexing
CPU
PC:
IR:
RAX:
…
RBX:
Memory
...
……
Challenge: how to prevent a process from reading/writing
another process’s memory?!
saved CPU state
saved CPU state
0x00…0028
mov %rax, (%rbx)
0x2
0x00..1234

## Slide 11: Processes need to share memory safely
(Simplicity) Processes are loaded at the same addresses
  e.g. Linker/loader can handle different processes with the same code
(Isolation) One process cannot access another process’ memory
  Process X cannot overwrite data in process Y
  Process X cannot peek sensitive data in process Y
How?
  Virtual Memory

## Slide 12: Hardware solution: Virtual addressing
CPU
0x00…0058
PC:
IR:
movq (%rax), %rbx
RAX:
0x38
0x1
…
RBX:
Memory
0x1
……
0x0…058
0x0…050
0x0…010
0x0…018
0x0…020
0x0…028
0x0…030
0x0…038
0x0…040
0x0…048
...
Virtual address
data: 0x1
MMU
0x38
Memory Management Unit
Physical address
0x10

## Slide 13: Address Translation – Strawman
CPU
0x00…0058
PC:
IR:
movq (%rax), %rbx
RAX:
0x38
0x1
…
RBX:
Memory
0x1
……
0x0…058
0x0…050
0x0…010
0x0…018
0x0…020
0x0…028
0x0…030
0x0…038
0x0…040
0x0…048
...
Virtual address
data: 0x1
MMU
0x38
Memory Management Unit
Physical address
0x10
Provide MMU with a mapping table at byte granularity
Map each virtual address into a physical address
Virtual address | Physical address
… | …
0x58 | 0x10
0x59 | 0x11
… | …
mapping table
Question: What is the size of mapping table?
For 64-bit address, size is 264

## Slide 14: Address Translation – Page
Problem: Mapping table too big
Solution: map at a coarser granularity
  Divide memory into fixed-size pages.
  Page table: map virtual pages to physical pages.

## Slide 15: Paging example: 4-bit address
4-bit virtual and physical addresses
4-byte page size
Question: for 32-bit address, 4KB page size,
how many pages?
Answer: 232/212=220 pages
0000
1111

## Slide 16: Paging example: 4-bit address
Not all virtual pages are used
  On 64-bit machine, vast majority of virtual pages are unused
0000
process 1’s address space
process 2’s address space
0100
1000
1100
physical memory
0000
0100
1000
1100
0000
0100
1000
1100

## Slide 17: Paging example: 4-bit address
What does the mapping table look like?
process 2’s address space
physical memory
0000
0100
1000
1100
Virtual Page | Physical Page
0000 | 1100
0100 | --
1000 | --
1100 | 0100
Can we eliminate this column?
mapping for process 2:
0000
0100
1000
1100

## Slide 18: Paging example: 4-bit address
What does the mapping table look like?
  An array of integers (Page Table Entry, PTE)
0x0
process 2’s address space
0x4
0x8
0xc
physical memory
0x0
0x4
0x8
0xc
1100
--
--
0100
0
1
2
3
index of array is
virtual page number
PTE is physical page number
For 2x page size, PTE’s least
significant x bits can be
used for other purposes
e.g. indicate PTE validity
1101
0000
0000
0101

## Slide 19: Paging example: 4-bit address
How to translate from virtual to physical address?
physical memory
0x0
0x4
0x8
0xc
1101
0000
0000
0101
CPU
Virtual Address
MMU
1110
Memory Management Unit
page table of p2
Physical Address
???

## Slide 20: Paging example: 4-bit address
How to translate from virtual to physical address?
physical memory
0x0
0x4
0x8
0xc
1101
0000
0000
0101
CPU
Virtual Address
MMU
1110
Memory Management Unit
Physical Address
???
virtual page
number
0100
page table of p2

## Slide 21: Paging example: 4-bit address
How to translate from virtual to physical address?
physical memory
0x0
0x4
0x8
0xc
1101
0000
0000
0101
CPU
Virtual Address
MMU
1110
Memory Management Unit
Physical Address
???
offset within a
page
0100
+
10
physical address
0110
page table of p2

## Slide 22: Each process has its own page table
physical memory
0x0
0x4
0x8
0xc
1101
0000
0000
0101
CPU
Virtual Address
MMU
1110
Memory Management Unit
Physical Address
0110
page table of p2
OS switches CPU to execute p1 instead of p2
1001
0000
0000
0001
page table of p1
CPU
0010

## Slide 23: Recap: Linux address space
0x00007ffffffff000
0x0000000000000000
s1[10000000]
Stack
Text
read-write data
Heap
0x0000000000400000
8MB
default
limit
Shared
Libraries
read-only data
What is this address?

## Slide 24: Address Translation: 32-bit address
Page size: 4 KB (212)
How many virtual pages?
How many bits for virtual page number (VPN)?
How many bits for page offset?
Virtual page number (VPN)
Page offset (VPO)
31
12
11
0
32-bit virtual address

## Slide 25: Address Translation: 32-bit address
Page size: 4 KB (212)
What’s the size of each PTE?
PTE :
P
W
S
present?
writable?
accessible by
OS only?
...
Physical Page #
4-byte PTE

## Slide 26: Address Translation: 32-bit address
Page size: 4 KB (212)
How many PTEs in the page table?
What’s the size of page table?
232/212 = 220
220*2 = 4MB

## Slide 27: Address Translation: 64-bit address
Page size: 4 KB (212)
How many virtual pages?
How many bits for virtual page number (VPN)?
How many bits for page offset?
Virtual page number (VPN)
Page offset (VPO)
63
12
11
0
64-bit virtual address

## Slide 28: Address Translation: 64-bit address
Page size: 4 KB (212)
What’s the size of each PTE?
How many PTEs in the page table?
264/212 = 252
4 Petabyte!!
Possible solution: Enlarge page size? e.g. 256MB (228) page size

## Slide 29: This lecture
Multi-level page tables
Demand paging
Accelerating address translation

## Slide 30: Multi-level page tables
Problem with 1-level page table:
For 64-bit address space and 4KB page size, page table is much too large
number of bytes addressable in 64-bit address space
page size
# of pages in 64-bit address space
= # of page table entries required

## Slide 31: Multi-level page tables
Problem
how to reduce # of page table entries required?
Solution
Multi-level page table
  A tree of “page tables”

## Slide 32: 2-level Paging Example
6-bit virtual and physical address, 4-byte page

## Slide 33: 2-level Paging Example
6-bit virtual and physical address, 4-byte page
1-level page table
Suppose a process has only two 2 mapped virtual pages
110001
000000
...
000000
010001
24 PTEs
1-level Page Table

## Slide 34: 2-level Paging Example
6-bit virtual and physical address, 4-byte page
2-level page table
Suppose a process has only two 2 mapped virtual pages
110001
000000
...
000000
010001
24 PTEs
1-level Page Table
110001
000000
000000
010001
22 L0
PTEs
110001
000000
000000
010001
110001
000000
000000
010001
010000
is physical
address of L1
page table
22 L1
PTEs

## Slide 35: 2-level Paging Example
110001
000000
...
000000
010001
1-level Page Table
1 1 1 1
10
Virtual
Page #
Page
offset
Index to
page table
how to perform address translation?
  1-level page table

## Slide 36: 2-level Paging Example
how to perform address translation?
  2-level page table
110001
000000
...
000000
010001
1-level Page Table
011001
000000
000000
110101
110001
000000
000000
010000
000000
000000
000000
010001
1 1 1 1
10
Page
offset
Index to
page table
1 1
10
Index to
L0 table
Page
offset
1 1
Index to
L1 table

## Slide 37: X86_64 supports 4-level page table
Virtual Address
63
0
MMU
Virtual Address
Offset
…
…
…
…
…
…
…
…
…
Entry at level i has the physical address of the page
PPN
Physical address
Level 0
Level 1
Level 2
Level 3

## Slide 38: Multi-level page tables on X86_64
63
0
48
47
39
38
30
29
21
20
Reserved
L0 Offset
L1 Offset
L2 Offset
Page Offset
L3 Offset
12
11
…
…
…
…
…
…
…
…
…
Level 0
Level 1
Level 2
Level 3
Current mapping uses 48 bits,
programs can address 248 bytes, i.e.
~256 TB
4-level page table
2^9 entries
9-bit offset

## Slide 39: Multi-level page tables on X86_64
63
0
…
…
…
…
…
…
…
…
…
Level 0
Level 1
Level 2
Level 3
48
47
39
38
30
29
21
20
Reserved
L0 Offset
L1 Offset
L2 Offset
Page Offset
L3 Offset
12
11
CPU Register: CR3
Root Addr
4-level page table

## Slide 40: Multi-level page tables on X86_64
63
0
…
…
…
…
…
…
…
…
…
Level 0
Level 1
Level 2
Level 3
48
47
39
38
30
29
21
20
Reserved
L0 Offset
L1 Offset
L2 Offset
Page Offset
L3 Offset
12
11
CPU Register: CR3
Root Addr
4-level page table

## Slide 41: Multi-level page tables on X86_64
63
0
Level 0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
CPU Register: CR3
Virtual Address: 0x80801fffa8
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
0x3466001
0x3467001
0x3468001
unused
…
Physical address
of the 1st entry at
level 1
4-level page table

## Slide 42: Multi-level page tables on X86_64
Virtual Address: 0x80801fffa8
63
0
Level 0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
CPU Register: CR3
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
0x3466001
0x3467001
0x3468001
unused
…
Physical address
of the 1st entry at
level 1
4-level page table

## Slide 43: Multi-level page tables on X86_64
63
0
Level 0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
CPU Register: CR3
Virtual Address: 0x80801fffa8
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
0x3466001
0x3467001
0x3468001
unused
…
Level 1
0x3587001
unused
0x3588001
unused
…
Physical address
of the 1st entry at
level 1
Physical address
of the 1st entry at
level 2
4-level page table

## Slide 44: Multi-level page tables on X86_64
Virtual Address: 0x80801fffa8
63
0
Level 0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
CPU Register: CR3
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
0x3466001
0x3467001
0x3468001
unused
…
Level 1
0x3587001
unused
0x3588001
unused
…
Physical address
of the 1st entry at
level 1
Physical address
of the 1st entry at
level 2
4-level page table

## Slide 45: Multi-level page tables on X86_64
63
0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
CPU Register: CR3
Virtual Address: 0x80801fffa8
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
Level 1
Physical address
of the 1st entry at
level 1
Physical address
of the 1st entry at
level 2
Level 2
0x3678001
0x3579001
unused
unused
…
Physical address
of the 1st entry at
level 3
4-level page table
Level 0
0x3466001
0x3467001
0x3468001
unused
…
0x3587001
unused
0x3588001
unused
…

## Slide 46: Multi-level page tables on X86_64
Virtual Address: 0x80801fffa8
63
0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
CPU Register: CR3
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
Physical address
of the 1st entry at
level 2
Level 2
Physical address
of the 1st entry at
level 3
4-level page table
Level 1
Physical address
of the 1st entry at
level 1
0x3678001
0x3579001
unused
unused
…
Level 0
0x3466001
0x3467001
0x3468001
unused
…
0x3587001
unused
0x3588001
unused
…

## Slide 47: Multi-level page tables on X86_64
63
0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
CPU Register: CR3
Virtual Address: 0x80801fffa8
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
Physical address
of the 1st entry at
level 2
Level 2
Physical address
of the 1st entry at
level 3
Level 3
0x5788001
0x5789001
0x578a001
0x5799001
…
Physical address
of the page
4-level page table
Level 1
Physical address
of the 1st entry at
level 1
0x3678001
0x3579001
unused
unused
…
Level 0
0x3466001
0x3467001
0x3468001
unused
…
0x3587001
unused
0x3588001
unused
…

## Slide 48: Multi-level page tables on X86_64
63
0
48
47
39
38
30
29
21
20
0x0
0x1
0x2
0x0
0xfa8
0x1ff
12
11
CPU Register: CR3
Virtual Address: 0x80801fffa8
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
0x4ffff000
Physical address
of the 1st entry at
level 0
Physical address
of the 1st entry at
level 2
Level 2
Physical address
of the 1st entry at
level 3
Level 3
0x5788001
0x5789001
0x578a001
0x5799001
…
Physical address
of the page
4-level page table
Level 1
Physical address
of the 1st entry at
level 1
0x3678001
0x3579001
unused
unused
…
Level 0
0x3466001
0x3467001
0x3468001
unused
…
0x3587001
unused
0x3588001
unused
…
Physical Address: 0x5799fa8

## Slide 49: Review Virtual Address
How can each process have the same virtual address space?
  OS sets up a separate page table for each process
  When executing a process p, MMU uses p’s page table to do address translation.

## Slide 50: Virtual Address Space For Each Process
Main memory
...
PP 0
PP 1
PP 2
PP k-2
Virtual Address Space for Process 1:
Virtual memory
vaddr1
vaddr2
vaddr3
…
…
…
…
…
…
…
…
…
…
Level 0
Level 1
Level 2
Level 3
Page Table 1
Virtual Address Space for Process 2:
Virtual memory
vaddr1
vaddr2
vaddr3
…
…
…
…
…
…
…
…
…
…
Level 0
Level 1
Level 2
Level 3
Page Table 2
PP k-1
PP k

## Slide 51: Demand Paging
Memory Allocation (e.g., p = sbrk(8192))
User program to OS:
Declare a virtual address range from p to p + 8192 for use by the current process.
OS’ actions:
Allocate the physical page and populate the page table.

## Slide 52: Demand Paging
char *p = (char *)sbrk(8192); // p is 0x80801fffa8
p[0] = ‘c’
p[4096] = ‘s’
Level 0
CPU Register: CR3
0x4ffff000
0x3466001
unused
unused
unused
…
…
current process’ page table
0x0
0x1
0x2
0x0
0xfa8
0x1ff
63
0
48
47
39
38
30
29
21
20
12
11
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
OS adds [0x80801fffa8, 0x80801fffa8+8192) to the process’ virtual address info

## Slide 53: Demand Paging
char *p = (char *)sbrk(8192); // p is 0x80801fffa8
p[0] = ‘c’
p[4096] = ‘s’
Level 0
CPU Register: CR3
0x4ffff000
0x3466001
unused
unused
unused
…
…
current process’ page table
0x0
0x1
0x2
0x0
0xfa8
0x1ff
63
0
48
47
39
38
30
29
21
20
12
11
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
OS adds [0x80801fffa8, 0x80801fffa8+8192) to the process’ virtual address info
MMU tells OS entry 1 is missing in the page at level 0. (Page fault)

## Slide 54: Demand Paging
char *p = (char *)malloc(8192); // p is 0x80801fffa8
p[0] = ‘c’
p[4096] = ‘s’
Level 0
CPU Register: CR3
0x4ffff000
0x3466001
0x3668001
unused
unused
…
…
current process’ page table
0x0
0x1
0x2
0x0
0xfa8
0x1ff
63
0
48
47
39
38
30
29
21
20
12
11
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
OS adds [0x80801fffa8, 0x80801fffa8+8192) to the process’ virtual address info
MMU tells OS entry 1 is missing in the page at level 0. (Page fault)
OS constructs the mapping for the address. (Page fault handler)

## Slide 55: Demand Paging
0. (Page fault)
OS constructs the mapping for the address. (Page fault handler)
OS constructs the mapping for the address. (Page fault handler)
char *p = (char *)sbrk(8192); // p is 0x80801fffa8
p[0] = ‘c’
p[4096] = ‘s’
Level 0
CPU Register: CR3
0x4ffff000
...
0x3668001
unused
unused
…
current process’ page table
0x0
0x1
0x2
0x0
0xfa8
0x1ff
63
0
48
47
39
38
30
29
21
20
12
11
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
Level 1
unused
unused
0x3588001
unused
…
Level 2
0x3678001
unused
unused
unused
…
Level 3
unused
…
0x5799001
unused
unused
New pages allocated by OS
Physical Page
...
....
…
...
...

## Slide 56: Demand Paging
OS adds [p, p+8192) to the process’ virtual address info
MMU tells OS entry 1 is missing in the page at level 0. (Page fault)
OS constructs the mapping for the address. (Page fault handler)
OS tells the CPU to resume execution
char *p = (char *)sbrk(8192); // p is 0x80801fffa8
p[0] = ‘c’
p[4096] = ‘s’
Level 0
CPU Register: CR3
0x4ffff000
...
0x3668001
unused
unused
…
current process’ page table
0x0
0x1
0x2
0x0
0xfa8
0x1ff
63
0
48
47
39
38
30
29
21
20
12
11
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
Level 1
unused
unused
0x3588001
unused
…
Level 2
0x3678001
unused
unused
unused
…
Level 3
unused
…
0x5799001
unused
unused
Physical Page
...
...
…
...
...

## Slide 57: Demand Paging
OS adds [p, p+8192) to the process’ virtual address info
MMU tells OS entry 1 is missing in the page at level 0. (Page fault)
OS constructs the mapping for the address. (Page fault handler)
5. MMU translates address again and access the physical memory.
char *p = (char *)sbrk(8192); // p is 0x80801fffa8
p[0] = ‘c’
p[4096] = ‘s’
Level 0
CPU Register: CR3
0x4ffff000
...
0x3668001
unused
unused
…
current process’ page table
0x0
0x1
0x2
0x0
0xfa8
0x1ff
63
0
48
47
39
38
30
29
21
20
12
11
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
Level 1
unused
unused
0x3588001
unused
…
Level 2
0x3678001
unused
unused
unused
…
Level 3
unused
…
0x5799001
unused
unused
Physical Page
...
...
…
...
‘c’

## Slide 58: Demand Paging
MMU tells OS entry 0x200 is missing in the page at level 3. (Page fault)
char *p = (char *)sbrk(8192); // p is 0x80801fffa8
p[0] = ‘c’
p[4096] = ‘s’ //0x8080200fa8
Level 0
CPU Register: CR3
0x4ffff000
...
0x3668001
unused
unused
…
current process’ page table
0x0
0x1
0x2
0x0
0xfa8
0x200
63
0
48
47
39
38
30
29
21
20
12
11
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
Level 1
unused
unused
0x3588001
unused
…
Level 2
0x3678001
unused
unused
unused
…
Level 3
unused
…
0x5799001
unused
unused
Physical Page
...
...
…
...
‘c’

## Slide 59: Demand Paging
OS constructs the mapping for the address. (Page fault handler)
char *p = (char *)sbrk(8192); // p is 0x80801fffa8
p[0] = ‘c’
p[4096] = ‘s’ //0x8080200fa8
Level 0
CPU Register: CR3
0x4ffff000
...
0x3668001
unused
unused
…
current process’ page table
0x0
0x1
0x2
0x0
0xfa8
0x200
63
0
48
47
39
38
30
29
21
20
12
11
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
Level 1
unused
unused
0x3588001
unused
…
Level 2
0x3678001
unused
unused
unused
…
Level 3
unused
…
0x5799001
unused
0x579a001
...
...
…
...
‘c’
Physical Pages
...
...
…
...
...

## Slide 60: Demand Paging
3. OS tells the CPU to resume
execution
char *p = (char *)sbrk(8192); // p is 0x80801fffa8
p[0] = ‘c’
p[4096] = ‘s’ //0x8080200fa8
Level 0
CPU Register: CR3
0x4ffff000
...
0x3668001
unused
unused
…
current process’ page table
0x0
0x1
0x2
0x0
0xfa8
0x200
63
0
48
47
39
38
30
29
21
20
12
11
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
Level 1
unused
unused
0x3588001
unused
…
Level 2
0x3678001
unused
unused
unused
…
Level 3
unused
…
0x5799001
unused
0x579a001
...
...
…
...
‘c’
Physical Pages
...
...
…
...
...

## Slide 61: Demand Paging
4. MMU translates the address again and access the physical memory.
char *p = (char *)sbrk(8192); // p is 0x80801fffa8
p[0] = ‘c’
p[4096] = ‘s’ //0x8080200fa8
Level 0
CPU Register: CR3
0x4ffff000
...
0x3668001
unused
unused
…
current process’ page table
0x0
0x1
0x2
0x0
0xfa8
0x200
63
0
48
47
39
38
30
29
21
20
12
11
L0 Offset
Reserved
L1 Offset
L2 Offset
L3 Offset
Page Offset
Level 1
unused
unused
0x3588001
unused
…
Level 2
0x3678001
unused
unused
unused
…
Level 3
unused
…
0x5799001
unused
0x579a001
...
...
…
...
‘c’
Physical Pages
...
...
…
...
‘s’

## Slide 62: Questions
What is the minimal page table size on 64 bit machine?
Given the minimal page table, how many physical pages it can refer to?
4 pages
page size
size of each page table entry

## Slide 63: Understanding Seg Fault
Where does segmentation fault come from?
Address translation fails due to 2 reasons
  MMU reads a missing page table entry (PTE)
    PTE’s present bit is unset
  MMU reads a PTE with wrong permission for the access
    write bit is unset for a write access
    OS bit is set for user program access
MMU generates “page fault”, to be handled by OS
OS either fixes the problem (e.g. demand paging) or aborts process with “segmentation fault”

## Slide 64: Memory Access Cost
Memory access latency
  100 ns
  160 ~ 200 CPU cycles
Instructions that do not involve memory access can execute very quickly:
  Instructions per CPU cycle >= 1
Notes: https://people.eecs.berkeley.edu/~rcs/research/interactive_latency.html

## Slide 65: Address translation is potentially very costly
CPU
Virtual Address
MMU
0x1234
Memory Management Unit
access 0x1234
Physical Memory Space
(real memory space)
e.g. 4GB
…...
……
0x0…1000
0x0…1008
…….
…….
0x0…000
0x0…008
......
......
0x0…ffff
PP0
PP1
PP2
PP3
…
+
0x0…2000
0x0…2008
0x0…3000
0x0…3008
0x3234
…
…
…
…
…
…
…
…
…
Level 0
Level 1
Level 2
Level 3
Offset
CR0:
0xffff000
Virtual Address
0xffff000
To read data
with some virtual address,
how many memory accesses?
PPN
0x4000

## Slide 66: Address translation is potentially very costly
CPU
Virtual Address
MMU
0x1234
Memory Management Unit
access 0x1234
Physical Memory Space
(real memory space)
e.g. 4GB
…...
……
0x0…1000
0x0…1008
…….
…….
0x0…000
0x0…008
......
......
0x0…ffff
PP0
PP1
PP2
PP3
…
PPN
0x4000
+
0x0…2000
0x0…2008
0x0…3000
0x0…3008
0x3234
…
…
…
…
…
…
…
…
…
Level 0
Level 1
Level 2
Level 3
Offset
CR0:
0xffff000
Virtual Address
0xffff000
To read data
with some virtual address,
how many memory accesses?
4 page table accesses +
one data access = 5 total memory accesses.

## Slide 67: Speedup Address Translation
Translation lookaside buffer (TLB)
  Small cache in MMU
  Maps virtual page numbers to physical page numbers
CPU
VPN | PPN
VP0 | PP1
VP1 | PP3
unused | unused
unused | unused
TLB (4 Entries)
MMU
VA: 0x1234
Calculate VPN
  VPN = VA >> 12
Check TLB
  Index = VPN % 4
  Check if TLB[Index].VPN == VPN
  On TLB hit,
  PA = TLB[Index].PPN + Offset
  On TLB miss
    Go though page table to get PPN
    Buffer the result in TLB

## Slide 68: Speedup Address Translation
Translation lookaside buffer (TLB)
  Small cache in MMU
  Maps virtual page numbers to physical page numbers
CPU
VPN | PPN
VP0 | PP1
VP1 | PP3
unused | unused
unused | unused
TLB (4 Entries)
MMU
VA: 0x1234
Example:
VPN = 0x1234 >> 12 = 0x1
TLB_Index = 0x1 % 4 = 1
Check TLB[1].VPN which is VP1
On TLB hit, PA = 0x234 + PP3 = 0x3234
Calculate VPN
  VPN = VA >> 12
Check TLB
  Index = VPN % 4
  Check if TLB[Index].VPN == VPN
  On TLB hit,
  PA = TLB[Index].PPN + Offset
  On TLB miss
    Go though page table to get PPN
    Buffer the result in TLB

## Slide 69: Speedup Address Translation
Translation lookaside buffer (TLB)
  Small cache in MMU
  Maps virtual page numbers to physical page numbers
CPU
VPN | PPN
VP0 | PP1
VP1 | PP3
unused | unused
unused | unused
TLB (4 Entries)
MMU
VA: 0x2234
Example:
VPN = 0x2234 >> 12 = 0x2
TLB_Index = 0x2 % 4 = 2
Check TLB[2].VPN which is Empty
Go through the page table
Calculate VPN
  VPN = VA >> 12
Check TLB
  Index = VPN % 4
  Check if TLB[Index].VPN == VPN
  On TLB hit,
  PA = TLB[Index].PPN + Offset
  On TLB miss
    Go though page table to get PPN
    Buffer the result in TLB
…
…
…
…
…
…
…
…
…
Level 0
Level 1
Level 2
Level 3
Virtual Address
PP5

## Slide 70: Speedup Address Translation
Translation lookaside buffer (TLB)
  Small cache in MMU
  Maps virtual page numbers to physical page numbers
CPU
VPN | PPN
VP0 | PP1
VP1 | PP3
VP2 | PP5
unused | unused
TLB (4 Entries)
MMU
VA: 0x2234
Example:
VPN = 0x2234 >> 12 = 0x2
TLB_Index = 0x2 % 4 = 2
Check TLB[2].VPN which is Empty
Go through the page table
Buffer the result in TLB
Calculate VPN
  VPN = VA >> 12
Check TLB
  Index = VPN % 4
  Check if TLB[Index].VPN == VPN
  On TLB hit,
  PA = TLB[Index].PPN + Offset
  On TLB miss
    Go though page table to get PPN
    Buffer the result in TLB
…
…
…
…
…
…
…
…
…
Level 0
Level 1
Level 2
Level 3
Virtual Address
PP5

## Slide 71: Latency
Memory access
  Hundreds of CPU cycles
TLB access
  Only a couple of CPU cycles

## Slide 72: Summary
TLB Access
Hit ?
Yes
No
Walk Though
Page Table
PPN + Offset
Virtual Address
Physical Address

## Slide 73: More on TLBs

## Slide 74: Speedup Address Translation
CPU
VPN | PPN
unused | unused
unused | unused
unused | unused
unused | unused
TLB (4 Entries)
MMU
TLB:
access 0x1234, TLB Miss
Calculate VPN
  VPN = VA >> 12
Check TLB
  Index = VPN % 4
  Check if TLB[Index].VPN == VPN
  On TLB hit,
  PA = TLB[Index].PPN + Offset
  On TLB miss
    Go though page table to get PPN
    Buffer the result in TLB
access 0x1234
access 0x5234
access 0x1234
access 0x5234
Access pattern
Both 0x1234 and 0x5234 go to the entry 1

## Slide 75: Speedup Address Translation
CPU
VPN | PPN
unused | unused
VP1 | PP3
unused | unused
unused | unused
TLB (4 Entries)
MMU
Calculate VPN
  VPN = VA >> 12
Check TLB
  Index = VPN % 4
  Check if TLB[Index].VPN == VPN
  On TLB hit,
  PA = TLB[Index].PPN + Offset
  On TLB miss
    Go though page table to get PPN
    Buffer the result in TLB
access 0x1234
access 0x5234
access 0x1234
access 0x5234
Access pattern
TLB:
access 0x1234, TLB Miss, cache VP1<->PP3
Both 0x1234 and 0x5234 go to the entry 1

## Slide 76: Speedup Address Translation
CPU
VPN | PPN
unused | unused
VP5 | PP8
unused | unused
unused | unused
TLB (4 Entries)
MMU
Calculate VPN
  VPN = VA >> 12
Check TLB
  Index = VPN % 4
  Check if TLB[Index].VPN == VPN
  On TLB hit,
  PA = TLB[Index].PPN + Offset
  On TLB miss
    Go though page table to get PPN
    Buffer the result in TLB
access 0x1234
access 0x5234
access 0x1234
access 0x5234
Access pattern
TLB:
access 0x1234, TLB Miss, cache VP1<->PP3
access 0x5234, TLB Miss, evict VP1<->PP3, cache VP5<->PP8
Both 0x1234 and 0x5234 go to the entry 1

## Slide 77: Speedup Address Translation
CPU
VPN | PPN
unused | unused
VP1 | PP3
unused | unused
unused | unused
TLB (4 Entries)
MMU
Calculate VPN
  VPN = VA >> 12
Check TLB
  Index = VPN % 4
  Check if TLB[Index].VPN == VPN
  On TLB hit,
  PA = TLB[Index].PPN + Offset
  On TLB miss
    Go though page table to get PPN
    Buffer the result in TLB
access 0x1234
access 0x5234
access 0x1234
access 0x5234
Access pattern
TLB:
access 0x1234, TLB Miss, cache VP1<->PP3
access 0x5234, TLB Miss, evict VP1<->PP3, cache VP5<->PP8
access 0x1234, TLB Miss, evict VP5<->PP8, cache VP1<->PP3
Both 0x1234 and 0x5234 go to the entry 1

## Slide 78: Speedup Address Translation
CPU
VPN | PPN
unused | unused
VP5 | PP8
unused | unused
unused | unused
TLB (4 Entries)
MMU
Calculate VPN
  VPN = VA >> 12
Check TLB
  Index = VPN % 4
  Check if TLB[Index].VPN == VPN
  On TLB hit,
  PA = TLB[Index].PPN + Offset
  On TLB miss
    Go though page table to get PPN
    Buffer the result in TLB
access 0x1234
access 0x5234
access 0x1234
access 0x5234
Access pattern
TLB:
access 0x1234, TLB Miss, cache VP1<->PP3
access 0x5234, TLB Miss, evict VP1<->PP3, cache VP5<->PP8
access 0x1234, TLB Miss, evict VP5<->PP8, cache VP1<->PP3
access 0x5234, TLB Miss, evict VP5<->PP8, cache VP1<->PP3
TLB eviction due to conflict!
Both 0x1234 and 0x5234 go to the entry 1

## Slide 79: Speedup Address Translation
CPU
VPN | PPN
unused | unused
VP5 | PP8
unused | unused
unused | unused
TLB (4 Entries)
MMU
Calculate VPN
  VPN = VA >> 12
Check TLB
  Index = VPN % 4
  Check if TLB[Index].VPN == VPN
  On TLB hit,
  PA = TLB[Index].PPN + Offset
  On TLB miss
    Go though page table to get PPN
    Buffer the result in TLB
access 0x1234
access 0x5234
access 0x1234
access 0x5234
Access pattern
TLB:
access 0x1234, TLB Miss, cache VP1<->PP3
access 0x5234, TLB Miss, evict VP1<->PP3, cache VP5<->PP8
access 0x1234, TLB Miss, evict VP5<->PP8, cache VP1<->PP3
access 0x5234, TLB Miss, evict VP5<->PP8, cache VP1<->PP3
TLB eviction due to conflict!  Multi-set associative TLB
Both 0x1234 and 0x5234 go to the entry 1

## Slide 80: Multi-set associative TLB
TLB (16 sets, 4 way associative)
MMU
Set 0
Set 1
……
Set 15
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN

## Slide 81: Multi-set associative TLB
TLB (16 sets, 4 way associative)
MMU
Set 0
Set 1
……
Set 15
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
63
0
15
Tag
Page Offset
Set Index
12
11

## Slide 82: Multi-set associative TLB
TLB (16 sets, 4 way associative)
MMU
Set 0
Set 1
……
Set 15
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
63
0
15
Tag
Page Offset
Set Index
12
11

## Slide 83: Example
TLB (16 sets, 4 way associative)
MMU
Set 0
Set 1
……
Set 15
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
63
0
15
0x1
0x234
0x1
12
11
access 0x11234, TLB Miss
access 0x21234
access 0x11234
access 0x21234
Tag
Set Index
Page Offset

## Slide 84: Example
TLB (16 sets, 4 way associative)
MMU
Set 0
Set 1
……
Set 15
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
1 | 0x1 | PP4
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
63
0
15
0x1
0x234
0x1
12
11
access 0x11234, TLB Miss, cache the translation result
access 0x21234
access 0x11234
access 0x21234
Tag
Set Index
Page Offset

## Slide 85: Example
TLB (16 sets, 4 way associative)
MMU
Set 0
Set 1
……
Set 15
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
1 | 0x1 | PP4
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
63
0
15
0x2
0x234
0x1
12
11
access 0x11234, TLB Miss, cache the translation result
access 0x21234, TLB Miss,
access 0x11234
access 0x21234
Tag
Set Index
Page Offset

## Slide 86: Example
TLB (16 sets, 4 way associative)
MMU
Set 0
Set 1
……
Set 15
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
1 | 0x2 | PP6
1 | 0x1 | PP4
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
63
0
15
0x2
0x234
0x1
12
11
access 0x11234, TLB Miss, cache the translation result
access 0x21234, TLB Miss, cache the translation result
access 0x11234
access 0x21234
Tag
Set Index
Page Offset

## Slide 87: Example
TLB (16 sets, 4 way associative)
MMU
Set 0
Set 1
……
Set 15
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
1 | 0x2 | PP6
1 | 0x1 | PP4
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
63
0
15
0x2
0x234
0x1
12
11
access 0x11234, TLB Miss, cache the translation result
access 0x21234, TLB Miss, cache the translation result
access 0x11234
access 0x21234
Tag
Set Index
Page Offset

## Slide 88: Example
TLB (16 sets, 4 way associative)
MMU
Set 0
Set 1
……
Set 15
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
1 | 0x2 | PP6
1 | 0x1 | PP4
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
v | Tag | PPN
63
0
15
0x2
0x234
0x1
12
11
access 0x11234, TLB Miss, cache the translation result
access 0x21234, TLB Miss, cache the translation result
access 0x11234, TLB Hit
access 0x21234, TLB Hit
Tag
Set Index
Page Offset