## Slide 1: Memory & Cache Jinyang Li based on Tiger Wang’s slides

## Slide 2: Memory access is costly
Memory resides off-chip
Microsoft Surface Pro 6 teardown
http://ifixit.com/teardown
Intel Core i5 CPU
Samsung 2GB DRAM

## Slide 3: Memory access is costly
How many memory access are needed?
  movq (%rax), %rbx
  addq %rax, %rbx
1 memory access.
Instruction takes 100 CPU cycles to execute
0 memory access.
Instruction takes ~1 CPU cycle to execute
How to reduce the cost of memory access?

## Slide 4: Principle of locality
Temporal locality
  If memory location x is referenced, then x will likely be referenced again in the near future.
Spatial locality
  If memory location x is referenced, then locations near x will likely be referenced in the near future.
Idea: buffer recently accessed data in cache close to CPU

## Slide 5: Basic idea - caching
Memory
Cache
CPU
rax
rbx
Smaller,
Faster,
Closer to CPU (on-chip)

## Slide 6: Basic idea – caching
Memory
Cache
d
CPU
rax
rbx
Smaller,
Faster,
Closer to CPU
Access the data d
Send the data d
to cpu
Buffer d in the
cache

## Slide 7: Basic idea – caching
Memory
Cache
d
CPU
rax
rbx
Smaller,
Faster,
Closer to CPU
Access the data d
Send the buffered d

## Slide 8: Basic idea – caching
Memory
Cache
d
CPU
rax
rbx
Smaller,
Faster,
Closer to CPU
Access the data d
Send the buffered d
100 ~ 200 cycles
~ 4 cycles

## Slide 9: Intuitive implementation
Caching at byte granularity?
Too slow
  movq (%rax), %rbx requires searching the cache 8 times
High bookkeeping overhead
  each cache entry has 8 bytes of address and 1 byte of data
PA (Physical address) | Data (1 byte)
0x100 | …
0x101 | …
0x102 | …
0x103 | …

## Slide 10: Caching at block granularity
Solution:
Cache one block (cacheline) at a time.
  A typical cacheline size is 64 bytes
Advantages:
Less bookkeeping overhead
  A cache line has 8 byte of address and 64 byte of data
Exploits spatial locality
  Accessing location x causes 64 bytes around x to be cached

## Slide 11: Direct-mapped cache
Caching at block granularity
Each cache line has 64 bytes
CPU Cache
PA | 64 bytes
0x100 | …
0x140 | …
0x80 | …
0xc0 | …
Memory
0x1
……
0x0…088
0x0…080
0x0…040
0x0…048
0x0…050
0x0…058
0x0…060
0x0…068
0x0…070
0x0…078
...
0x1
CPU
access 0x1234
MMU
0x1234
1. In cache? No
3. Return
2. Fetch
0x40

## Slide 12: Direct-mapped cache
CPU Cache
PA | 64 bytes
0x100 | …
0x40 | …
0x80 | …
0xc0 | …
Memory
0x1
……
0x0…088
0x0…080
0x0…040
0x0…048
0x0…050
0x0…058
0x0…060
0x0…068
0x0…070
0x0…078
...
0x1
CPU
access 0x1234
MMU
0x1234
1. In cache? No
3. Return
2. Fetch
0x1
4. Buffer the cacheline,
send 0x1 to the CPU
0x40
Caching at block granularity
Each cache line has 64 bytes

## Slide 13: Direct-mapped cache
CPU Cache
Memory
0x2
0x1
……
0x0…088
0x0…080
0x0…040
0x0…048
0x0…050
0x0…058
0x0…060
0x0…068
0x0…070
0x0…078
...
0x1
CPU
access 0x123c
MMU
0x123c
1. In cache? Yes
0x2
2. Send 0x2 to CPU
0x48
PA | 64 bytes
0x100 | …
0x40 | …
0x80 | …
0xc0 | …
Caching at block granularity
Each cache line has 64 bytes

## Slide 14
Cache line tag
Offset in the cache line
63
8
5
0
CPU Cache (64 bytes cache line)
0
1
2
3
CPU access data at (PA)
Tag | 64 (26) bytes
0x1 | …
Index
6
7
PA
address: 0x48
0000 0000 .... 0000 0000 0000 0000 0100 1000

## Slide 15: Check and identify the location
0x0
0x8
63
8
5
0
CPU Cache (64 bytes cache line)
0
1
2
3
Use bits[6:7] to find the cache line
which may buffer the data.
CPU access data at (0x48 PA)
Tag | 64 (26) bytes
0x1 | …
0x1
6
7
Cache line tag
Index
Offset in the cache line

## Slide 16: Check and identify the location
0x0
0x8
63
8
5
0
CPU Cache (64 bytes cache line)
0
1
2
3
Use bits[6:7] to find the cache line
which may buffer the data.
Compare the cache line tag bits[8:63]
(Cache miss)
CPU access data at (0x48 PA)
Tag | 64 (26) bytes
0x1 | …
0x1
6
7
Cache line tag
Index
Offset in the cache line

## Slide 17: Check and identify the location
0x0
0x8
63
8
5
0
CPU Cache (64 bytes cache line)
0
1
2
3
Use bits[6:7] to find the cache line
which may buffer the data.
Compare the cache line tag bits[8:63]
(Cache miss)
3. Load 64 bytes from 0x40
CPU access data at (0x48 PA)
Tag | 64 (26) bytes
0x0 | …
0x1
6
7
Cache line tag
Index
Offset in the cache line

## Slide 18: Check and identify the location
0x0
0x8
63
8
5
0
CPU Cache (64 bytes cache line)
0
1
2
3
Use bits[6:7] to find the cache line
which may buffer the data.
Compare the cache line tag bits[8:63]
(Cache miss)
Load 64 bytes from 0x40
Send the data at the offset of 0x8 in
buffered cache line.
CPU access data at (0x48 PA)
Tag | 64 (26) bytes
0x0 | …
0x1
6
7
Cache line tag
Index
Offset in the cache line

## Slide 19: Issue I: Cache Collision
Access pattern:
access 0x40
access 0x140
access 0x40
access 0x140
CPU Cache
0
1
2
3
Tag | 64 bytes
0x0 | 64 bytes start at 0x40
Cache line tag: 0
Cache line index: 1
Load 64 bytes start at 0x40 into 1st entry
cache miss

## Slide 20: Issue I: Cache Collision
CPU Cache
0
1
2
3
Tag | 64 bytes
0x1 | 64 bytes start at 0x140
Cache line tag: 1
Cache line index: 1
Evict old cache line (1st entry),
Load 64 bytes start at 0x140 into 1st entry
cache miss
cache miss
Access pattern:
access 0x40
access 0x140
access 0x40
access 0x140

## Slide 21: Issue I: Cache Collision
CPU Cache
0
1
2
3
Tag | 64 bytes
0x0 | 64 bytes start at 0x40
Cache line tag: 0
Cache line index: 1
Evict old cache line (1st entry),
Load 64 bytes start at 0x40 into 1st entry
cache miss
cache miss
cache miss
Access pattern:
access 0x40
access 0x140
access 0x40
access 0x140

## Slide 22: Issue I: Cache Collision
CPU Cache
0
1
2
3
Tag | 64 bytes
0x1 | 64 bytes start at 0x140
Cache line tag: 1
Cache line index: 1
Evict old cache line (1st entry),
Load 64 bytes start at 0x140 into 1st entry
cache miss
cache miss
cache miss
cache miss
Access pattern:
access 0x40
access 0x140
access 0x40
access 0x140

## Slide 23: Solution: Multi-way set associative cache
CPU Cache
Set 0
Set 1
Set 15
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
……
2-way set associative cache
63
0
9
Tag
Cache line offset
Set Index
6
5

## Slide 24: Multi-way set associative cache
CPU Cache
Set 0
Set 1
Set 15
v | Tag | Cache line
v | Tag | Cache line
v | 0x0 | …
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
……
63
0
9
6
5
Tag
Set Index
Cache line offset
0x0
0x0
0x1
Access pattern:
access 0x40
access 0x440
access 0x40
access 0x440
miss

## Slide 25: Multi-way set associative cache
CPU Cache
Set 0
Set 1
Set 15
v | Tag | Cache line
v | Tag | Cache line
v | 0x0 | …
v | 0x1 | …
v | Tag | Cache line
v | Tag | Cache line
……
63
0
9
6
5
Tag
Set Index
Cache line offset
0x1
0x0
0x1
Access pattern:
access 0x40
access 0x440
access 0x40
access 0x440
miss
miss

## Slide 26: Multi-way set associative cache
CPU Cache
Set 0
Set 1
Set 15
v | Tag | Cache line
v | Tag | Cache line
v | 0x0 | …
v | 0x1 | …
v | Tag | Cache line
v | Tag | Cache line
……
63
0
9
6
5
Tag
Set Index
Cache line offset
0x1
0x0
0x1
Access pattern:
access 0x40
access 0x440
access 0x40
access 0x440
miss
miss
hit
hit

## Slide 27: Multi-way set associative cache
CPU Cache
Set 0
Set 1
Set 15
v | Tag | Cache line
v | Tag | Cache line
v | 0x0 | …
v | 0x1 | …
v | Tag | Cache line
v | Tag | Cache line
……
63
0
9
6
5
Tag
Set Index
Cache line offset
0x2
0x0
0x1
Access pattern:
access 0x40
access 0x440
access 0x840
Which cache line in set 1 should be evicted?

## Slide 28: Cache line replacement policy
LFU (least-frequently-used)
  Replace the line that has been referenced the fewest times over some past time window
LRU (least-recently-used)
  Replace the line that has the furthest access in the past
These policies require additional time and hardware

## Slide 29: Issue II: sequential address translation and cache access
Current design:
  Address translation must finish before cache access
CPU Cache
Memory
0x1
……
0x0…088
0x0…080
0x0…040
0x0…048
0x0…050
0x0…058
0x0…060
0x0…068
0x0…070
0x0…078
...
0x1
CPU
MMU
64 bytes data
0x1234
Set 0
Set 1
Set 15
……
Virtual Address
Physical Address
Physical Address
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line

## Slide 30: Solution: virtual indexing and physical tag
How to parallelize address translation and cache access?
Use VA to index set, match tag from PA
CPU Cache
Memory
0x1
……
0x0…088
0x0…080
0x0…040
0x0…048
0x0…050
0x0…058
0x0…060
0x0…068
0x0…070
0x0…078
...
0x1
CPU
MMU
64 bytes data
0x1234
Set 0
Set 1
Set 15
……
1. Virtual Address
3. Physical Address
2. Physical Address
 Tag
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
1. Virtual Address
Set Index

## Slide 31: Virtual Index and Physical Tag
CPU Cache
Set 0
Set 1
Set 15
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
……
2-way set associative cache
63
0
Tag
Cache line offset
6
5
PA:
…
Cache line offset
Set Index
VA:
9
6

## Slide 32: Virtual Index and Physical Tag
CPU Cache
Set 0
Set 1
Set 15
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
v | Tag | Cache line
……
2-way set associative cache
63
0
0x3fffc01
Cache line offset
6
5
PA:
VA:
9
6
access va 0x1040 pa 0xffff0040
…
Cache line offset
0x1

## Slide 33: Memory hierarchy
Memory
L1 Cache
CPU
rax
rbx
L2 Cache
L3 Cache
~ 4 cycles
Virtual Index
Physical Tag
Virtual/Physical Index
Physical Tag
Physical/Virtual Index
Physical Tag
~ 12 cycles
~ 35 cycles
~ 150 cycles

## Slide 34: Which program runs faster?
#define ROWS 100
#define COLS 100
float matrix[ROWS][COLS];
void MulRowByRow(float mat[ROWS][COLS], float c) {
for (int i = 0; i < ROWS; i++)
for (int j = 0; j < COLS; j++)
mat[i][j] *= c;
}
void MulColByCol(float mat[ROWS][COLS], float c) {
for (int j = 0; j < COLS; j++)
for (int i = 0; i < ROWS; i++)
mat[i][j] *= c;
}

## Slide 35: Cache summary
Caching is used to speed up memory access
  L1/L2/L3 cache data
TLB cache address translation
Cache design:
  Direct mapping
  Multi-way set associative
  Virtual index + physical tag parallelize cache access and address translation