## Slide 1: Pipelined CPU
Jinyang Li
Based on the slides of Patterson and Hennessy

## Slide 2: What we’ve learnt so far
Combinatorial logic
  ALU
Sequential logic
  Clocks and basic state elements (SR latch, D latch, flip-flop)
The single-cycle CPU design

## Slide 3: Single-cycle CPU uses a slow clock
Load instruction latency (in ps)
200
instruction
fetch
1 picosecond = 10-12 sec
+ 100
register
read
+ 200
ALU
+ 200
data
access
+ 100
register
write
Clock cycle >= 800 ps

## Slide 4: Pipelining: a laundry analogy
wash
dry
fold
store
Pipelined laundry: overlapping execution
  Parallelism improves performance

## Slide 5: RISC-V Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 6: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 7: Pipeline Speedup
Pipelining increases throughput (instructions/sec)
  Latency (time for each instruction) does not decrease
If all stages are balanced (i.e., all take the same time)
  throughputpipelined = number-of-stages * throughputnonpipelined
  If not balanced, speedup is less
Throughput = 1/time between instructions

## Slide 8: Pipelining and ISA Design
RISC-V ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage

## Slide 9: Pipeline challenges: hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 10: Structure Hazards
Conflict use of a single resource
Example: Suppose CPU uses a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Solution: Use separate instruction/data memories

## Slide 11: Data Hazards
  An instruction depends on the previous instruction to complete its data read/write
  add x19, x0, x1 sub x2, x19, x3

## Slide 12: Control hazard
Wait until branch outcome determined before fetching next instruction

## Slide 13: A basic pipelined RISC-V CPU

## Slide 14: Pipelined Datapath
Right-to-left flow leads to hazards
IF: instruction
fetch
ID: instruction
decode/reg
read
EX: execute/
address calc
MEM: memory access
WB: write-back

## Slide 15: Pipeline registers
  Needed to hold information produced in previous cycle
IF/ID
ID/EX
EX/MEM
MEM/WB

## Slide 16: IF for Load, Store
Single-clock-cycle diagram shows the state of an entire datapath
during a single clock cycle
Right-shading indicates read access

## Slide 17: ID for Load, Store, …

## Slide 18: EX for Load

## Slide 19: MEM for Load

## Slide 20: WB for Load
Wrong register number

## Slide 21: Corrected Datapath for Load

## Slide 22: EX for Store

## Slide 23: MEM for Store

## Slide 24: WB for Store

## Slide 25: Multi-Cycle Pipeline Diagram
Traditional form

## Slide 26: Multi-Cycle Pipeline Diagram
Form showing resource usage

## Slide 27: Single-Cycle Pipeline Diagram
State of pipeline in a given cycle

## Slide 28: Pipelined Control (Simplified)
Set in EX
Set in MEM
Set in WB

## Slide 29: Pipelined Control
ALUSrc
ALUOp
MemWrite
Branch
PCSrc
MemToReg
RegWrite
Control signals derived from instruction, same as
in single-cycle implementation

## Slide 30: Data Hazards in ALU Instructions
Example instruction sequence:
  sub x2, x1,x3 and x12,x2,x5 or x13,x6,x2 add x14,x2,x2 sd x15,100(x2)
Solution: forwarding (aka bypassing)
  Use result when it’s computed; don’t wait for it to be stored in register

## Slide 31: Dependencies & Forwarding
Data hazards

## Slide 32: Detecting the Need to Forward
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs1: register number for Rs1 in ID/EX pipeline register
ALU operand register numbers (in EX stage) are:
  ID/EX.RegisterRs1
  ID/EX.RegisterRs2
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs1
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRs2
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs1
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRs2
EX-hazard:
Fwd from EX/MEM pipeline reg
Mem-hazard: Fwd from MEM/WB pipeline reg

## Slide 33: Detecting the Need to Forward
But only if forwarding instruction will write to a register!
  EX/MEM.RegWrite, MEM/WB.RegWrite
And only if Rd for that instruction is not x0
  EX/MEM.RegisterRd ≠ 0, MEM/WB.RegisterRd ≠ 0

## Slide 34: Forwarding Paths

## Slide 35: Double Data Hazard
Consider the sequence:
  add x1,x1,x2 add x1,x1,x3 add x1,x1,x4
Both hazards occur
  Want to use the most recent
Revise MEM hazard condition
  Only fwd if EX hazard condition isn’t true
MEM hazard
EX hazard

## Slide 36: Load-Use Hazard Detection
Load-use hazard cannot be resolved using forwarding alone
Check load-use hazard using condition
  ID/EX.MemRead and ((ID/EX.RegisterRd = IF/ID.RegisterRs1) or (ID/EX.RegisterRd = IF/ID.RegisterRs1))
If detected, stall and insert bubble
ld x2, 20(x1)
and x4, x2, x5
Cannot be forwarded

## Slide 37: How to Stall the Pipeline
Force control values in ID/EX register to 0
  EX, MEM and WB do nop (no-operation)
Prevent update of PC and IF/ID register
  Using instruction is decoded again
  Following instruction is fetched again
  1-cycle stall allows MEM to read data for ld
    Can subsequently forward to EX stage

## Slide 38: Load-Use Data Hazard
Stall inserted here

## Slide 39: Datapath with Hazard Detection
If hazard is detected, set WB/MEM/EX controls to zero (so no registers/memory is written)

## Slide 40: Summary
Pipeline increases throughput by overlapping execution of multiple instructions
Pipeline hazard
  Structure (solution: add resources)
  Data (solution: forwarding)
  Control (next class)
Pipeline stalls