## Slide 1: Machine Program: Basics
Jinyang Li
Some are based on Tiger Wang’s slides

## Slide 2: Lesson plan
What we’ve learnt so far:
  How integers/reals/characters are represented by computers
  C programming
Today:
  Basic hardware execution of a program
  x86 registers
  x86 move instruction

## Slide 3: Can we build a machine to execute C directly?
Historical precedents:
  LISP machine (80s)
  Intel iAPX 432 (Ada)

## Slide 4: Why not directly execute C?
Results in very complex hardware design
  Complex  Hard to implement w/ high performance
A better approach:
C program
Simple hardware interface
Optimizing Compiler (e.g. gcc) translates C to hardware API

## Slide 5: C vs. assembly vs. machine code
long x;
long y;
y = x;
y = 2*y;
Compiler
movq %rdi, %rax
addq %rax, %rax
assembler
01000010000001110
10001001010100110
….
gcc –c
does both
gcc –S
compiles to assembly
C source
x86 assembly
x86 machine code

## Slide 6: C vs. machine code
long x;
long y;
y = x;
y = 2*y;
Memory
……
0x00…0058
0x00…0050
…
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
instruction
instruction
instruction
data
data
data
data
x:
y:
compile to
x86 machine code
E.g. move data from one memory location to another
E.g. multiply the number at some memory location by a constant
No concept of
variables, scopes, types

## Slide 7: How CPU executes a program
CPU
Memory
……
…
instruction
instruction
instruction
instruction
data
data
data
data
instruction
data
How does CPU know which instr/data to fetch?
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
instruction
address
data
address
Questions
Where does CPU keep the instruction and data?

## Slide 8: How CPU executes a program
CPU
Memory
……
…
instruction
instruction
instruction
instruction
data
data
data
data
instruction
data
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
instruction
address
data
address
CPU can execute billions of instructions per second
CPU can do ~10 million fetches/sec from memory

## Slide 9: Register – temporary storage area built into a CPU
PC: Program counter, also called instruction pointer (IP).
  Store memory address of next instruction
IR: CPU’s internal buffer storing the fetched instruction
General purpose registers:
  Store data and address used by programs
Program status and control register:
  Status of the instruction executed

## Slide 10: Steps of execution in CPU
1. PC contains the instruction’s address
2. Fetch the instruction to internal buffer
3. Execute the instruction which does one of following:
  Memory operations: move data from memory to register (or opposite)
  Arithmetic operations: add, shift etc.
  Control flow operations.
4. PC is updated to contain the next instruction’s address.

## Slide 11: Instruction Set Architecture (ISA)
ISA: interface exposed by hardware to software writers
X86_64 is the ISA implemented by Intel/AMD CPUs
  64-bit version of x86
ARM is another common ISA
  Phones, tablets, Raspberry Pi, Apple’s new M1 laptop
RISC-V is yet another ISA
  P&H textbook’s ISA.
  Open-sourced, royalty-free
Apple laptops use ARM chips. Hence we need a virtual
machine to run C programs compiled to x86
Lectures on assembly
Lectures on hardware

## Slide 12: X86-64 ISA: registers
Program counter:
  called %rip in x86_64
IR: CPU’s internal buffer storing the fetched instruction
General purpose registers:
  16 8-byte registers: %rax, %rbx …
Program status and control register:
  Called “RFLAGS” in x86_64
Visible to programmers
(aka part of ISA)

## Slide 13: X86-64 general purpose registers: 8-byte
%rsp
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
8 bytes
%r14
%r8
%r9
%r10
%r11
%r12
%r13
%r15

## Slide 14: X86-64 general purpose registers: 4-byte
%rsp
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
%r14
%r8
%r9
%r10
%r11
%r12
%r13
%r15
8 bytes
%eax
%ebx
%ecx
%edx
%esi
%r8d
%r9d
%r10d
%r11d
%r12d
%edi
%esp
%ebp
%r13d
%r14d
%r15d
4 bytes
%eax refers to the lower-order 4-byte of %rax
4-byte registers refer to the lower-order 4-bytes of original registers.

## Slide 15: X86-64 general purpose registers: 2-byte
%rax
%eax
8 bytes
4 bytes
%ax
2 bytes
2-byte registers refer to the lower-order 2-bytes of original registers.

## Slide 16: X86-64 general purpose registers: 1-byte
%rax
%eax
8 bytes
4 bytes
%ax
2 bytes
%rax
%eax
%ah
%al
1 byte

## Slide 17: x86-64 execution
Memory
……
…
instruction
instruction
instruction
instruction
data
data
data
data
CPU
0x00…0058
RIP:
instruction
IR:
instruction
addr
addr
data
GPRs:
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rsp
%rbp
…
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048

## Slide 18: X86 ISA
https://software.intel.com/en-us/articles/intel-sdm#combined
A must-read for
compiler and OS writers

## Slide 19: x86 instruction: Moving data
movq Source, Dest
  Copy a quadword (64-bit) from the source operand (first operand) to the destination operand (second operand).
We use AT&T (instead of Intel) syntax for assembly

## Slide 20: Moving data
movq Source, Dest
  Copy a quadword (8-bytes) from the source operand to the destination operand.
suffix
Suffix | Name | Size (byte)
b | Byte | 1
w | Word | 2
l | Long | 4
q | Quadword | 8

## Slide 21: Why using a size suffix?
movq Source, Dest
  Support full backward compatibility
    New processor can run the same binary file compiled for older processors
  In the Intel x86 world, a word = 16 bits.
    8086 refers to 16 bits as a word

## Slide 22: Moving data
movq Source, Dest
Operand Types
  Immediate: Constant integer data
    Prefixed with $
    E.g: $0x400, $-533
  Register: One of general purpose registers
    E.g: %rax, %rsi
  Memory: 8 consecutive bytes of memory
    Indexed by register with various “address modes”
    Simplest example: (%rax)

## Slide 23: movq Operand combinations
movq
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
movq $0x4,%rax
movq $0x4,(%rax)
movq %rax,%rdx
movq %rax,(%rdx)
movq (%rax),%rdx
Example
2. No memory-memory mov
1. Immediate can only be source

## Slide 24: movq Imm, Reg
Memory
movq %rax,%rbx
……
…
CPU
0x00…0050
RIP:
IR:
RAX:
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
movq $0x4,%rax
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
%rip
movq $0x4,%rax
0x00…0004

## Slide 25: movq Reg, Reg
Memory
movq $0x4,%rax
movq %rax,%rbx
……
…
CPU
0x00…0058
RIP:
IR:
RAX:
0x00…0004
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
movq $0x4, %rax
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
%rip
movq %rax, %rbx
0x00…0004

## Slide 26: movq Mem, Reg
How to represent a “memory” operand?

## Slide 27: Direct addressing: use register to index memory
(Register)
  The content of the register specifies memory address
  movq (%rax), %rbx

## Slide 28: movq (%rax), %rbx
movq (%rax), %rbx
0x10
……
…
CPU
0x00…0058
RIP:
IR:
RAX:
0x18
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
%rip
movq (%rax),%rbx
How many bytes are copied? Source? Destination?

## Slide 29: movq (%rax), %rbx
Memory
movq (%rax), %rbx
0x10
……
…
CPU
0x00…0058
RIP:
IR:
RAX:
0x18
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
movq (%rax), %rbx
0x00…0018
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
%rip
0x10

## Slide 30: Demo: Swap

## Slide 31: swap function
void
swap(long *a, long* b) {
long tmp = *a;
*a = *b;
*b = tmp;
}
swap:
gcc –S –O3 swap.c
Makes gcc output assembly
(human readable machine instructions)

## Slide 32: swap function
void
swap(long *a, long* b) {
long tmp = *a;
*a = *b;
*b = tmp;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
gcc –S –O3 swap.c
%rdi stores a
%rsi stores b
%rax is local variable tmp

## Slide 33: swap function
void
swap(long *a, long* b) {
long tmp = *a;
*a = *b;
*b = tmp;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
gcc –S –O3 swap.c
Use two instructions and %rdx to perform
memory to memory move

## Slide 34: swap function
void
swap(long *a, long* b) {
long tmp = *a;
*a = *b;
*b = tmp;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
gcc –S –O3 swap.c

## Slide 35: swap func
CPU
0x00…0048
PC:
IR:
RAX:
0x00…0018
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
Memory
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
movq (%rdi), %rax
0x2
0x1
……
…
PC
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
main.x:
main.y:

## Slide 36: swap func
Memory
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
movq (%rdi), %rax
0x2
0x1
……
…
CPU
0x00…0048
PC:
IR:
RAX:
0x00…0018
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
movq (%rdi), %rax
PC
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
main.x:
main.y:

## Slide 37: swap func
CPU
0x00…0048
PC:
IR:
RAX:
0x1
0x00…0018
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
movq (%rdi), %rax
Memory
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
movq (%rdi), %rax
0x2
0x1
……
…
PC
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
main.x:
main.y:

## Slide 38: swap func
CPU
0x00…0050
PC:
IR:
RAX:
0x1
0x00…0018
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
movq (%rsi), %rdx
Memory
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
movq (%rdi), %rax
0x2
0x1
……
…
PC
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
main.x:
main.y:

## Slide 39: swap func
CPU
0x00…0050
PC:
IR:
RAX:
0x1
0x2
0x00…0018
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
movq (%rsi), %rdx
Memory
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
movq (%rdi), %rax
0x2
0x1
……
…
PC
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
main.x:
main.y:

## Slide 40: swap func
CPU
0x00…0058
PC:
IR:
RAX:
0x1
0x2
0x00…0018
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
movq %rdx, (%rdi)
Memory
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
movq (%rdi), %rax
0x2
0x1
……
…
PC
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
main.x:
main.y:

## Slide 41: swap func
CPU
0x00…0058
PC:
IR:
RAX:
0x1
0x2
0x00…0018
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
movq %rdx, (%rdi)
Memory
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
movq (%rdi), %rax
0x2
0x2
……
…
PC
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
main.x:
main.y:

## Slide 42: swap func
CPU
0x00…0060
PC:
IR:
RAX:
0x1
0x2
0x00…0018
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
movq %rax, (%rsi)
Memory
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
movq (%rdi), %rax
0x2
0x2
……
…
PC
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
main.x:
main.y:

## Slide 43: swap func
CPU
0x00…0060
PC:
IR:
RAX:
0x1
0x2
0x00…0018
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
movq %rax, (%rsi)
Memory
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
movq (%rdi), %rax
0x1
0x2
……
…
PC
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
main.x:
main.y:

## Slide 44: Summary
Basic hardware execution
  Instructions and data stored in memory
  CPU fetches instructions one at a time according to PC
X86-64 ISA
  %rip (PC), 16 general-purpose registers
  movq allows copying data across registers or memory ↔register.
Notes: .

## Slide 45: Limitation of direct addressing
Issue: the address must be calculated and stored in the register before each memory access.

## Slide 46: Issue
Issue: the address must be calculated and stored in the register before each memory access.
long a[3] = {3, 2, 1};
for(int i = 0; i < 3; i++) {
a[i] = i;
}
long a[3] = {1, 2, 3};
for(int i = 0; i < 3; i++) {
1. calculate &a[i] and put result in reg
2. mov $i, (reg)
}

## Slide 47: Observation
long a[3] = {3, 2, 1};
for(int i = 0; i < 3; i++) {
a[i] = i;
}
  a[0], a[1] and a[2] have the same base address:&a[0]
  &a[0]: &a[0] + 0
  &a[1]: &a[0] + 1
  &a[2]: &a[0] + 2

## Slide 48: Address mode with displacement
  D(Register): val(Register) + D
  Register specifies the start of the memory region
  Constant D specifies the offset
0x10
RAX:
20(RAX)
0x10
20
+
RAX:
0x24

## Slide 49: Address mode with displacement
long a[] = {3, 2, 1};
for(int i = 0; i < 3; i++) {
a[i] = i;
}
long a[] = {1, 2, 3};
for(int i = 0; i < 3; i++) {
mov $i, D(reg); // D = i * 8, reg = &a[0]
}
  D(Register): val(Register) + D
  Register specifies the start of the memory region
  Constant D specifies the offset

## Slide 50: Complete Memory Addressing Mode
D(Rb, Ri, S): val(Rb) + S * val(Ri) + D
  Rb: Base register
  D: Constant “displacement”
  Ri: Index register (not %rsp)
  S: Scale: 1, 2, 4, or 8
0x8
4
*
rbx:
0x3a
0x10
rax:
S:
+
0x20
10
D:
10(%rax, %rbx, 4)

## Slide 51: Complete Memory Addressing Mode
D(Rb, Ri, S): val(Rb) + S * val(Ri) + D
  D: Constant “displacement”
  Rb: Base register
  Ri: Index register (not %rsp)
  S: Scale: 1, 2, 4, or 8
If S is 1 or D is 0, they can be omitted
  (Rb, Ri): val(Rb) + val(Ri)
  D(Rb, Ri): val(Rb) + val(Ri) + D
  (Rb, Ri, S): val(Rb) + S * val(Ri)

## Slide 52: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Carnegie Mellon
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
%rdx | 0xf000
%rcx | 0x100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 53: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Carnegie Mellon
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
%rdx | 0xf000
%rcx | 0x100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 54: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Carnegie Mellon
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
%rdx | 0xf000
%rcx | 0x100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 55: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Carnegie Mellon
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) |  | 
%rdx | 0xf000
%rcx | 0x100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 56: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Carnegie Mellon
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) | 2*0xf000 + 0x80 | 0x1e080
%rdx | 0xf000
%rcx | 0x100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 57: Example
Memory
movq $1, 8(%rdi, %rax, 8)
movq $2, (%rdi, %rbx, 8)
a[3]
a[2]
a[1]
a[0]
……
…
a[4]
CPU
0x00…0050
PC:
IR:
movq $1, 8(%rdi, %rax, 8)
RAX:
0x00…0001
0x00…0002
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
PC
a[5]
a[6]
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060

## Slide 58: Example
Memory
movq $1, 8(%rdi, %rax, 8)
movq $2, (%rdi, %rbx, 8)
a[3]
a[2]: 1
a[1]
a[0]
……
…
a[4]
CPU
0x00…0050
PC:
IR:
movq $1, 8(%rdi, %rax, 8)
RAX:
0x00…0001
0x00…0002
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
PC
a[5]
a[6]
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060

## Slide 59: Example
Memory
movq $1, 8(%rdi, %rax, 8)
movq $2, (%rdi, %rbx, 8)
a[3]
a[2]: 2
a[1]
a[0]
……
…
a[4]
CPU
0x00…0058
PC:
IR:
movq $1, (%rdi, %rbx, 8)
RAX:
0x00…0001
0x00…0002
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
PC
a[5]
a[6]
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060

## Slide 60: mov{bwlq}
movb src, dest | Copy a byte from the source operand to the destination operand. e.g., movb %al, %bl
movw src, dest | Copy a word from the source operand to the destination operand. e.g., movw %ax, %bx
movl src, dest | Copy a long (32 bits) from the source operand to the destination operand. e.g., movl %eax, %ebx
movq src, dest | Copy a quadword from the source operand to the destination operand. e.g., movq %rax, %rbx

## Slide 61: The lea instruction
leaq Source, Dest
  load effective address: set Dest to the address denoted by Source address mode expression

## Slide 62: Example
Memory
movq 8(%rdi), %rax
movq (%rbx), %rcx
leaq 8(%rdi), %rbx
300
200
100
……
…
CPU
0x00…0048
PC:
IR:
leaq 8(%rdi),%rbx
RAX:
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
PC
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060

## Slide 63: Example
Memory
movq 8(%rdi), %rax
movq (%rbx), %rcx
leaq 8(%rdi), %rbx
300
200
100
……
…
CPU
0x00…0048
PC:
IR:
leaq 8(%rdi),%rbx
RAX:
0x00…0018
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
PC
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060

## Slide 64: A common usage of leaq
Compute expressions: x + K*y + d (K=1, 2, 4, or 8)
long m3(long x)
{
return x*3;
}
Assume %rdi has the value of x
leaq (%rdi, %rdi,2), %rax

## Slide 65: Arithmetic Expression Puzzle
Carnegie Mellon
leaq (%rdi,%rsi,2), %rax
leaq (%rax,%rax,4), %rax
Suppose %rdi, %rsi, %rax contains variable x, y, s respectively
long f(long x, long y)
{
long s = ??;
return s;
}
Notes: long s = x+2*y;
s *= 5;

## Slide 66: Arithmetic Expression Puzzle
Carnegie Mellon
leaq (%rdi,%rsi,2), %rax
leaq (%rax,%rax,4), %rax
Suppose %rdi, %rsi, %rax contains variable x, y, s respsectively
long f(long x, long y)
{
long s = 5(x + 2y);
return s;
}
Notes: long s = x+2*y;
s *= 5;

## Slide 67: Basic Arithmetic Operations
Carnegie Mellon
    addq Src, Dest Dest = Dest + Src
    subq Src, Dest Dest = Dest  Src
    imulq Src, Dest Dest = Dest * Src
    incq Dest Dest = Dest + 1
    decq Dest Dest = Dest  1
    negq Dest Dest =  Dest

## Slide 68: Bitwise Operations
Carnegie Mellon
    salq Src,Dest Dest = Dest << Src Arithmetic left shift
    sarq Src,Dest Dest = Dest >> Src Arithmetic right shift
    shlq Src,Dest Dest = Dest << Src Logical left shift
    shrq Src,Dest Dest = Dest >> Src Logical right shift
    xorq Src,Dest Dest = Dest ^ Src
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
    notq Dest Dest = ~Dest
same

## Slide 69: Example
Memory
addq %rax , 8(%rdi)
300
200
100
……
…
CPU
0x00…0058
PC:
IR:
addq %rax, 8(%rdi)
RAX:
0x00…0001
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
PC
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060

## Slide 70: Example
Memory
addq %rax , 8(%rdi)
300
201
100
……
…
CPU
0x00…0058
PC:
IR:
addq %rax, 8(%rdi)
RAX:
0x00…0001
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
PC
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060