## Slide 1: Basic/Pipelined processor Implementation
Jinyang Li

## Slide 2: Today’s lesson plan
Basic single-cycle CPU design, continued
Pipelining idea and challenges

## Slide 3: Recall our basic RISC-V CPU: datapath w/ control
Control derived from instruction type

## Slide 4: R-Type Inst
add x5, x6, x7
funct7
rs2
rs1
rd
funct3
opcode

## Slide 5: BEQ Instruction
beq x5, x6, 100
rs2
rs1
funct3
opcode

## Slide 6: Load Inst
ld x5, 40(x6)
immediate
rs1
rd
funct3
opcode

## Slide 7: Basic CPU must finish an instruction in one clock cycle  use a “slow” clock
Load instruction latency (in ps)
200
instruction
fetch
1 picosecond = 10-12 sec
+ 100
register
read
+ 200
ALU
+ 200
data
access
+ 100
register
write
Clock cycle >= 800 ps

## Slide 8: Our basic design is slow
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary clock period for different instructions
Next: improve performance by pipelining

## Slide 9: Pipelining: a laundry analogy
wash
dry
fold
store
Pipelined laundry: overlapping execution
  Parallelism improves performance

## Slide 10: RISC-V Pipeline
Five stages:
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 11: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 12: Pipeline Speedup
Pipelining increases throughput (instructions/sec)
  Latency (time for each instruction) does not decrease
If all stages are balanced (i.e., all take the same time)
  throughputpipelined = number-of-stages * throughputnonpipelined
  If not balanced, speedup is less
Throughput = 1/(time between instructions)

## Slide 13: Pipelining and ISA Design
RISC-V ISA is designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage

## Slide 14: Pipeline challenges: hazards
Situations that prevent starting next instruction in the next cycle
Structure hazard
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its write
Control hazard
  Which instruction to execute depends on previous instruction

## Slide 15: Structure Hazards
Conflict use of a single resource
Example: Suppose CPU uses a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Solution: Use separate instruction/data memories

## Slide 16: Data Hazards
  An instruction depends on the previous instruction to complete its write
add x19, x0, x1 sub x2, x19, x3
Instruction mem is read; right-shading indicates read
Regfile is read
Regfile is written; left-shading indicates write

## Slide 17: Control hazard
Wait until branch outcome is determined before fetching next instruction
Assume we put in extra hardware to resolve branch outcome at this stage

## Slide 18: Control hazard
Wait until branch outcome is determined before fetching next instruction

## Slide 19: A basic pipelined RISC-V CPU

## Slide 20: Pipelined Datapath
Right-to-left flow leads to hazards
IF: instruction
fetch
ID: instruction
decode/reg
read
EX: execute/
address calc
MEM: memory access
WB: write-back

## Slide 21: Pipeline registers
  : needed to hold data produced in previous cycle
IF/ID
ID/EX
EX/MEM
MEM/WB

## Slide 22: IF for Load, Store
Single-clock-cycle diagram shows the state of an entire datapath
during a single clock cycle

## Slide 23: ID for Load, Store, …

## Slide 24: EX for Load

## Slide 25: MEM for Load

## Slide 26: WB for Load
Wrong register number

## Slide 27: Corrected Datapath for Load

## Slide 28: EX for Store

## Slide 29: MEM for Store

## Slide 30: WB for Store

## Slide 31: Single-Cycle Pipeline Diagram
State of pipeline in a given cycle

## Slide 32: Multi-Cycle Pipeline Diagram
Traditional form

## Slide 33: Multi-Cycle Pipeline Diagram
Form showing resource usage

## Slide 34: Pipelined Control (Simplified)
Set in EX
Set in MEM
Set in WB

## Slide 35: Pipelined Control
ALUSrc
ALUOp
MemWrite
Branch
PCSrc
MemToReg
RegWrite
Control signals derived from instruction, same as
in single-cycle implementation

## Slide 36: Summary
Basic single-cycle CPU design
  Data path vs. control path
  Clock frequency is limited by the longest delay
Basic 5-stage pipelined design:
  Main idea: Parallel processing of different stages of an instruction’s execution
  RISC-V 5-stage pipeline (IF, ID, EXE, MEM, WB)
  Pipeline hazards: structure, data, control