## Slide 1: Machine execution
Jinyang Li

## Slide 2: Lesson Plan: last time
Basic h/w execution model:
  CPU fetch next instructions from memory according to %rip
  Decode and execute instruction (e.g. mov instruction)
  CPU updates %rip to point to next instruction
ISA (instruction set architecture): x86, ARM, RISC-V
X86 ISA
  %rip, 16 general purpose registers
  mov instruction

## Slide 3: Lesson Plan: today
mov
  complete memory addressing
lea
arithmetic instructions
How CPUs realize non-linear control flow

## Slide 4: mov: limitation of direct addressing
Direct addressing
  The address must be calculated and stored in the register before each memory access.
long a[3] = {1, 2, 3};
for(int i = 0; i < 3; i++)
a[i] = 0;
Calculate address of a[i]
Store it in some register, e.g. %rax
Do memory write, e.g. movq $0, (%rax)
&a[i] = address of a[0] + stride * i

## Slide 5: Address mode with displacement
  D(Register): val(Register) + D
  Register specifies the start of the memory region
  Constant D specifies the offset
Memory Operand: 20(RAX)
0x10
20
+
RAX:
0x24

## Slide 6: Address mode with displacement
long a[] = {1, 2, 3};
for(int i = 0; i < 3; i++) {
a[i] = 0;
}
Store address of a[0] in some register, e.g. %rax
Do 3 memory writes:
  mov $0, (%rax)
  mov $0, 8(%rax)
  mov $0, 16(%rax)
  D(Register): val(Register) + D
  Register specifies the start of the memory region
  Constant D specifies the offset

## Slide 7: X86’s Complete Memory Addressing Mode
D(Rb, Ri, S): val(Rb) + S * val(Ri) + D
  Rb: Base register
  D: Constant “displacement”
  Ri: Index register (not %rsp)
  S: Scale: 1, 2, 4, or 8
0x8
4
*
rbx:
0x3a
0x10
rax:
S:
+
0x20
10
D:
Memory operand: 10(%rax, %rbx, 4)

## Slide 8: Complete Memory Addressing Mode
D(Rb, Ri, S): val(Rb) + S * val(Ri) + D
If S is 1 or D is 0, they can be omitted
  (Rb, Ri): val(Rb) + val(Ri)
  D(Rb, Ri): val(Rb) + val(Ri) + D
  (Rb, Ri, S): val(Rb) + S * val(Ri)

## Slide 9: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Carnegie Mellon
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
%rdx | 0xf000
%rcx | 0x100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 10: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Carnegie Mellon
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
%rdx | 0xf000
%rcx | 0x100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 11: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Carnegie Mellon
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
%rdx | 0xf000
%rcx | 0x100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 12: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Carnegie Mellon
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) |  | 
%rdx | 0xf000
%rcx | 0x100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 13: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Carnegie Mellon
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) | 2*0xf000 + 0x80 | 0x1e080
%rdx | 0xf000
%rcx | 0x100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 14: Complete addressing mode
long a[] = {1, 2, 3};
for(int i = 0; i < 3; i++) {
a[i] = 0;
}
Store address of a[0] in some register, say %rdi, store i in another register, say %rax
Do memory write: mov $0, (%rdi, %rax, ? )
D(Rb, Ri, S): val(Rb) + S * val(Ri) + D

## Slide 15: Example
Memory
movq $0, (%rdi, %rax, 8)
addq $1, %rax
movq $0, (%rdi, %rax, 8)
0x3
0x2
0x1
……
…
CPU
0x00…0050
RIP:
RAX:
0x00…0000
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
%rip
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
a[0]:
a[1]:
a[2]:
…
addq $1, %rax
0x00…0068

## Slide 16: Example
Memory
movq $0, (%rdi, %rax, 8)
addq $1, %rax
movq $0, (%rdi, %rax, 8)
0x3
0x2
0x0
……
…
CPU
0x00…0050
RIP:
RAX:
0x00…0000
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
%rip
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
a[0]:
a[1]:
a[2]:
…
addq $1, %rax
0x00…0068

## Slide 17: Example
Memory
movq $0, (%rdi, %rax, 8)
addq $1, %rax
movq $0, (%rdi, %rax, 8)
0x3
0x2
0x0
……
…
CPU
0x00…0050
RIP:
RAX:
0x00…0001
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
%rip
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
a[0]:
a[1]:
a[2]:
…
addq $1, %rax
0x00…0068

## Slide 18: Example
Memory
movq $0, (%rdi, %rax, 8)
addq $1, %rax
movq $0, (%rdi, %rax, 8)
0x3
0x0
0x0
……
…
CPU
0x00…0050
RIP:
RAX:
0x00…0001
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
%rip
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
a[0]:
a[1]:
a[2]:
…
addq $1, %rax
0x00…0068

## Slide 19: lea instruction
leaq Source, Dest
  Short for Load Effective Address
  Set Dest to the address denoted by Source address mode expression
  Performs address calculation only; no memory access!

## Slide 20: Example
Memory
…
…
…
leaq 8(%rdi), %rbx
0x3
0x2
0x1
……
…
CPU
0x00…0048
RIP:
RAX:
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
%rip
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060

## Slide 21: Example
Memory
…
…
…
leaq 8(%rdi), %rbx
0x3
0x2
0x1
……
…
CPU
0x00…0048
RIP:
RAX:
0x00…0018
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
%rip
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060

## Slide 22: A common use case for leaq
Lea is used to compute certain simple arithmetic expression
long m3(long x)
{
return x*3;
}
Assume %rdi has the value of x
leaq (%rdi, %rdi,2), %rax

## Slide 23: Arithmetic Expression Puzzle
Carnegie Mellon
leaq (%rdi,%rsi,2), %rax
leaq (%rax,%rax,4), %rax
Suppose %rdi, %rsi, %rax corresponds to variables x, y, s, respectively
long f(long x, long y)
{
long s = ??;
return s;
}
Notes: long s = x+2*y;
s *= 5;

## Slide 24: Arithmetic Expression Puzzle
Carnegie Mellon
leaq (%rdi,%rsi,2), %rax
leaq (%rax,%rax,4), %rax
Suppose %rdi, %rsi, %rax contains variable x, y, s respectively
long f(long x, long y)
{
long s = 5(x + 2y);
return s;
}
Notes: long s = x+2*y;
s *= 5;

## Slide 25: Basic Arithmetic Operations
Carnegie Mellon
    addq Src, Dest Dest = Dest + Src
    subq Src, Dest Dest = Dest  Src
    imulq Src, Dest Dest = Dest * Src
    incq Dest Dest = Dest + 1
    decq Dest Dest = Dest  1
    negq Dest Dest =  Dest

## Slide 26: Bitwise Operations
Carnegie Mellon
    salq Src,Dest Dest = Dest << Src Arithmetic left shift
    sarq Src,Dest Dest = Dest >> Src Arithmetic right shift
    shlq Src,Dest Dest = Dest << Src Logical left shift
    shrq Src,Dest Dest = Dest >> Src Logical right shift
    xorq Src,Dest Dest = Dest ^ Src
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
    notq Dest Dest = ~Dest
same

## Slide 27: Example
Memory
addq %rax , 8(%rdi)
…
0x3
0x2
0x1
……
…
CPU
0x00…0058
RIP:
RAX:
0x00…0001
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
%rip
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060

## Slide 28: Example
Memory
addq %rax , 8(%rdi)
…
0x3
0x3
0x1
……
…
CPU
0x00…0058
RIP:
RAX:
0x00…0001
0x00…0010
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
%rip
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060

## Slide 29: Lesson Plan: today
mov
  complete memory addressing
lea
arithmetic instructions
How CPUs realize non-linear control flow

## Slide 30: How is control flow realized?
???
if … else
for loop
while loop
…

## Slide 31: Control flow uses RFLAGS register
PC: Program counter
  Store memory address of next instruction
  Also called “RIP” in x86_64
IR: instruction register
  Store the fetched instruction
General purpose registers:
  Store operands and pointers used by program
Program status and control register:
  Contain status of the instruction executed
  All called “RFLAGS” in x86_64

## Slide 32: How control flow uses RFLAGS register
RFLAGS is a special purpose register
Different bits represent different status flags
Certain instructions set status flags
  Regular arithmetic instructions
  Special flag-setting instructions: cmp, test, set
jmp instructions use flags to determine value of %rip

## Slide 33: EFLAGS register: ZF
ZF (Zero Flag):
  Set if the result of the instruction is zero; cleared otherwise.
movq $2, %rax
subq $2, %rax

## Slide 34: EFLAGS register: SF
SF (Sign Flag):
  Set to be the most-significant bit of the result.
movq $2, %rax
subq $10, %rax

## Slide 35: EFLAGS register: CF
CF (Carry Flag):
  Set if adding/subtracting two numbers carries out of MSB
movq $0xffffffffffffffff, %rax
addq $2, %rax
movq $0, %rax
subq $1, %rax
i.e. Set if overflow for unsigned integer arithmetic

## Slide 36: EFLAGS register: OF
OF (Overflow Flag):
  Set if there is carry-in but no carry-out of MSB
  or, there is no carry-in but there's carry-out of MSB
movq $0x7fffffffffffffff, %rax
addq $1, %rax
movq $0x8000000000000000, %rax
addq $0xffffffffffffffff, %rax
Set if overflow for signed integer (2’s complement) arithmetic.

## Slide 37: CF and OF are different flags
CPU does care if data represents signed or unsigned integer:
  Same underlying arithmetic hardware circuitry.
  OF and CF flags are set by examining various carry bits
Up to programmer/compiler to use either CF or OF flag
Notes: http://teaching.idallen.com/dat2343/10f/notes/040_overflow.txt

## Slide 38: Status flags summary
flag | status
ZF (Zero Flag) | set if the result is zero.
SF (Sign Flag) | set if the result is negative.
CF (Carry Flag) | Overflow for unsigned-integer arithmetic
OF (Overflow Flag) | Overflow for signed-integer arithmetic
Set by arithmetic instructions, e.g. add, inc, and, sal
Not set by lea, mov

## Slide 39
Memory
addq %rax, (%rsi)
0xff…ffffff
……
…
CPU
0x00…0060
RIP:
RAX:
0x00…001
0x00…0018
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
%rip
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
ZF:
0
SF:
0
CF:
0
OF:
0
0x00…0068

## Slide 40
Memory
addq %rax, (%rsi)
0x00..0000
……
…
CPU
0x00…0060
RIP:
RAX:
0x00…001
0x00…0018
…
RBX:
RCX:
RDX:
RSI:
RDI:
RSP:
RBP:
%rip
0x00…0058
0x00…0050
0x00…0010
0x00…0018
0x00…0020
0x00…0028
0x00…0030
0x00…0038
0x00…0040
0x00…0048
0x00…0060
ZF:
1
SF:
0
CF:
1
OF:
0
0x00…0068

## Slide 41: Summary
X86 ISA
  %rip, 16 general purpose registers
  mov
  Lea
  Various arithmetic instructions
  RFLAGS: ZF, SF, CF, OF

## Slide 42: Exercises
src | dest | operation | ZF | SF | CF | OF
0xffffffff | 0x1 | addl |  |  |  | 
0xffffffff |  |  |  |  |  | 
0xffffffff |  |  |  |  |  | 
0xffffffff |  |  |  |  |  | 

## Slide 43: Exercises
src | dest | operation | ZF | SF | CF | OF
0xffffffff | 0x1 | addl | 1 | 0 | 1 | 0
0xffffffff | 0x80000000 | addl |  |  |  | 
0xffffffff |  |  |  |  |  | 
0xffffffff |  |  |  |  |  | 

## Slide 44: Exercises
src | dest | operation | ZF | SF | CF | OF
0xffffffff | 0x1 | addl | 1 | 0 | 1 | 0
0xffffffff | 0x80000000 | addl | 0 | 0 | 1 | 1
0xffffffff | 0x80000000 | subl |  |  |  | 
0xffffffff |  |  |  |  |  | 

## Slide 45: Exercises
src | dest | operation | ZF | SF | CF | OF
0xffffffff | 0x1 | addl | 1 | 0 | 1 | 0
0xffffffff | 0x80000000 | addl | 0 | 0 | 1 | 1
0xffffffff | 0x80000000 | subl | 0 | 1 | 1 | 0
0xffffffff | 0x1 | subl |  |  |  | 

## Slide 46: Exercises
src | dest | operation | ZF | SF | CF | OF
0xffffffff | 0x1 | addl | 1 | 0 | 1 | 0
0xffffffff | 0x80000000 | addl | 0 | 0 | 1 | 1
0xffffffff | 0x80000000 | subl | 0 | 1 | 1 | 0
0xffffffff | 0x1 | subl | 0 | 0 | 1 | 0