## Slide 1: Bits, Bytes, Ints
Jinyang Li
Some slides are due to Tiger Wang

## Slide 2: Lesson plan
How computers represent integers in binary formats
  Bit, Byte
How to make binary formats readable to humans
  Hex notation
How computers add/subtract integers
Unsigned vs. signed integer representation

## Slide 3: The language of technology has evolved from analog signals…
Analog signals: smooth and continuous
Analog components: resistors, capacitors, inductors, diodes, etc.
Hard
  Difficult to design
  Susceptible to noise

## Slide 4: … to digital
Digital signals: discrete (0 or 1)
Digital components: transistors, logic gates …
Easier
  Easier to design
  Robust to noise
1 0 1 0 1 0 1 0 1 0 1 0

## Slide 5: Using bits to represent everything
Bit = Binary digit, 0 or 1
A bit is too small to be useful
  A bit has 2 values; the English alphabet has 26 values (characters)
Idea: use a group of bits
  different bit patterns represent different “values”

## Slide 6: Question
How many bit patterns can a group of 2 bits have?
b1
b0
How many bit patterns does a group of n bits have?
Can be
either 0 or 1
All patterns of 2-bits: 00, 01, 10, 11
bn-1bn-2...b1b0
n bits
# of patterns of n-bits: 2n

## Slide 7: Digression: Any self-respecting CS person must memorize powers of 2
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024

## Slide 8
25

## Slide 9
28

## Slide 10: Approximations of powers of 2
210 = 1024
≈
103 (Kilo)
220
≈
103*2 = 106 (Mega)
230
≈
103*3 = 109 (Giga)
240
≈
103*4 = 1012 (Tera)
250
≈
103*5 = 1015 (Peta)

## Slide 11
≈ 2??

## Slide 12: Represent non-negative integer
bits: b1b0
Goal: map each bit pattern to an integer
unsigned
00  0
01  1
10  2
11  3
4 patterns
Range: [0, 3]

## Slide 13: Represent unsigned integer
bi is bit at i-th position (from right to left, starting at i=0)
Base-2 representation:
bn-1bn-2…b2b1b0 =
Bit pattern: bn-1bn-2…b2b1b0
Range: [0, 2n -1]

## Slide 14: Examples
Bit pattern: 00000110
Value: 0*27+0*26+0*25+0*24+0*23+1*22+1*21+0*20 = 6
Bit pattern: 10000110
Value: ?

## Slide 15: Byte
Byte: a fixed size group of bits
  The term is coined by Werner Buchholz (IBM).
  Long long ago, different vendors use different byte sizes
Now: Byte is 8-bit
IBM System/360, 1964
Introduced 8-bit byte
Intel 8080, 1974
Widely adopted
Modern processors
Standardized
Notes: Why byte?

## Slide 16: Byte
00111010
Byte is the smallest unit of information storage, computation and transfer
10101110
11001010
00001110
00011010
Memory
......
CPU
Integers are represented by 1,2,4, or 8 bytes.
Notes: Why byte?

## Slide 17
Range of 1-byte non-negative integers: [0, ??]
Bit-pattern of the largest integer?

## Slide 18
Range of 4-byte non-negative integers: [0, ??]
Bit-pattern of the largest integer?

## Slide 19: Most and least significant bit
MSB: bit position with the largest positional value
LSB: bit position with the smallest positional value
1-byte unsigned int:
10011010
4-byte unsigned int:
01110011 10001101 01010011 11011010
Most significant byte
Least significant byte

## Slide 20: What we’ve learnt so far
Digital information is represented in bits
Byte = 8 bits
Base2 representation of unsigned integers:
  1-byte range: [0, 28-1]
  4-byte range: [0, 232-1]
bn-1bn-2…b2b1b0 =

## Slide 21: Describing bit patterns in a human-readable way
1-byte int: 10101110
unsigned int a = 0b10101110;
If I ask you to type a 4-byte int, …
C program:

## Slide 22: Describing a bit pattern: hex notation
10101110
How many hex symbols are needed?
Use one (hex) symbol to represent
a group of 4 bits
Binary | Hex
1000 | 8
1001 | 9
1010 | a
1011 | b
1100 | c
1101 | d
1110 | e
1111 | f
Binary | Hex
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
unsigned int a = 0xae;
C program:

## Slide 23: Breakout time!

## Slide 24: Breakout exercises
What's the least significant bit of any even number?
Write the hex notation of this 2-byte bit pattern: 1111000011000011
What's the decimal value of unsigned int: 0xff
0
0xf0c2
255

## Slide 25: Lesson plan
How computers represent integers
  Bit, Byte
Hex notation
How computers add/subtract integers
Unsigned vs. signed integer representation

## Slide 26: Unsigned int addition
0 0 0 0 1 0 1 1
0 0 0 0 1 0 1 0
+
0 0 0 1 0 1 0 1
🤔
1 0 0 0 1 0 1 1
1 0 0 0 1 0 1 0
+
0 0 0 1 0 1 0 1
Overflow!

## Slide 27: Unsigned int subtraction
0 0 0 0 1 1 1 0
0 0 0 0 1 0 1 1
-
0 0 0 0 0 0 1 1
🤔
0 0 0 0 1 0 1 0
0 0 0 0 1 0 1 1
-
1 1 1 1 1 1 1 1
Overflow!

## Slide 28
How to represent negative numbers?

## Slide 29: Strawman
Most significant bit (MSB) represents the sign
0 0 0 0 0 0 0 12
1 0 0 0 0 0 0 12
1
-1
0 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
1 0 0 0 0 0 1 0
magnitude
sign
-2 ???
☹Need different h/w for signed
vs. unsigned computation

## Slide 30: Two’s complement
10010110
Unsigned int
= 1*27 + 0*26 + 0*25 + 1*24 + 0*23 + 1*22 + 1*21 + 0*20
Signed int
00010110
= 0*27 + 0*26 + 0*25 + 1*24 + 0*23 + 1*22 + 1*21 + 0*20
10010110
= 1*(-27) +0*26 +0*25 +1*24 +0*23 +1*22 +1*21+0*20
00010110
= 0*(-27) +0*26 +0*25 +1*24 +0*23 +1*22 +1*21+0*20

## Slide 31: Two’s complement
1-byte bit pattern  signed int
Bit pattern | value
00000000 | 0
00000001 | 1
… | …
01111111 | 27-1 = 127
10000000 | -27 = -128
10000001 | -27 +1= -127
… | 
11111111 | -27+(27-1) = -1

## Slide 32: Two’s complement
1-byte bit pattern  signed int
Source: xkcd.com

## Slide 33: Basic facts of 2’s complement
Negative numbers  MSB=1
A sequence of 1’s (e.g. 0xff, 0xffffffff)  -1
Size (bytes) | Bit pattern of smallest | Bit pattern of largest | Range
1 |  |  | 
2 |  |  | 
4 |  |  | 
8 |  |  | 
0x80 | 0x7f | [-27, 27-1]
0x8000 | 0x7fff | [-215, 215-1]
0x80000000 | 0x7fffffff | [-231, 231-1]
0x8000000000000000 | 0x7fffffffffffffff | [-263, 263-1]
Signed int
🤔 Home exercise: make a similar table for unsigned int

## Slide 34: Signed addition on hardware
🤔
0 0 0 0 0 0 0 1
0 0 0 0 0 0 1 1
+
(1)10
(3)10
0 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
(1)10
(-127)10
0 1 0 0 0 0 0 1
0 1 0 0 0 0 0 0
+
(65)10
(64)10
1 0 0 0 0 0 0 1
(-127)10
Overflow!
This is what 2’s complement is designed to accomplish!
1 0 0 0 0 0 0 1
1 1 1 1 1 1 1 0
+
(-127)10
(-2)10
0 1 1 1 1 1 1 1
(127)10
0 0 0 0 0 1 0 0
(4)10
1 0 0 0 0 0 1 0
(-126)10

## Slide 35: Signed subtraction on hardware
0 0 0 0 0 0 0 1
0 0 0 0 0 0 1 1
-
(1)10
(3)10
0 0 0 0 0 0 0 1
1 1 1 1 1 1 1 1
-
(1)10
(-1)10
1 0 0 0 0 0 0 0
0 0 0 0 0 0 0 1
-
(-128)10
(1)10
1 0 0 0 0 0 0 1
(-127)10
Overflow!
This is what 2’s complement is designed to accomplish!
🤔
1 1 1 1 1 1 1 0
(-2)10
0 0 0 0 0 0 1 0
(2)10
0 1 1 1 1 1 1 1
1 1 1 1 1 1 1 0
-
(127)10
(-2)10
0 1 1 1 1 1 1 1
(127)10

## Slide 36: Summary
Integer representation
  Unsigned (base-2)
  Signed (2’s complement)
Hex notation
Operations (e.g. add,subtract) on fixed-width integers can cause overflow