## Slide 1: Bits, Bytes, Ints
Jinyang Li
Slides are based on Tiger Wang’s class

## Slide 2: The world has moved away from analog signal to …
Analog signals: smooth and continuous
Analog components: resistors, capacitors, inductors, diodes, etc.
Problems
  Difficult to design
  Susceptible to noise

## Slide 3: … to digital
Digital signals: discrete (encode sequence of 0s and 1s)
Digital components: transistors, logic gates …
Advantages
  Easier to design
  Robust to noise
1 0 1 0 1 0 1 0 1 0 1 0

## Slide 4: Using bits to represent everything
Bit = Binary digit, 0 or 1
A bit is too small to be very useful
  A bit has 2 values; the English alphabet has 26 values (characters)
Using a group of bits instead of bit
  different bit patterns represent different “values”

## Slide 5: Question
How many values can a group of 2 bits represent?
How many values can a group of n bits represent?
0 | 0
0 | 1
1 | 0
1 | 1
4
2n

## Slide 6: A digression: you must memorize common powers of 2
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024

## Slide 7: Represent non-negative integer
Solution: Base-2 representation
bn-1bn-2…b2b1b0 =
bits: bn-1bn-2…b2b1b0
Question: how to map each bit pattern to a unique integer in [0, ??]?
bi is bit at i-th position (from right to left, starting i=0)
[0, 2n -1]

## Slide 8: Most significant bit (MSB)
The bit position has the greatest value
Bits 01010
MSB ?
Bits 11011010
MSB ?

## Slide 9: Most significant bit (MSB)
The bit position has the greatest value
  The leftmost bit
Bits 01010
MSB 0
Bits 11011010
MSB 1

## Slide 10: Least significant bit (LSB)
The bit position has the least value
  The rightmost bit
Bits 01010
MSB 0
Bits 11011010
MSB 0
Notes: xxd -b 01-example1.c

## Slide 11: Examples
Bits 0110
Value 0*23 + 1*22 + 1*21 + 0*20 = 6
Bits 1110
Value ?
1*23+1*22+1*21+0*20 = 14

## Slide 12: Byte
Byte: Basic unit of computation and storage
  The term is coined by Dr. Werner Buchholz (IBM).
  Byte sizes from 1 bit to 48 bits have been used in the history
Notes: Why byte?

## Slide 13: Byte
0100
1111
0000
1000
1010
0011
1101
1010
Memory
CPU
Arithmetic Logic Unit
0011
Memory is a continuous array.
Each unit is a byte.
1 Byte is the smallest information
CPU can fetch from memory
(One cannot fetch just 1 bit)
Notes: Why byte?

## Slide 14: Byte – 8 bits chunk
IBM System/360, 1964
Introduce
Intel 8080, 1974
Widely adopted
Modern processors
Standard
Notes: Why byte?

## Slide 15: Your mental model
CPU
Arithmetic Logic Unit
10101110
Each byte has 8 bits
10101110
11001010
00001110
00011010
Memory
......
addresses
addr4
addr3
addr2
addr1
addr1
addresses
Notes: Why byte?

## Slide 16: Range of Single Byte
Maximum
Minimum

## Slide 17: Range of Single Byte
Maximum
  111111112  255
Minimum

## Slide 18: Range of Single Byte
Maximum
  111111112  255
Minimum
  000000002  0

## Slide 19: Describing a bit pattern – intuitive way
How to make a bit pattern human readable?
  Use base-2 notation?
Bits 10101110 11001010 00001110 00011010
4 bytes
15 cm on my laptop

## Slide 20: Describing a bit pattern – strawman
How many decimal digits needed
to represent 1 byte?
How to make a bit pattern human readable?
  Use base-2 notation? Too verbose
  Use base-10 notation?
Bits 10101110 11001010 00001110 00011010
3
Decimal 174 202 014 026
  Conversion from base-2 to base-10 (and vice versa)
  is mentally difficult for humans

## Slide 21: Describing a bit pattern- Hex Notation
Use base-16 (hexadecimal) notation
  Hex “digit” is one of 16 symbols: 0-9, a,b,c,d,e,f
  How many bits needed to represent a hex digit?
4

## Slide 22: Hexadecimal “digit”
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
Hex
Decimal
Binary
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111

## Slide 23: Hex Notation
1 byte = 8 bits = 2 hex digits
Bits 10101110 11001010 00001110 00011010
Decimal 174 202 014 026
Hex
Hex(C)
1010 =

## Slide 24: Hexadecimal Notation
1 byte = 8 bits = 2 hex digits
Bits 10101110 11001010 00001110 00011010
Decimal 174 202 014 026
Hex A
Hex(C)
1010 = 1 * 23 + 0 * 22 + 1 * 2 + 0 = 10 = A16

## Slide 25: Hexadecimal Notation
Bits 10101110 11001010 00001110 00011010
Decimal 174 202 014 026
Hex A
Hex(C)
1110 =
1 byte = 8 bits = 2 hex digits

## Slide 26: Hexadecimal Notation
Bits 10101110 11001010 00001110 00011010
Decimal 174 202 014 026
Hex A E
Hex(C)
1110 = 1 * 23 + 1 * 22 + 1 * 2 + 0 = 14 = E16
1 byte = 8 bits = 2 hex digits

## Slide 27: Hexadecimal Notation
Bits 10101110 11001010 00001110 00011010
Decimal 174 202 014 026
Hex A E
Hex(C)
1100 =
1 byte = 8 bits = 2 hex digits

## Slide 28: Hexadecimal Notation
Bits 10101110 11001010 00001110 00011010
Decimal 174 202 014 026
Hex A E C
Hex(C)
1100 = 1 * 23 + 1 * 22 + 0 * 2 + 0 = 12 = C16
1 byte = 8 bits = 2 hex digits

## Slide 29: Hexadecimal Notation
1 byte = 8 bits = 2 hex digits
Bits 10101110 11001010 00001110 00011010
Decimal 174 202 014 026
Hex A E C
Hex(C)
1010 =

## Slide 30: Hexadecimal Notation
Bits 10101110 11001010 00001110 00011010
Decimal 174 202 014 026
Hex A E C A
Hex(C)
1010 = 1 * 23 + 0 * 22 + 1 * 2 + 0 = 10 = A16
1 byte = 8 bits = 2 hex digits

## Slide 31: Hexadecimal Notation
1 byte = 8 bits = 2 hex digits
Bits 10101110 11001010 00001110 00011010
Decimal 174 202 014 026
Hex A E C A 0
Hex(C)
0000 = 0 * 23 + 0 * 22 + 0 * 2 + 0 = 0 = 016

## Slide 32: Hexadecimal Notation
Bits 10101110 11001010 00001110 00011010
Decimal 174 202 014 026
Hex A E C A 0 E
Hex(C)
1110 = 1 * 23 + 1 * 22 + 1 * 2 + 0 = 14 = E16
1 byte = 8 bits = 2 hex digits

## Slide 33: Hexadecimal Notation
1 byte = 8 bits = 2 hex digits
Bits 10101110 11001010 00001110 00011010
Decimal 174 202 014 026
Hex A E C A 0 E 1
Hex(C)
0001 = 0 * 23 + 0 * 22 + 0 * 2 + 1 = 1 = 116

## Slide 34: Hexadecimal Notation
Bits 10101110 11001010 00001110 00011010
Decimal 174 202 014 026
Hex A E C A 0 E 1 A
Hex(C)
1010 = 1 * 23 + 0 * 22 + 1 * 2 + 0 = 10 = A16
1 byte = 8 bits = 2 hex digits

## Slide 35: Hexadecimal Notation
Bits 10101110 11001010 00001110 00011010
Decimal 174 202 014 026
Hex A E C A 0 E 1 A
Hex(C) 0xAECA0E1A
Each byte is represented with 2 hex numbers (0016 -- FF16)

## Slide 36: Exercises Time
Hexadecimal | Decimal | Binary
 |  | 1010 0111
 |  | 0011 1110
0xBC |  | 
 | 55 | 
0xF3 |  | 

## Slide 37: Answers
Hexadecimal | Decimal | Binary
0xA7 | 10*16 + 7 = 167 | 1010 0111
0x3E | 3*16 + 14 = 62 | 0011 1110
0xBC | 11*16 + 12 = 188 | 1011 1100
0x37 | 3*16+7=55 | 0011 0111
0xF3 | 15*16+3=243 | 1111 0011

## Slide 38: Unsigned addition
11 + 10
0xB + 0xA
000010112 + 000010102

## Slide 39: Unsigned addition
11 + 10
0xB + 0xA
000010112 + 000010102
0 0 0 0 1 0 1 1
0 0 0 0 1 0 1 0
+

## Slide 40: Unsigned addition
11 + 10
0xB + 0xA
000010112 + 000010102
0 0 0 0 1 0 1 1
0 0 0 0 1 0 1 0
+
1

## Slide 41: Unsigned addition
11 + 10
0xB + 0xA
000010112 + 000010102
0 0 0 0 1 0 1 1
0 0 0 0 1 0 1 0
+
2 1

## Slide 42: Unsigned addition
11 + 10
0xB + 0xA
000010112 + 000010102
0 0 0 0 1 0 1 1
0 0 0 0 1 0 1 0
+
0 1
1

## Slide 43: Unsigned addition
11 + 10
0xB + 0xA
000010112 + 000010102
0 0 0 0 1 0 1 1
0 0 0 0 1 0 1 0
+
1 0 1
1

## Slide 44: Unsigned addition
11 + 10
0xB + 0xA
000010112 + 000010102
0 0 0 0 1 0 1 1
0 0 0 0 1 0 1 0
+
0 0 0 1 0 1 0 1

## Slide 45: Unsigned subtraction
11 - 10
0xB - 0xA
000010112 - 000010102
0 0 0 0 1 0 1 1
0 0 0 0 1 0 1 0
-
0 0 0 0 0 0 0 1

## Slide 46: Unsigned subtraction
11 - 10
0xB - 0xA
000010112 - 000010102
0 0 0 0 1 0 1 1
0 0 0 0 1 0 1 0
-
0 0 0 0 0 0 0 1

## Slide 47: Unsigned subtraction
10 - 11
0xA – 0xB
000010102 - 000010112
0 0 0 0 1 0 1 0
0 0 0 0 1 0 1 1
-
? ? ?

## Slide 48
Question:
How to represent negative numbers?

## Slide 49: Strawman
Most significant bit (MSB) represent the sign
0 0 0 0 0 0 0 12
1 0 0 0 0 0 0 12
1
-1
0 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+

## Slide 50: Strawman
Most significant bit (MSB) represent the sign
0 0 0 0 0 0 0 12
1 0 0 0 0 0 0 12
1
-1
0 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
1 0 0 0 0 0 1 0

## Slide 51: Strawman
Most significant bit (MSB) represent the sign
0 0 0 0 0 0 0 12
1 0 0 0 0 0 0 12
1
-1
0 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
1 0 0 0 0 0 1 0
-2 ???

## Slide 52: Two’s complement
Byte 10010110
Unsigned number
1 * 27 + 0 * 26 + 0 * 25 + 1 * 24 + 0 * 23 + 1 * 22 + 1 * 2 + 0 * 20

## Slide 53: Two’s complement
Byte 10010110
Unsigned number
1 * 27 + 0 * 26 + 0 * 25 + 1 * 24 + 0 * 23 + 1 * 22 + 1 * 2 + 0 * 20
Signed number
-1 * 27 + 0 * 26 + 0 * 25 + 1 * 24 + 0 * 23 + 1 * 22 + 1 * 2 + 0 * 20

## Slide 54: Two’s complement
MSB: val( bw ) = -bw * 2w
Other: val ( bi ) = bi * 2i, 0 <= i < w

## Slide 55: Two’s complement
Binary |  | Value
1000 0001 |  | 
1010 0101 |  | 
0101 0101 |  | 

## Slide 56: Two’s complement
Binary |  | Value
1000 0001 | -1 * 27 + 1 | -127
1010 0101 |  | 
0101 0101 |  | 

## Slide 57: Two’s complement
Binary |  | Value
1000 0001 | -1 * 27 + 1 | -127
1010 0101 | -1 * 27 + 25 + 22 + 20 | -91
0101 0101 |  | 

## Slide 58: Two’s complement
Binary |  | Value
1000 0001 | -1 * 27 + 1 | -127
1010 0101 | -1 * 27 + 25 + 22 + 20 | -91
0101 0101 | 26 + 24 + 22 + 2 | 85

## Slide 59: Two’s complement
0 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
1 0 0 0 0 0 1 0

## Slide 60: Two’s complement
0 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
1 0 0 0 0 0 1 0
-127
1
-126
-1 * 27 + 20
20
-1 * 27 + 21

## Slide 61: Find 2’s complement quickly
With a negative number, how to give its binary representation? e.g. -40

## Slide 62: Find 2’s complement quickly
With a negative number, how to give its binary representation? e.g. -40
Step 1. represent 40 in binary
0010 1000

## Slide 63: Find 2’s complement quickly
With a negative number, how to give its binary representation? e.g. -40
Step 2. flip all bits
0010 1000
1101 0111

## Slide 64: Find 2’s complement quickly
With a negative number, how to give its binary representation? e.g. -40
Step 3. add 1
0010 1000
1101 0111
1101 1000

## Slide 65: Find 2’s complement quickly
With a negative number, how to give its binary representation? e.g. -40
Step 3. add 1
0010 1000
1101 0111
1101 1000
0010 1000
1101 0111
+
1111 1111

## Slide 66: Find 2’s complement quickly
With a negative number, how to give its binary representation? e.g. -40
Step 3. add 1
0010 1000
1101 0111
1101 1000
0010 1000
1101 0111
+
1
1 0000 0000

## Slide 67: Why does this trick work
What is 1111...112 in 2’s complement?
b with bits flipped

## Slide 68: Exercise Time II
Hexadecimal | Decimal | Binary
0xce |  | 
 |  | 1001 1100
 | 127 | 
 | -128 | 
 | -90 | 

## Slide 69: Answers
Hexadecimal | Decimal | Binary
0xce | -50 | 1100 1110
0x9c | -100 | 1001 1100
0x7f | 127 | 0111 1111
0x80 | -128 | 1000 0000
0xa6 | -90 | 1010 0110

## Slide 70: Ranges
 | Range | Min | Max
1 byte unsigned | [0, 28 – 1] | 0 | 255
1 byte signed |  |  | 

## Slide 71: Ranges
 | Range | Min | Max
1 byte unsigned | [0, 28 – 1] | 0 | 255
1 byte signed | [-27, 27 – 1] | -128 | 127
Min: 1000 0000
Max: 0111 1111

## Slide 72: Overflow
1 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
-127
-127
 | Range | Min | Max
1 byte unsigned | [0, 28 – 1] | 0 | 255
1 byte signed | [-27, 27 – 1] | -128 | 127

## Slide 73: Overflow
1 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
0 0 0 0 0 0 1 0
-127
-127
1
2 ???
 | Range | Min | Max
1 byte unsigned | [0, 28 – 1] | 0 | 255
1 byte signed | [-27, 27 – 1] | -128 | 127

## Slide 74: Intel 8080
0x4c
0x4c
0x1e
0xaf
0x0f
Memory
0xcb
0xea
0xba
0x00
0xff
0x8c
……
0xb0
0xa9
…
0xa1
0xa2
0xa3
0xa4
0xa5
0xa6
0xa7
0xa8
CPU
0x4c
registers
Arithmetic Logic
Unit

## Slide 75: Intel 8080
CPU
0x4c
0x4c
0x1e
0xaf
0x0f
Memory
0xcb
0xea
0xba
0x00
0xff
0x8c
……
0x4c
Arithmetic Logic
Unit
registers
0xb0
0xa9
…
0xa1
0xa2
0xa3
0xa4
0xa5
0xa6
0xa7
0xa8
8 bits machine – 8 bits length of
Memory – processor transfer
CPU Register
Memory Address
Instruction

## Slide 76: Intel 386
CPU
0x4c1eaf0f
0x4c
0x1e
0xaf
0x0f
Memory
0xcb
0xea
0xba
0x00
0xff
0x8c
……
0x4c1eaf0f
Arithmetic Logic
Unit
registers
0x000000b0
0x000000a9
…
0x000000a1
0x000000a2
0x000000a3
0x000000a4
0x000000a5
0x000000a6
0x000000a7
0x000000a8
32 bits machine – 32 bits length of
Memory – processor transfer
CPU Register
Memory Address
Instruction

## Slide 77: Intel Opteron  i7
CPU
0x00bacbea4c1eaf0f
0x4c
0x1e
0xaf
0x0f
Memory
0xcb
0xea
0xba
0x00
0xff
0x8c
……
0x00bacbea4c1eaf0f
Arithmetic Logic Unit
registers
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
64 bits machine – 64 bits length of
Memory – processor transfer
CPU Register
Memory Address
Instruction

## Slide 78: Intel Opteron  i7
CPU
0x00bacbea4c1eaf0f
0x4c
0x1e
0xaf
0x0f
Memory
0xcb
0xea
0xba
0x00
0xff
0x8c
……
0x00bacbea4c1eaf0f
Arithmetic Logic Unit
registers
Word
Memory – processor transfer
CPU Register
Memory Address
Instruction
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8

## Slide 79: Word
Definition
  Fixed size of data handled as a unit by the instruction set or processor
Length
  8 for 8 bits machine
  32 for 32 bits machine
  64 for 64 bits machine

## Slide 80: Wrapping up last lecture
What you have learnt:
  information as bits
  byte: 8-bit
  how to represent unsigned/signed integer
    Computers use fixed-width representation (1, 2, 4, 8 bytes)
    overflow
  32-bit vs. 64-bit computer architecture
Wrapping up:
  C’s integer data types
  How multi-byte integers are stored in memory

## Slide 81: C’s integral data types on 64 bits machine
 | Length | Min | Max
[signed] char | 1 byte | -27 | 27 - 1
unsigned char | 1 byte | 0 | 28 - 1
short | 2 bytes |  | 
unsigned short | 2 bytes |  | 
int | 4 bytes |  | 
unsigned int | 4 bytes |  | 
long | 8 bytes |  | 
unsigned long | 8 bytes |  | 

## Slide 82: Integral data types on 64 bits machine
 | Length | Min | Max
[signed] char | 1 byte | -27 | 27 - 1
unsigned char | 1 byte | 0 | 28 - 1
short | 2 bytes | -215 | 215 - 1
unsigned short | 2 bytes | 0 | 216 - 1
int | 4 bytes |  | 
unsigned int | 4 bytes |  | 
long | 8 bytes |  | 
unsigned long | 8 bytes |  | 

## Slide 83: Integral data types on 64 bits machine
 | Length | Min | Max
[signed] char | 1 byte | -27 | 27 - 1
unsigned char | 1 byte | 0 | 28 - 1
short | 2 bytes | -215 | 215 - 1
unsigned short | 2 bytes | 0 | 216 - 1
int | 4 bytes | -231 | 231 - 1
unsigned int | 4 bytes | 0 | 232 - 1
long | 8 bytes |  | 
unsigned long | 8 bytes |  | 

## Slide 84: Integral data types on 64 bits machine
 | Length | Min | Max
[signed] char | 1 byte | -27 | 27 - 1
unsigned char | 1 byte | 0 | 28 - 1
short | 2 bytes | -215 | 215 - 1
unsigned short | 2 bytes | 0 | 216 - 1
int | 4 bytes | -231 | 231 - 1
unsigned int | 4 bytes | 0 | 232 - 1
long | 8 bytes | -263 | 263 - 1
unsigned long | 8 bytes | 0 | 264 - 1

## Slide 85: Your first C program
#include <stdio.h>
int
main()
{
char x = -127;
char y = 0x81;
char z = x + y;
printf(“hello world sum is %d\n”, z);
}
$ gcc helloworld.c
$ ./a.out
1 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
0 0 0 0 0 0 1 0
-127
-127
1
2

## Slide 86: Memory layout for multi-byte integers
CPU
Memory
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address: 0x00…00a2
int a

## Slide 87: Memory layout for multi-byte integers: 2 ways
CPU
Memory
0x78
0x56
0x34
0x12
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address: 0x00…00a2
int a

## Slide 88: Memory layout for multi-byte integers: 2 ways
CPU
Memory
0x12
0x34
0x56
0x78
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address: 0x00…00a2
int a

## Slide 89: Memory layout – Little Endian
CPU
Memory
0x12
0x34
0x56
0x78
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address: 0x00…00a2
int a
  Least significant byte in smallest address,
  e.g, laptops, and server machines

## Slide 90: Advantages of Little Endian
0x12345678
0x12131415
+
Processor performs the calculation
from the least significant bit
Processor can simultaneously
perform memory transfer and
calculation.

## Slide 91: Advantages of Little Endian
CPU
Memory
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address of variable a: 0x00…00a2
int a

## Slide 92: Advantages of Little Endian
CPU
Memory
0x12
0x34
0x56
0x78
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address: 0x00…00a2
int a

## Slide 93: Advantages of Little Endian
CPU
Memory
0x12
0x34
0x56
0x78
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address: 0x00…00a2
int a
short b = (short)a
Directly get the data from
0x00…00a2
short b

## Slide 94: Memory layout – Big Endian
CPU
Memory
0x78
0x56
0x34
0x12
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
address: 0x00…00a2
int a
  Most significant byte in smallest address,
  e.g, ARM architecture >v3 (cellphones, ipads)

## Slide 95: Advantages of Big Endian
Test whether the number is positive or negative by looking at the byte at offset zero.