## Slide 1: Bits, Bytes, Ints
Jinyang Li
Some slides are due to Tiger Wang

## Slide 2: Lesson plan
How computers represent integers in binary formats
  Bit, Byte
How to make binary formats readable to humans
  Hex notation
How computers add/subtract integers
Unsigned vs. signed integer representation

## Slide 3: The language of technology has evolved from analog signals…
Analog signals: smooth and continuous
Analog components: resistors, capacitors, inductors, diodes, etc.
Hard
  Difficult to design
  Susceptible to noise

## Slide 4: … to digital
Digital signals: discrete (0 or 1)
Digital components: transistors, logic gates …
Easier
  Easier to design
  Robust to noise
1 0 1 0 1 0 1 0 1 0 1 0

## Slide 5: Using bits to represent everything
Bit = Binary digit, 0 or 1
A bit is too small to be useful
  A bit has 2 values; the English alphabet has 26 values (characters)
Idea: use a group of bits
  different bit patterns represent different “values”

## Slide 6: Question
How many bit patterns can a group of 2 bits have?
b1
b0
How many bit patterns does a group of n bits have?
Can be
either 0 or 1
All patterns of 2-bits: 00, 01, 10, 11
bn-1bn-2...b1b0
n bits
# of patterns of n-bits: 2n

## Slide 7: Digression: All self-respecting CS students should memorize powers of 2
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024

## Slide 8
25

## Slide 9
28

## Slide 10: Approximations of powers of 2
210 = 1024
≈
103 (Kilo)
220
≈
103*2 = 106 (Mega)
230
≈
103*3 = 109 (Giga)
240
≈
103*4 = 1012 (Tera)
250
≈
103*5 = 1015 (Peta)

## Slide 11
≈ 2??

## Slide 12: Represent non-negative integer
bits: b1b0
Goal: map each bit pattern to an integer
unsigned
00  0
01  1
10  2
11  3
4 patterns
Range: [0, 3]

## Slide 13: Represent unsigned integer
bi is bit at i-th position (from right to left, starting at i=0)
Base-2 representation:
bn-1bn-2…b2b1b0 =
Bit pattern: bn-1bn-2…b2b1b0
Range: [0, 2n -1]

## Slide 14: Examples
Bit pattern: 00000110
Value: 0*27+0*26+0*25+0*24+0*23+1*22+1*21+0*20 = 6
Bit pattern: 10000110
Value: ?
Notes: 128+4+2 = 134

## Slide 15: Byte
Byte: a fixed size group of bits
  The term is coined by Werner Buchholz (IBM).
  Long long ago, different vendors use different byte sizes
Now: Byte is 8-bit
IBM System/360, 1964
Introduced 8-bit byte
Intel 8080, 1974
Widely adopted
Modern processors
Standardized
Notes: Why byte?

## Slide 16: Byte
00111010
Byte is the smallest unit of information storage, computation and transfer
10101110
11001010
00001110
00011010
Memory
......
CPU
Integers are represented by 1,2,4, or 8 bytes.
Notes: Why byte?

## Slide 17
Range of 1-byte non-negative integers: [0, ??]
Bit-pattern of the largest integer?

## Slide 18
Range of 4-byte non-negative integers: [0, ??]
Bit-pattern of the largest integer?

## Slide 19: Most and least significant bit
MSB: bit position with the largest positional value
LSB: bit position with the smallest positional value
1-byte unsigned int:
10011010
4-byte unsigned int:
01110011 10001101 01010011 11011010
Most significant byte
Least significant byte

## Slide 20: Describing bit patterns in a human-readable way
1-byte int: 10101110
unsigned int a = 0b10101110;
If I ask you to type a 4-byte int, …
C program:

## Slide 21: Describing a bit pattern: hex notation
10101110
How many hex symbols are needed?
Use one (hex) symbol to represent
a group of 4 bits
Binary | Hex
1000 | 8
1001 | 9
1010 | a
1011 | b
1100 | c
1101 | d
1110 | e
1111 | f
Binary | Hex
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
unsigned int a = 0xae;
C program:

## Slide 22: Breakout time!

## Slide 23: Breakout exercises
What's the least significant bit of any even number?
Write the hex notation of this 2-byte bit pattern: 1111000011000011
What's the decimal value of unsigned int: 0xff
0
0xf0c2
255

## Slide 24: What have we learnt
How computers represent integers
  Bit, Byte
Hex notation
Q: What is 10001111 in decimal?
Q: What is 10001111 in hex?
A: 143
A: 0x8F
Q: What's the least significant bit of any even number?

## Slide 25: Lesson plan
How computers represent integers
  Bit, Byte
Hex notation
How computers add/subtract integers
Signed integer representation
  2’s complement
A short history of processors:
  from 8-bit to 64-bit machines
Byte ordering: big vs. small endian

## Slide 26: Unsigned int addition
0 0 0 0 1 0 1 1
0 0 0 0 1 0 1 0
+
0 0 0 1 0 1 0 1
1 0 0 0 1 0 1 1
1 0 0 0 1 0 1 0
+
0 0 0 1 0 1 0 1
Overflow!
Grade school
method

## Slide 27: Unsigned int subtraction
0 0 0 0 1 1 1 0
0 0 0 0 1 0 1 1
-
0 0 0 0 0 0 1 1
0 0 0 0 1 0 1 0
0 0 0 0 1 0 1 1
-
???
Grade school
method
🤔
How to represent
negative numbers?

## Slide 28: Represent negative numbers: a strawman
Most significant bit (MSB) represents the sign
0 0 0 0 0 0 0 12
1 0 0 0 0 0 0 12
1
-1
0 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
1 0 0 0 0 0 1 0
magnitude
sign
-2 ???
☹Need different h/w for signed
vs. unsigned computation

## Slide 29: Two’s complement
10010110
Unsigned int
= 1*27 + 0*26 + 0*25 + 1*24 + 0*23 + 1*22 + 1*21 + 0*20
Signed int
00010110
= 0*27 + 0*26 + 0*25 + 1*24 + 0*23 + 1*22 + 1*21 + 0*20
10010110
= 1*(-27) +0*26 +0*25 +1*24 +0*23 +1*22 +1*21+0*20
00010110
= 0*(-27) +0*26 +0*25 +1*24 +0*23 +1*22 +1*21+0*20

## Slide 30: Two’s complement
1-byte bit pattern  signed int
Bit pattern | value
00000000 | 0
00000001 | 1
… | …
01111111 | 27-1 = 127
10000000 | -27 = -128
10000001 | -27 +1= -127
… | 
11111111 | -27+(27-1) = -1

## Slide 31: Two’s complement
?-byte bit pattern  signed int
Source: xkcd.com

## Slide 32: Basic facts of 2’s complement
Negative numbers  MSB=1
A sequence of 1’s (e.g. 0xff, 0xffffffff)  -1
Size (bytes) | Bit pattern of smallest | Bit pattern of largest | Range
1 |  |  | 
2 |  |  | 
4 |  |  | 
8 |  |  | 
0x80 | 0x7f | [-27, 27-1]
0x8000 | 0x7fff | [-215, 215-1]
0x80000000 | 0x7fffffff | [-231, 231-1]
0x8000000000000000 | 0x7fffffffffffffff | [-263, 263-1]
Signed int
🤔 Home exercise: make a similar table for unsigned int

## Slide 33: Two’s complement: 8-bit signed integer
11011000
= 1*(-27) +1*26 +0*25 +1*24 +1*23 +0*22 +0*21+0*20 = -40
11111111
= -1
01011000
= 0*(-27) +1*26 +0*25 +1*24 +1*23 +0*22 +0*21+0*20 = 88
00000000
= 0
10000000
= -27= -128
01111111
= 27-1= 127

## Slide 34: 2’s complement: find a number’s negation
00101000
(40)10
(-40)10
??
A useful trick to do negation:
Step-1: flip all bits
Step-2: add 1
00101000
(40)10
11010111
+00000001
11011000
(-40)10
Step-1: flip bits
Step-2:

## Slide 35: Why does the negation trick work
b with bits flipped

## Slide 36: Using negation trick to find the bit-pattern of a negative number
The bit pattern of 8-bit signed integer -33?
Answer:
33 = (00100001)2
Apply negation trick: (11011110)2+1=(11011111)2

## Slide 37: Negation trick helps computers do subtraction
(-3)10
0 0 0 0 0 1 0 0
0 0 0 0 0 0 1 1
-
(4)10
(3)10
Instead of doing this:
0 0 0 0 0 1 0 0
(4)10
Do this instead:
0 0 0 0 0 0 1 1
(3)10
1 1 1 1 1 1 0 0
0 0 0 0 0 0 0 1
0 0 0 0 0 0 0 1
(1)10
0 0 0 0 0 0 0 1
(1)10
+
Works for both unsigned and signed subtraction!

## Slide 38: Unsigned addition
🤔
0 0 0 0 0 0 0 1
0 0 0 0 0 0 1 1
+
(1)10
(3)10
0 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
(1)10
(129)10
0 1 0 0 0 0 0 1
0 1 0 0 0 0 0 0
+
(65)10
(64)10
1 0 0 0 0 0 0 1
(129)10
Overflow!
1 0 0 0 0 0 0 1
1 1 1 1 1 1 1 0
+
(129)10
(254)10
0 1 1 1 1 1 1 1
(127)10
0 0 0 0 0 1 0 0
(4)10
1 0 0 0 0 0 1 0
(130)10

## Slide 39: Signed addition
🤔
0 0 0 0 0 0 0 1
0 0 0 0 0 0 1 1
+
(1)10
(3)10
0 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
(1)10
(-127)10
0 1 0 0 0 0 0 1
0 1 0 0 0 0 0 0
+
(65)10
(64)10
1 0 0 0 0 0 0 1
(-127)10
This is what 2’s complement is designed to accomplish!
1 0 0 0 0 0 0 1
1 1 1 1 1 1 1 0
+
(-127)10
(-2)10
0 1 1 1 1 1 1 1
(127)10
0 0 0 0 0 1 0 0
(4)10
1 0 0 0 0 0 1 0
(-126)10
Overflow!
Overflow!

## Slide 40: Unsigned subtraction
0 0 0 0 0 0 0 1
0 0 0 0 0 0 1 1
-
(1)10
(3)10
0 0 0 0 0 0 0 1
1 1 1 1 1 1 1 1
-
(1)10
(255)10
1 0 0 0 0 0 0 0
0 0 0 0 0 0 0 1
-
(128)10
(1)10
1 0 0 0 0 0 0 1
(129)10
🤔
1 1 1 1 1 1 1 0
(254)10
0 0 0 0 0 0 1 0
(2)10
0 1 1 1 1 1 1 1
1 1 1 1 1 1 1 0
-
(127)10
(254)10
0 1 1 1 1 1 1 1
(127)10
Overflow!
Overflow!
Overflow!

## Slide 41: Signed subtraction
0 0 0 0 0 0 0 1
0 0 0 0 0 0 1 1
-
(1)10
(3)10
0 0 0 0 0 0 0 1
1 1 1 1 1 1 1 1
-
(1)10
(-1)10
1 0 0 0 0 0 0 0
0 0 0 0 0 0 0 1
-
(-128)10
(1)10
1 0 0 0 0 0 0 1
(-127)10
🤔
1 1 1 1 1 1 1 0
(-2)10
0 0 0 0 0 0 1 0
(2)10
0 1 1 1 1 1 1 1
1 1 1 1 1 1 1 0
-
(127)10
(-2)10
0 1 1 1 1 1 1 1
(127)10
Overflow!
Overflow!

## Slide 42: Lesson plan
How computers represent integers
  Bit, Byte
Hex notation
How computers add/subtract integers
Signed integer representation
  2’s complement
A short history of processors:
  from 8-bit to 64-bit machines
Byte ordering: big vs. small endian

## Slide 43: The evolution of integer sizes in processors

## Slide 44: 8-bit processors: Intel 8080 (1974)
CPU
0x4c
0x4c
0x1e
0xaf
0x0f
Memory
0xcb
0xea
0xba
0x00
0xff
0x8c
……
0x4c
Arithmetic Logic
Unit
registers
0xb0
0xa9
…
0xa1
0xa2
0xa3
0xa4
0xa5
0xa6
0xa7
0xa8
8 bits machine: 8 bits length of
CPU register
Memory address
Nowadays: 8-bit processor (microcontroller)
Is used for embedded systems

## Slide 45: 32-bit processors: Intel 386 (1985)
CPU
0x4c1eaf0f
0x4c
0x1e
0xaf
0x0f
Memory
0xcb
0xea
0xba
0x00
0xff
0x8c
……
0x4c1eaf0f
Arithmetic Logic
Unit
registers
0x000000b0
0x000000a9
…
0x000000a1
0x000000a2
0x000000a3
0x000000a4
0x000000a5
0x000000a6
0x000000a7
0x000000a8
32 bits machine: 32 bits length of
CPU register
Memory address
Most commonly used desktop/server processors
in the latest 80s to early 00s

## Slide 46: 64-bit processors: Intel Pentium 4 (2000)
CPU
0x00bacbea4c1eaf0f
0x4c
0x1e
0xaf
0x0f
Memory
0xcb
0xea
0xba
0x00
0xff
0x8c
……
0x00bacbea4c1eaf0f
Arithmetic Logic Unit
registers
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
64 bits machine: 64 bits length of
CPU register
Memory address
Nowadays:
Servers/laptops: Intel/AMD 64-bit x86 processors
Mobile phones/tablets: 64-bit ARM processors (made by Apple/Qualcomm/Samsung etc)

## Slide 47: C’s Integer data types on 64-bit machine
 | Length | Min | Max
char | 1 byte | -27 | 27 - 1
unsigned char | 1 byte | 0 | 28 - 1
short | 2 bytes | -215 | 215 - 1
unsigned short | 2 bytes | 0 | 216 - 1
int | 4 bytes | -231 | 231 - 1
unsigned int | 4 bytes | 0 | 232 - 1
long | 8 bytes | -263 | 263 - 1
unsigned long | 8 bytes | 0 | 264 - 1

## Slide 48: Your first C program
#include <stdio.h>
int
main()
{
char x = -127;
char y = 0x81;
char z = x + y;
printf(“hello world sum is %d\n”, z);
}
$ gcc helloworld.c
$ ./a.out
1 0 0 0 0 0 0 1
1 0 0 0 0 0 0 1
+
0 0 0 0 0 0 1 0
-127
-127
1
2

## Slide 49: Memory layout for multi-byte integers
CPU
Memory
……
Arithmetic Logic Unit
registers
0x00…00b0
0x00…00a9
…
0x00…00a1
0x00…00a2
0x00…00a3
0x00…00a4
0x00…00a5
0x00…00a6
0x00…00a7
0x00…00a8
4-byte

## Slide 50: Memory layout: Little Endian
CPU
Memory
0x12
0x34
0x56
0x78
……
Arithmetic Logic Unit
registers
int x = 0x12345678
x:
  Little endian:
  Least significant byte stored at smallest address
  Used in x86 processors (servers/laptops) and most ARM (phones/tablets) implementation
0x12 | 0x34 | 0x56 | 0x78
address of x
addr+1
addr
addr+2
addr+3

## Slide 51: Advantage of Little Endian
0x12345678
0x12131415
+
Processor performs calculation
from the least significant bit
Processor can simultaneously
perform memory transfer and
calculation.

## Slide 52: Another advantage of Little Endian
CPU
Memory
0x12
0x34
0x56
0x78
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678;
…
short b = (short)a;
Casting a larger integer to a smaller one requires no explicit conversion.
a:
b:
addr+1
addr
addr+2
addr+3

## Slide 53: Memory layout: Big Endian
CPU
Memory
0x78
0x56
0x34
0x12
……
…
Arithmetic Logic Unit
registers
int a = 0x12345678;
…
  Big Endian:
  Most significant byte stored at smallest address
  ARM processors (phones/tablets) in principle support both endian
0x12 | 0x34 | 0x56 | 0x78
a:
addr+1
addr
addr+2
addr+3

## Slide 54: Advantages of Big Endian
Quick to test whether the number is positive or negative
  Examine byte stored at the address offset zero.

## Slide 55: Big or Little Endian?
#include <stdio.h>
int main()
{
int x = 0x05060708;
int *p;
p = &x; //p contains the address of x
char y = *(char *)p; //y is the 1-byte value pointed to by p
printf(“y=%d\n”, y);
}
$ gcc endian.c
$ ./a.out

## Slide 56: Summary
Integer representation
  Unsigned (base-2)
  Signed (2’s complement)
Hex notation
Operations (e.g. add,subtract) on fixed-width integers can cause overflow
Big vs. little endian