## Slide 1: Architecture: Overview and Basic Logic Design
Jinyang Li

## Slide 2: What we’ve learnt so far
Hardware
Software
Logical Circuits, Flip-Flops, Gates, …
CPU
Memory
I/O
Operating System
Apps

## Slide 3: What we’ve learnt so far
High level language program
(e.g. C)
Assembly program
(e.g. x86)
Machine language program
(e.g. x86)
Software
Hardware
tmp = a
a = b
b = tmp
tmp = a
a = b
b = tmp
tmp = a
a = b
b = tmp

## Slide 4: Today’s lecture plan
Computer Hardware Basic
  CPU, memory, I/O devices
  Moore’s law
Basics of Logic design

## Slide 5: Computer hardware under the cover
CPU
Memory
Input/Output devices
Major components
of a computer

## Slide 6: Computer hardware under the cover
CPU
Memory
Input/Output devices
Major components of a computer
1 rack-mountable server
Many racks full of rack-mountable servers
(data center)

## Slide 7: Computer hardware under the cover
CPU
Memory
Major components
of a computer
Network card
Input/Output devices
Solid state vs magnetic disk
LCD monitor
(various brands)
16GB for $100

## Slide 8: Teardown of a packaged computer

## Slide 9: Teardown of a packaged computer

## Slide 10: Teardown of a packaged computer
heat sink and cooling fan
If you peel away that fan….

## Slide 11: Teardown of a packaged computer
Intel® Core™ i7-5500U 3GHz processor
Thermal paste makes the CPU hard to see

## Slide 12: Teardown of a packaged computer
Micron 8GB memory

## Slide 13: Teardown of a packaged computer
Hard-drive

## Slide 14: Teardown of a packaged computer
Wireless card

## Slide 15
An off/off switch controlled by electricity
Combine numerous transistors on a single chip
Technological trend: exponential growth
CSO will focus on CPU and memory

## Slide 16
Moore’s Law:
Transistor count
doubles every 2 years
Moore’s Law in CPU

## Slide 17
Moore’s Law in memory

## Slide 18: Today’s lecture plan
Computer Hardware Basic
  CPU, memory, I/O devices
  Moore’s law
Basics of Logic design

## Slide 19: Digital Computer
Operate with only two voltage levels: high/low
  that’s why computers work with binary numbers
The clock signal
  “heartbeat” of the system

## Slide 20: Digital Signals
Clock

## Slide 21: Digital signals

## Slide 22: Basic element of implementation: switches
Close switch (if A is “1” or asserted)  light bulb is on (Z)
A
Z
Open switch (if A is “0” or unasserted)  light bulb is off (Z)
Z  A
A
Z

## Slide 23: Basic element of implementation: switches
AND
OR
Z  A and B
Z  A or B
A
B
A
B
Compose switches into more complex ones (Boolean functions):
Modern digital systems are done in CMOS transistors

## Slide 24: Transistors act as switches
Modern digital systems are implemented using CMOS transistors
MOS transistors act as voltage-controlled switches
Bardeen, Shockley and Brattain at Bell Labs, 1948

## Slide 25: Historical Note
Early computer are built from ad hoc circuits
Common patterns emerge: ANDs, ORs, …
Claude Shannon made the link to work of 19th century mathematician George Boole
  Called it “Boolean” in his honor
Shannon
Boole

## Slide 26: Gates: building blocks made from small groups of transistors

## Slide 27: More gates
XOR
a
b
c
NAND
NOR

## Slide 28: Boolean Algebra
Express (logic) functions with (logic) equations
  AB (AND), A+B (OR), Ā (NOT)
Laws of Boolean algebra:
  Basic:
  Inverse:
  Commutativity:
  Associativity:
  Distribution:

## Slide 29: Boolean Algebra

## Slide 30: Boolean Algebra
Method 1: Compare Truth Table

## Slide 31: Boolean Algebra
Method 2: Simplify using basic laws

## Slide 32: Logic circuits == Boolean algebra
What is the Boolean expression?

## Slide 33: Logic circuits == Boolean algebra
What is the Boolean expression?

## Slide 34: Two types of logic circuit
Combinatorial circuit
  output is dependent only on the input
Sequential circuit
  output is dependent on both input and state (memory)

## Slide 35: How to implement any CL
Implement a function with AND/OR/NOT
Step1: obtain truth tables
E.g.: Count # of 1’s in 3-bit inputs

## Slide 36: How to implement any CL
Implement a function with AND/OR/NOT
E.g.: Count # of 1’s in 3-bit inputs

## Slide 37: How to implement any CL
Implement a function with AND/OR/NOT
E.g.: Count # of 1’s in 3-bit inputs

## Slide 38: How to implement any CL
Implement a function with AND/OR/NOT
Step 1: Write truth table
E.g.: Count # of 1’s in 3-bit inputs

## Slide 39: How to implement any CL
Implement a function with AND/OR/NOT
Step 2: Find sum of product
E.g.: Count # of 1’s in 3-bit inputs

## Slide 40: How to implement any CL
A
B
C

## Slide 41: How to implement any CL
Implement a function with AND/OR/NOT
Step 2: Find sum of product
E.g.: Count # of 1’s in 3-bit inputs

## Slide 42: How to implement any CL
A
B
C

## Slide 43: PLA (Programmable Logic Array)

## Slide 44: Common CL: decoder
a1 | a0 | out3 | out2 | out1 | out0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
decoder
2
out3
out2
out1
out0

## Slide 45: Common CL: decoder
a0
a1
out0
out1
out2
out3
decoder
2
out3
out2
out1
out0

## Slide 46: Common CL: Multiplexor
Select among a set of inputs based on control
Mux
2
S
in3
in2
in1
in0
out
s1 | s0 | in3 | in2 | in1 | in0 | out
0 | 0 | x | x | x | 0 | 0
0 | 0 | x | x | x | 1 | 1
0 | 1 | x | x | 0 | x | 0
0 | 1 | x | x | 1 | x | 1
1 | 0 | x | 0 | x | x | 0
1 | 0 | x | 1 | x | x | 1
1 | 1 | 0 | x | x | x | 0
1 | 1 | 1 | x | x | x | 1

## Slide 47: Common CL: Multiplexor
Select among a set of inputs based on control
Mux
2
S
in3
in2
in1
in0
out
out
in3
in2
in1
in0
decoder
s0
s1