## Slide 1: Floats (continued) Intro to C programming

## Slide 2: Lesson plan
Rounding
FP operations and caveats
C programming: overview
C programming: bitwise operators

## Slide 3: IEEE Floating Point
±0
Denormalized numbers
Normalized numbers
+M * 2E
s | exp = E + 127 | fraction (F)
31
30
23
22
0
Normalized Encoding:
1 <= M < 2, M = ( 1.F )2
s | exp =0000 0000 | fraction (F)
31
30
23
22
0
Denormalized Encoding:
0 <= M < 1, M = ( 0.F )2
E = 1 – bias = -126
2-126
-2-126
0 0….01 0…00

## Slide 4: FP: Rounding
  What if the result of computation is at ?
Values that are represented precisely
Rounding: Use the “closest” representable value x’ for x.
  4 modes:
  Round-down
  Round-up
  Round-toward-zero
  Round-to-nearest (Round-to-even in text book)

## Slide 5: Round down vs. round up
-0.875
-0.75
0.5
0.625
Round(x) = x- (x-<= x)
Round down rounds to the left
0
Round up rounds to the right
Round(x) = x+ (x+>= x)

## Slide 6: Round towards zero
-0.875
-0.75
0.5
0.625
Round(x) = x- if x < 0
Rounds to the left if x >0
Rounds to the right if x < 0
Round(x) = x+ if x < 0
0

## Slide 7: Round to nearest; ties to even
-0.875
-0.75
0.5
0.625
Round to the right if x+ is nearer to x than x-
0
Round to the left if x- is nearer to x than x+
In case of a tie, the one with its least significant bit equal to zero is chosen.

## Slide 8: IEEE FP: single vs. double precision
s | exp=E+127 | frac
31
30
23
22
0
single precision
(32 bits)
s | exp=E+1023 | frac
63
62
52
51
0
double precision
(64 bits)
float f = 0.1;
double d = 0.1;
C program:
What’s the highest precision? (aka intervals between two denormalized numbers?)
What’s the largest positive FP?
Notes: Smallest denormalized 0
Next smallest denormalized?
Exp=00000000 E=1-bias=-126
Frac=0….001 M=0.00….01 = 2^-23
Final number = 2^{-23}*2^{-126} = 2^-149
Exp=000…00 E=1-bias = -1022
Frac = 00…1 M=0.000…01 = 2^{-52}
Single precision
Exp=1111 1110 Frac=11…1
E = 254-127=127 M=1.1….1 = 2-2^-23 \approx. 2 = 1.1…1 + 0.00..01 = (10)_2 = (2)_10
Double precision
E = 1023 M = \approx. 2

## Slide 9: IEEE FP: single vs. double precision
s | exp=E+127 | frac
31
30
23
22
0
single precision
(32 bits)
s | exp=E+1023 | frac
63
62
52
51
0
double precision
(64 bits)
float f = 0.1;
double d = 0.1;
C program:
What’s the highest precision? (aka intervals between two denormalized numbers?)
  (single) 2-149 (double) 2-1045
What’s the largest positive FP?
  (single) ≈2128 (double) ≈21024

## Slide 10: How does CPU know if data is FP or integer ?
CPU has separate registers for FPs and integers.
CPU uses different instructions for FPs and integer operations.
Interpret as signed int: -231+1
4-byte data: 0x80000001
Interpret as IEEE single-precision FP: -2-149

## Slide 11: Floating point operations
Addition, subtraction, multiplication, division etc.
Invalid operations (resulting in NaN):
  0/0
  sqrt(-1)
  +
Divide by zero: x/0
Caveats:
  Overflow: Outside the range
  Underflow: 0 < result < smallest denormalized value
  Inexact: due to rounding

## Slide 12: Why divide by zero = ?
Allow a calculation to continue and produce a valid result
Example:
If R1 or R2 is 0, overall resistance should be 0

## Slide 13: Floating point addition
Commutative? x+y == y+x?
Associative? (x+y)+z = x + (y+z)?
  Rounding:
  (3.14+1e10)-1e10 = 0
  3.14+(1e10-1e10) = 3.14
  Overflow
Every number has an additive inverse?
  Yes, by flipping the sign.

## Slide 14: Floating point multiplication
Commutative? x* y == y*x?
Associative? (x*y)*z = x * (y*z)?
  Overflow:
  (1e20*1e20)*1e-20= inf, 1e20*(1e20*1e-20)= 1e20
  Rounding
Distributive? (x+y)*z = x*z + y*z?
  1e20*(1e20-1e20)= 0.0, 1e20*1e20 – 1e20*1e20 = NaN

## Slide 15: FP precision decreases as value gets larger
Storing time in computer games as a FP?
Precision diminishes as time gets bigger
FP value (decimal) | Time value | FP precision | Time precision
1 | 1 sec | 1.19E-07 | 119 nanoseconds
100 | ~1.5 min | 7.63E-06 | 7.63 microseconds
10 000 | ~3 hours | 0.000977 | .976 milliseconds
1000 000 | ~11 days | 0.0625 | 62.5 milliseconds

## Slide 16: Floating point in the real world
Using floating point to measure distances
FP value | Length | FP precision | Precision size
1 | 1 meter | 1.19E-07 | Virus
100 | 100 meter | 7.63E-06 | red blood cell
10 000 | 10 km | 0.000977 | toenail thickness
1000 000 | .16x earth radius | 0.0625 | credit card width
Table source: Random ASCII

## Slide 17: Floating point trouble
Comparing floats for equality is a bad idea!
float f = 0.1;
while (f != 1.0) {
f += 0.1;
}
Notes: You can not represent 0.1 exactly in floating point

## Slide 18: Breakout time!

## Slide 19: Breakout exercises
In a shooter game, the accuracy of shooting another player 1200m away is:
Result of count?
int count = 0;
for (float f = 0.0; f <= 1.0; f += 0.1) {
count++;
}
1200 = 210*(1.17)10 Precision: 210*2-23=2-13
int count = 0;
for (int f = 0; f <= 10; f += 1) {
count++;
}
count=11
count=10
Notes: You can not represent 0.1 exactly in floating point

## Slide 20: Floating point summary
FP format is based on normalized exponential notation
Floating points are tricky
  Precision diminishes as magnitude grows
  overflow, rounding error
Many real world disasters due to FP trickiness
  Patriot Missile failed to intercept due to rounding error (1991)
  Ariane 5 explosion due to overflow in converting from double to int (1996)