## Slide 1: Building an ALU
Jinyang Li

## Slide 2: What we’ve learnt so far
Basic logic design
  Logic circuits == Boolean expressions
How to build a combinatorial logic circuit
  Specify the truth table
  Output is the sum of products
Common CL
  Decoder
  Multiplexer
decoder
2
out3
out2
out1
out0
Mux
2
S
in3
in2
in1
in0
out

## Slide 3: Lesson plan
ROM
ALU
  Logical ops: AND/OR
  Arithmetic ops: addition, subtraction…

## Slide 4: ROM (read-only memory)
A combinatorial component for storing (fixed) data
Programmed in the factory or field
n x m ROM
Height: n entries
Width: m bits per entry
....
log2n inputs
for address
...
m outputs

## Slide 5: ROM (read-only memory)
A n x m ROM can store the truth table for m functions defined on log2n variables.
A | B | X1 | X0
0 | 0 | 0 | 1
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 1
2 x 2 ROM
01
00
10
11
00:
01:
10:
11:
A
B
X1
X0

## Slide 6: ROM (read-only memory)
Both ROM and PLA can impl. boolean functions
ROM is not as efficient for sparse functions
  # of entries grows exponentially with inputs
ROM is easier to change if function changes

## Slide 7: Array of logic elements
So far, our circuits work on 1-bit inputs/outputs
How to build circuits with n-bit inputs/outputs?
MUX
2
sel
in3
in2
in1
in0
64
64
64
64
64
out
Bus: a collection of data lines treated together as a single signal

## Slide 8: Array of logic elements
64-bit multiplexor: an array of 64 1-bit multiplexors
MUX
MUX
MUX
…
sel
In363
In263
In163
In063
In31
In21
In11
In01
In30
In20
In10
In00
Out0
Out1
Out63
0th bit (LSB) of input
1st bit of input
63rd bit of input (MSB)

## Slide 9: ALU overview
ALU
operation
A
B
Result
Op | 
00 | A & B
01 | A ¦ B
10 | A + B
Example

## Slide 10: Implementing ALU: AND
Mux
Result
A&B
A|B
A+B
operation

## Slide 11: Implementing ALU: AND
Mux
Result
A&B
A|B
A+B
operation
A
B

## Slide 12: Implementing ALU: OR
Mux
Result
A&B
A|B
A+B
operation
A
B

## Slide 13: Implementing ALU: adder
Mux
Result
A&B
A|B
A+B
operation
A
B
+

## Slide 14: 1-bit adder
+
CarryIn
A
B
Sum
CarryOut

## Slide 15: 1-bit adder
+
CarryIn
A
B
Sum
CarryOut
Brute force PLA

## Slide 16: 1-bit adder
We can do better than PLA for CarryOut

## Slide 17: 1-bit adder

## Slide 18: Subtraction
Idea: a – b = a + (-b)
How to calculate 2’s complement?

## Slide 19: Subtraction in1-bit ALU
Result
operation
carryOut
A&B
A|B
A±B
A
B
+
Mux
Mux
BInvert
carryIn
Set Binvert=1
carryIn=1
Op=(10)2
to compute A-B
Subtraction reuses hardware for addition

## Slide 20: Extend 1-bit ALU to 64-bit
Result
operation
carryOut
A&B
A|B
A±B
A
B
+
Mux
Mux
BInvert
carryIn

## Slide 21: Extend 1-bit ALU to 64-bit ALU
a63
b63
Result63
ALU63

## Slide 22: Extend ALU to include NOR
Set Binvert=1, Ainvert=1
Op=(00)2
to compute a NOR b

## Slide 23: Extend ALU to include slt
RISC-V slt (set-less-than) instruction
  Result = (A < B) ? 1 : 0 Signed
  X86 equivalent: cmpq %rbx,%rax setl %rcx
Less
0
1
2
3
New input “Less”:
always 0 for bits1:63
Set to 1 for bit0 if a<b
ALU unit for bits 0-62

## Slide 24: Extend ALU to include slt
ALU unit for MSB(bit63)
A < B iff:
  (A-B) is negative (MSB is 1)
  (A-B) overflowed
  But not both
MSB
XOR
Set
Wire to “Less” input of the least significant bit ALU

## Slide 25: Extend ALU to include slt
ALU63
Result63
a63
b63

## Slide 26: Downside of ripple carry?
a63
b63
Result63
ALU63
Must wait for sequential evaluation of all 64 1-bit adders

## Slide 27: In search of a faster adder
Ripple carry:
  Delay: 64, Gate count: 64*c
Brute-force (truth table->PLA)
  Delay: 2, Gate count: O(264+64)
Clever designs in between?
Idea #1: (Carry lookahead) compute multiple carry-bits at a time

## Slide 28: Faster adder: carry lookahead
Idea #1: (Carry lookahead) compute multiple carry-bits at a time
ci+1 = aibi + (ai + bi)ci
CarryIn to i-th bit
= CarryOut of (i-1)-th bit
CarryOut of i-th bit
= CarryIn of (i+1)-th bit
ci+1 = gi + pici
gi = aibi , pi= ai + bi
gi
Generate
generates carryOut
regardless of carryIn
pi
Propagate
propagates carryIn
to carryOut

## Slide 29: Faster adder: carry lookahead
Idea #1: (Carry lookahead) compute multiple carry-bits at a time
Computing all carry-bits of a 4-bit adder:
Delay?
4-bit ripple carry delay: 2 * 4
3

## Slide 30: Faster adder: carry lookahead
Idea #1: (Carry lookahead) compute multiple carry-bits at a time
Computing all result bits in a 4-bit adder:

## Slide 31: Faster adder: carry lookahead
Build a 16-bit adder with carry-ahead 4-bit adders
carryIn (C0)
ALU0
a[0:3]
b[0:3]
ALU1
ALU2
ALU3
a[4:7]
b[4:7]
a[8:11]
b[8:11]
a[12:15]
b[12:15]
C1
C2
C3
carry
lookahead
carryOut (C4)
p0
g0
p1
g1
p2
g2
p3
g3
P0
G0
P1
G1
P2
G2
P3
G3
P0 = p3· p2· p1· p0
P1 = p7· p6· p5· p4
P2 = p11· p10· p9· p8
P3 = p15· p14· p13· p12
G0 = g3+ p3·g2 +
p3· p2·g1+ p3· p2·p1 ·g0
G1 = g7+ p7·g6 +
p7· p6·g5+ p7· p6·p5 ·g4
G2 = g11+ p11·g10 +
p11· p10·g9+ p11· p10·p9·g8
G3 = g15+ p15·g14 +
p15·p14·g13+ p15·p14·p13·g12