## Slide 1: Building an ALU
Jinyang Li

## Slide 2: What we’ve learnt so far
Basic logic design
  Logic circuits == Boolean expressions
How to build a combinatorial logic circuit
  Specify the truth table
  Output is the sum of products (implemented in PLA, programmable logic array)
Common CL
  Decoder
  Multiplexer
decoder
2
out3
out2
out1
out0
Mux
2
S
in3
in2
in1
in0
out

## Slide 3: Lesson plan
ROM (another way to implement CL)
ALU
  Logical ops: AND/OR
  Arithmetic ops: addition, subtraction…

## Slide 4: ROM (read-only memory)
A combinatorial component for storing (fixed) data
Programmed in the factory or field
n x m ROM
Height: n entries
Width: m bits per entry
....
log2n inputs
for address
...
m outputs

## Slide 5: ROM (read-only memory)
A n x m ROM can store the truth table for m functions defined on log2n variables.
A | B | X1 | X0
0 | 0 | 0 | 1
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 1
2 x 2 ROM
01
00
10
11
00:
01:
10:
11:
A
B
X1
X0

## Slide 6: ROM (read-only memory)
Both ROM and PLA can impl. boolean functions
ROM is not as efficient for sparse functions
  # of entries grows exponentially with inputs
ROM is easier to change if function changes

## Slide 7: Array of logic elements
So far, our circuits work on 1-bit inputs/outputs
How to build circuits with n-bit inputs/outputs?
MUX
2
sel
in3
in2
in1
in0
64
64
64
64
64
out
Bus: a collection of data lines treated together as a single signal

## Slide 8: Array of logic elements
64-bit multiplexor: an array of 64 1-bit multiplexors
MUX
MUX
MUX
…
sel
In363
In263
In163
In063
In31
In21
In11
In01
In30
In20
In10
In00
Out0
Out1
Out63
0th bit (LSB) of input
1st bit of input
63rd bit of input (MSB)

## Slide 9: ALU overview
ALU
operation
A
B
Result
Op | 
00 | A & B
01 | A ¦ B
10 | A + B
Example

## Slide 10: Implementing ALU: AND
Mux
Result
A&B
A|B
A+B
operation

## Slide 11: Implementing ALU: AND
Mux
Result
A&B
A|B
A+B
operation
A
B

## Slide 12: Implementing ALU: OR
Mux
Result
A&B
A|B
A+B
operation
A
B

## Slide 13: Implementing ALU: adder
Mux
Result
A&B
A|B
A+B
operation
A
B
+

## Slide 14: Implementing the adder: 1-bit adder
Recall how base-2 addition works
0 0 1 1
1 0 0 1
1 1 0 0
1
1
0
0
0
carryIn at pos0
carryOut at pos0 = carryIn at pos1
carryOut at pos1 = carryIn at pos2
carryOut at pos2 = carryIn at pos3
carryOut at pos3
At each bit position (e.g. pos1), take as inputs carryIn(c1), a1, b1,
and compute sum (s1), carryout(c2). Feed c2 to the next bit position as carryIn.
a3 a2 a1 a0
b3 b2 b1 b0
s3 s2 s1 s0
+
+
c4 c3 c2 c1 c0

## Slide 15: 1-bit adder
+
CarryIn
A
B
Sum
CarryOut

## Slide 16: 1-bit adder
+
CarryIn
A
B
Sum
CarryOut
Brute force PLA

## Slide 17: 1-bit adder: computing CarryOut
Rows where CarryOut is 1
Notes: c_out = ~a*b*c_in + a * ~b * c_in + a * b * ~c_in + a * b * c_in = (~a*b*c_in + a * b * c_in)+ (a * ~b * c_in+a * b * c_in) + (a * b * ~c_in +a * b * c_in)
= b * c_in + a*c_in + a*b
(Note that x === x + x for any Boolean formula x)

## Slide 18: 1-bit adder: computing CarryOut

## Slide 19: 1-bit adder: computing Sum

## Slide 20: Subtraction
Idea: a – b = a + (-b)
How to calculate 2’s complement?

## Slide 21: Subtraction in 1-bit ALU
Result
operation
carryOut
A&B
A|B
A±B
A
B
+
Mux
Mux
BInvert
carryIn
Set Binvert=1
carryIn=1
Op=(10)2
to compute A-B
Subtraction reuses hardware for addition

## Slide 22: Extend 1-bit ALU to 64-bit
Result
operation
carryOut
A&B
A|B
A±B
A
B
+
Mux
Mux
BInvert
carryIn

## Slide 23: Extend 1-bit ALU to 64-bit ALU
a63
b63
Result63
ALU63

## Slide 24: Extend ALU to include NOR
Set Binvert=1, Ainvert=1
Op=(00)2
to compute a NOR b

## Slide 25: Extend ALU to include slt
RISC-V slt (set-less-than) instruction
  Result = (A < B) ? 1 : 0 Signed
  X86 equivalent: cmpq %rbx,%rax setl %rcx
Less
0
1
2
3
New input “Less”:
always 0 for bits1:63
Set to 1 for bit0 if a<b
ALU unit for bits 0-62

## Slide 26: Extend ALU to include slt
ALU unit for MSB(bit63)
A < B iff:
  (A-B) is negative (MSB is 1)
  (A-B) overflowed
  But not both
MSB
XOR
Set
Wire to “Less” input of the least significant bit ALU

## Slide 27: Extend ALU to include slt
ALU63
Result63
a63
b63

## Slide 28: Downside of ripple carry?
a63
b63
Result63
ALU63
Must wait for sequential evaluation of all 64 1-bit adders

## Slide 29: In search of a faster adder
Ripple carry:
  Delay: 64, Gate count: 64*c
Brute-force (truth table->PLA)
  Delay: 2, Gate count: O(264+64)
Clever designs in between?
Idea #1: (Carry lookahead) compute multiple carry-bits at a time

## Slide 30: Faster adder: carry lookahead
Idea #1: (Carry lookahead) compute multiple carry-bits at a time
ci+1 = aibi + (ai + bi)ci
CarryIn to i-th bit
= CarryOut of (i-1)-th bit
CarryOut of i-th bit
= CarryIn of (i+1)-th bit
ci+1 = gi + pici
gi = aibi , pi= ai + bi
gi
Generate
generates carryOut
regardless of carryIn
pi
Propagate
propagates carryIn
to carryOut

## Slide 31: Faster adder: carry lookahead
Idea #1: (Carry lookahead) compute multiple carry-bits at a time
Computing all carry-bits of a 4-bit adder:
Delay?
4-bit ripple carry delay: 2 * 4
3

## Slide 32: Faster adder: carry lookahead
Idea #1: (Carry lookahead) compute multiple carry-bits at a time
Computing all result bits in a 4-bit adder:
Notes: This is the same as in Slide 18.

## Slide 33: Faster adder: carry lookahead
Build a 16-bit adder with carry-ahead 4-bit adders
carryIn (C0)
ALU0
a[0:3]
b[0:3]
ALU1
ALU2
ALU3
a[4:7]
b[4:7]
a[8:11]
b[8:11]
a[12:15]
b[12:15]
C1
C2
C3
carry
lookahead
carryOut (C4)
p0
g0
p1
g1
p2
g2
p3
g3
P0
G0
P1
G1
P2
G2
P3
G3
P0 = p3· p2· p1· p0
P1 = p7· p6· p5· p4
P2 = p11· p10· p9· p8
P3 = p15· p14· p13· p12
G0 = g3+ p3·g2 +
p3· p2·g1+ p3· p2·p1 ·g0
G1 = g7+ p7·g6 +
p7· p6·g5+ p7· p6·p5 ·g4
G2 = g11+ p11·g10 +
p11· p10·g9+ p11· p10·p9·g8
G3 = g15+ p15·g14 +
p15·p14·g13+ p15·p14·p13·g12

## Slide 34: Summary
ROM
2 x 2 ROM
01
00
10
11
00:
01:
10:
11:
A
B
X1
X0
Addr
output
ALU