## Slide 1: CSO-Recitation 14 CSCI-UA 0201-007
R14: Assessment 13 & ALU & RegFile & Pipeline

## Slide 2: Today’s Topics
Assessment 13
  Review pipelined CPU

## Slide 3: Something you may care about..
The overall grade decomposition published on campuswire #206
1 lab required:
  Lab5: due Dec 16 11pm
2 assessments to do:
  Assessment-14: release this Friday 9am and due Sat 9am
  Final assessment: release this Sunday 9pm and due next Monday 9pm
Optional lab6:
  postpone to due Dec 17 11pm

## Slide 4: Assessment 13
Q1 Single-cycle CPU

## Slide 5: Q1 FSM
In the lecture example on "electronic eyes" (see slide 28 of https://nyu-cso.github.io/notes/arch-seq.pdf). The desired pattern of lights to be lit up is: left, middle, right, middle, left, middle, right ...
What is the minimum number of distinct state values needed for a FSM to implement this electronic eyes device?
4
L
M1
R
M2
next/ light middle
next/ light right
next/ light left
next/ light middle

## Slide 6: Q2 single-cycle CPU
Q2.1 Data path
Suppose the RISC-V instruction being executed is add x6, x7, x8, where x6 is the destination register, and x7/x8 are the 1st/2nd source register operand, respectively.
What are the values corresponding to Instruction[11-7] that are fed into the "write register" pins of the RegisterFile?
00110
Write register  register code
The code of register xi is i.
For example, the code of x5 is (00101)2,
x6: (00110)2
Note: use 5 bits since we have 32 registers

## Slide 7: Q2.2 Control path
There are 3 Mux in the Figure whose selectors are to be set by the control logic, located at the top-right, bottom-middle, and bottom-right.
Which of the following instructions' execution cause the top-right Mux's selector to be set to 1?
add x6, x7, x8 //x6 = x7+x8
beq x6, x7, 100, if x6 and x7 have the same value.
beq x6, x7, 100, regardless of whether x6 and x7 have the same value.
ld x5, 40(x6) //load a doubleword (8-byte) from Memory[x6+40]Memory[x6+40] to register x5
addi x6, x7, 200 //x6 = x7+200
sd x5, 40(x6) //store a doubleword (8-byte) from register x5 to Memory[x6+40]Memory[x6+40]

## Slide 8: Q2.2 Control path
Control which branch to take next (SB-type instruction)
Control the input for ALU
Control whether write what read from memory back to register

## Slide 9: Q2.2 Control path
Control which how to compute next PC (SB-type instruction)
PC=target address (e.g. PC+2*100)
PC=PC+4

## Slide 10: Q2.2 Control path
There are 3 Mux in the Figure whose selectors are to be set by the control logic, located at the top-right, bottom-middle, and bottom-right.
Which of the following instructions' execution cause the top-right Mux's selector to be set to 1?
add x6, x7, x8 //x6 = x7+x8
beq x6, x7, 100, if x6 and x7 have the same value.
beq x6, x7, 100, regardless of whether x6 and x7 have the same value.
ld x5, 40(x6) //load a doubleword (8-byte) from Memory[x6+40]Memory[x6+40] to register x5
addi x6, x7, 200 //x6 = x7+200
sd x5, 40(x6) //store a doubleword (8-byte) from register x5 to Memory[x6+40]Memory[x6+40]

## Slide 11: Q2.3 Control path
Continuing from Q2.2, which of the following instructions cause the value for the bottom-middle Mux's selector (aka ALUSrc) to be set to 1?
add x6, x7, x8
beq x6, x7, 100, if x6 and x7 have the same value.
beq x6, x7, 100, regardless of whether x6 and x7 have the same value.
ld x5, 40(x6)
addi x6, x7, 200
sd x5, 40(x6)

## Slide 12: Q2.3 Control path
Control ALU input
1 -> select Imm
0 -> select read data 2 (i.e. register)

## Slide 13: Q2.3 Control path
Continuing from Q2.2, which of the following instructions cause the value for the bottom-middle Mux's selector (aka ALUSrc) to be set to 1?
add x6, x7, x8
beq x6, x7, 100, if x6 and x7 have the same value.
beq x6, x7, 100, regardless of whether x6 and x7 have the same value.
ld x5, 40(x6)
addi x6, x7, 200
sd x5, 40(x6)
x6 + 40 (imm)
x7 + 200 (imm)
x6 + 40 (imm)

## Slide 14: Q2.3 Control path
sd x5, 40(x6)
x6
40
x6 + 40
x5

## Slide 15: Q2.5 Control path
Which of the following instructions cause the value of the RegWrite input to the RegisterFile to be set?
add x6, x7, x8
beq x6, x7, 100, if x6 and x7 have the same value.
beq x6, x7, 100, regardless of whether x6 and x7 have the same value.
ld x5, 40(x6)
addi x6, x7, 200
sd x5, 40(x6)

## Slide 16: Q2.5 Control path
Set when we want to store a value into a register
If set, write to this register
With this data

## Slide 17: Q2.5 Control path
Which of the following instructions cause the value of the RegWrite input to the RegisterFile to be set?
add x6, x7, x8
beq x6, x7, 100, if x6 and x7 have the same value.
beq x6, x7, 100, regardless of whether x6 and x7 have the same value.
ld x5, 40(x6)
addi x6, x7, 200
sd x5, 40(x6)
write in memory: memory[x6+40]=x5
x5= memory[x6+40]
[11:7] rd
[11:7] rd

## Slide 18: Q2.5 Control path
Set when we want to store a value into a register
With what data?
If set, write to this register
With this data

## Slide 19: Q2.4 Control path
Set when we want to store a value into a register
With what data?
If set, write to this register
With this data
Data from memory
Data from ALU

## Slide 20: Q2.4 Control path
Control what to write back to the register
1 -> select read data
  ld x5, 40(x6)
  x5=Mem[x6+40]
0 -> select ALU result
  add x6, x7, x8
  x6=x7+x8

## Slide 21: Q2.4 Control path
Continuing from Q2.3, which of the following instructions cause the value for the bottom-right Mux's selector (aka MemToReg) to be set to 1?
add x6, x7, x8
beq x6, x7, 100, if x6 and x7 have the same value.
beq x6, x7, 100, regardless of whether x6 and x7 have the same value.
ld x5, 40(x6)
addi x6, x7, 200
sd x5, 40(x6)

## Slide 22: Q2.2 Control path
x5= memory[x6+40]
6
5
40
x6
x6+40
memory[x6+40]
memory[x6+40]

## Slide 23: Pipeline
Design & Hazards

## Slide 24: RISC-V Pipeline
Pipeline increases throughput by overlapping execution of multiple instructions
We split the instruction memory from the data memory
  Otherwise reading data would delay reading an instruction
There are 5 stages in the RISC-V pipeline
  Instruction Fetch – IF
    It takes a cycle to read an instruction from instruction memory
  Instruction Decode – ID
    Decode the instruction, read registers, and predict branching
  Execute – EX
    Performs computations using the ALU or performs shift operations
  Memory Access - MEM
    Read or write to memory
  Write Back – WB
    Write results to registers

## Slide 25: RISC-V Pipeline
Pipeline increases throughput by overlapping execution of multiple instructions
We split the instruction memory from the data memory
  Otherwise reading data would delay reading an instruction
There are 5 stages in the RISC-V pipeline

## Slide 26: Pipeline latency and throughput
Latency=max(stage time) * (#stages – 1) + last_stage_time
  e.g., stage times is
    IF: 200ps; 1st Reg: 100ps; ALU: 200ps; Data access: 200ps; 2nd Reg: 100ps;
  max(stage time)=200ps=clock cycle
  latency=200ps*4+100=900ps
Throughput=1/max(stage time)=clock rate
  e.g., 1/200ps

## Slide 27: Pipeline Registers
In between each stage of the pipeline, we have registers store information
  Each stage reads from the previous register to figure out what to do
  Each stage writes to the next register to pass the instruction along

## Slide 28: Assessment 13
Q2&3 Pipelined CPU

## Slide 29: Q3 Pipelining performance
clock rate=throughtput=1/max stage time
  old: 1/200
  new: 1/400
  old 2x faster
 | IF | ID | EX | MEM | WB | max
old | 200 | 100 | 200 | 200 | 100 | 200
new |  |  | 400 |  |  | 400

## Slide 30: Q3 Pipelining performance
Suppose the 5 stage pipeline has the following latency for each pipeline stage, 200ps (Instruction fetch aka IF), 100ps (Register read aka ID), 200ps (ALU operation aka EX), 200ps (Data access aka MEM), 100ps (Register write aka WB).
Suppose we build a new CPU by adding the multiplication function to ALU, which causes the ALU latency to increase from 200ps to 400ps. Which of the following statements are true?
The new CPU has twice the instruction throughput of the original one.
The old CPU has twice the instruction throughput as fast as the new one.
The ALU latency increase would cause the new CPU to run at a slower clock rate than the old CPU.
The ALU latency increase would cause the new CPU to run at a faster clock rate than the old CPU.

## Slide 31: Q4 Pipelining performance
Suppose we change the RISC-V ISA to restrict load/store instructions to use a base register only (without an immediate offset/displacement). Thus, load/store instructions no longer need to use the ALU to compute addresses. As a result, we can change the CPU to overlap the data access (aka MEM) and ALU operation (aka EX) into one stage, resulting in a 4-stage pipeline. Note that in the merged MEM-EX stage, an instruction either performs data access or ALU operation, but not both. Hence the merged stage still takes 200ps, same as the latency of either MEM or EX in Q2.

## Slide 32: Q4
Merge

## Slide 33: Q4
Merge
IF
ID
EX
MEM
WB
Why we can merge them in a single stage?
Because there is no dependency.
No dependency => parallelism
load/store instructions no longer need to use the ALU to compute addresses

## Slide 34: Q4
Merge
Mem only depends on 2nd stage

## Slide 35: Q4
Merge

## Slide 36: Q4.1 Clock speed
How does the new 4-stage design affect the clock speed?
Clock for 4-stage pipelined CPU must run faster than that in the 5-stage pipelined CPU.
Clock for 4-stage pipelined CPU must run slower than that in the 5-stage pipelined CPU.
Clock for 4-stage pipelined CPU can run at the same speed as that of the 5-stage pipelined CPU.
clock cycle (=max) remains unchanged
 | IF | ID | EX | MEM | WB | max
old | 200 | 100 | 200 | 200 | 100 | 200
new |  |  | 200 |  |  | 200

## Slide 37: Q4.2 Instruction latency
How does the new 4-stage design affect the instruction latency?
instruction latency (e.g. for load) for 4-stage pipelined CPU is lower than that in the 5-stage pipelined CPU.
instruction latency (e.g. for load) for 4-stage pipelined CPU is higher than that in the 5-stage pipelined CPU.
instruction latency (e.g. for load) for 4-stage pipelined CPU is the same as that in the 5-stage pipelined CPU.
Instruction latency:
5-stage: 400ps*4+100
4-stage:
  200ps*3+100

## Slide 38: Pipeline hazard
No dependency => parallelism
Pipeline: parallelly execute the instructions:
  For a specific instruction, a stage depends on the previous stage.
  But we can utilize the independency across instructions
    We can execute the next instruction without waiting for the finish of the previous instruction => pipeline
However, not always true => hazard.

## Slide 39: Pipeline hazard
x5 = 0, x6 = 1, x7 = 1
add x5, x6, x7 (x5 = x6 + x7)
add x4, x5, x6 (x4 = x5 + x6)
x4 should be 3
IF
EX
MEM
WB
add x5, x6, x7
add x4, x5, x6
IF
ID
EX
MEM
WB
ID

## Slide 40: Pipeline hazard
x5 = 0, x6 = 1, x7 = 1
add x5, x6, x7 (x5 = x6 + x7)
add x4, x5, x6 (x4 = x5 + x6)
x4 should be 3
IF
ID
EX
MEM
add x5, x6, x7
add x4, x5, x6
IF
EX
MEM
WB
ID
WB

## Slide 41: Pipeline hazard
inst
x5 = 0, x6 = 1, x7 = 1
add x5, x6, x7 (x5 = x6 + x7)
add x4, x5, x6 (x4 = x5 + x6)
x4 should be 3
IF
ID
EX
MEM
add x5, x6, x7
add x4, x5, x6
IF
EX
MEM
x6 = 1
x7 = 1
WB
ID
WB

## Slide 42: Pipeline hazard
ID
x5 = 0, x6 = 1, x7 = 1
add x5, x6, x7 (x5 = x6 + x7)
add x4, x5, x6 (x4 = x5 + x6)
x4 should be 3
IF
ID
EX
MEM
add x5, x6, x7
add x4, x5, x6
IF
EX
MEM
out
= 2
x5 = 0
x6 = 1
Why?
The result hasn’t written back to x5!
WB
WB
ID

## Slide 43: Pipeline hazard
x5 = 0, x6 = 1, x7 = 1
add x5, x6, x7 (x5 = x6 + x7)
add x4, x5, x6 (x4 = x5 + x6)
x4 should be 3
IF
EX
MEM
add x5, x6, x7
add x4, x5, x6
IF
EX
MEM
out
= 1
Wrong! Should be 3
WB
ID
WB
ID

## Slide 44: Pipeline hazard
Sometimes instructions depend on each other
In fact, that is very often the case, that some instruction uses the result of a previous instruction
This becomes an issue, however, when an instruction depends on a value that has been computed but not written back yet

## Slide 45: Hazard Motivation
Consider the following C Program:
int calc(int a, int b, int c) {
  a = a + b;
  a = a + c;
  return a;
}
Which becomes :
  add x10, x10, x11
  add x10, x10, x12
What might cause sadness here?

## Slide 46: Pipeline hazard
Structure Hazard
  Caused by limited hardware resources.
  Solution: add resources (e.g., separating inst. and data mem)
Data Hazard
Control Hazard
Caused by the dependency between instructions:
The execution of i2 depends on some output of i1.
=> wouldn’t happen in sequential model, because i2 is executed after finishing i1 and thus i2 can always see the output of i1.

## Slide 47: Pipeline hazard
Structure Hazard
  Caused by limited hardware resources.
  Solution: add resources (e.g., separating inst. and data mem)
Data Hazard
Control Hazard
Caused by the dependency between instructions:
The execution of i2 depends on some output of i1.
=> wouldn’t happen in sequential model, because i2 is executed after finishing i1 and thus i2 can always see the output of i1.
i2 must wait for the finish of i1?
Can we get the output sooner and thus doesn’t affect the execution of i2?

## Slide 48: Forwarding
ID
WB
WB
x5 = 0
x6 = 1
x5 = 0, x6 = 1, x7 = 1
add x5, x6, x7 (x5 = x6 + x7)
add x4, x5, x6 (x4 = x5 + x6)
x4 should be 3
IF
EX
MEM
add x5, x6, x7
add x4, x5, x6
IF
EX
MEM
out
= 2
Forwarding
ID

## Slide 49: Forwarding
x5 = 0, x6 = 1, x7 = 1
add x5, x6, x7 (x5 = x6 + x7)
add x4, x5, x6 (x4 = x5 + x6)
x4 should be 3

## Slide 50: Forwarding
x5 = 0, x6 = 1, x7 = 1
add x5, x6, x7 (x5 = x6 + x7)
add x4, x5, x6 (x4 = x5 + x6)
x4 should be 3
IF
EX
MEM
add x5, x6, x7
add x4, x5, x6
IF
EX
MEM
out
= 3
Correct!
ID
WB
WB
ID

## Slide 51: Forwarding
The input of some stage s2 in i2 depends on the output of some stage s1 in i1:
  E.g. i2’s input of EX stage depends on the i1’s output of EX stage
  Trying to forward i1’s output of s1 to i2’s s2.
  But this doesn’t work all the time.
    Need to delay i2’s s2 until i1 has the output.
    How? By adding bubble (nop instruction)
Sometimes i1 cannot have the output at the time when i2 needs it (e.g., i2’s input of EX depends on i1’s output of MEM)

## Slide 52: Bubble
x5 = 0, x6 = 1, mem[101] = 1
i1: ld x5, x6(100) (x5 = mem[x6 + 100])
i2: add x4, x5, x6 (x4 = x5 + x6)
x4 should be 2
IF
ID
EX
MEM
WB
i1: ld x5, x6(100)
i2: add x4, x5, x6
IF
ID
EX
MEM
WB
input of i2’s EX stage depends on the output of i1’s MEM stage

## Slide 53: Bubble
x5 = 0, x6 = 1, mem[101] = 1
i1: ld x5, x6(100) (x5 = mem[x6 + 100])
i2: add x4, x5, x6 (x4 = x5 + x6)
x4 should be 2
IF
ID
EX
MEM
i1: ld x5, x6(100)
i2: add x4, x5, x6
IF
EX
MEM
However, when i2 starts EX stage, i1 just starts its MEM stage!
=> We do not have the correct input yet!
input of i2’s EX stage depends on the output of i1’s MEM stage
ID
WB
WB

## Slide 54: Bubble
ID
WB
WB
x5 = 0, x6 = 1, mem[101] = 1
i1: ld x5, x6(100) (x5 = mem[x6 + 100])
i2: add x4, x5, x6 (x4 = x5 + x6)
x4 should be 2
IF
EX
MEM
i1: ld x5, x6(100)
i2: add x4, x5, x6
IF
EX
MEM
However, when i2 starts EX stage, i1 just starts its MEM stage!
=> We do not have the correct input yet!
input of i2’s EX stage depends on the output of i1’s MEM stage
We need to delay i2’s EX stage,
so that i1 can prepare the required output.
How many bubbles?
ID

## Slide 55: Bubble
ID
WB
WB
x5 = 0, x6 = 1, mem[101] = 1
i1: ld x5, x6(100) (x5 = mem[x6 + 100])
i2: add x4, x5, x6 (x4 = x5 + x6)
x4 should be 2
IF
EX
MEM
i1: ld x5, x6(100)
i2: add x4, x5, x6
IF
EX
MEM
WB
How many bubbles?
How many cycles it needs for i1 to prepare the output before i2 uses it.
When i2 starts EX, i1 starts MEM.
i1 just needs 1 more cycle and then it can provide the output.
ID

## Slide 56: Bubble
x5 = 0
x6 = 1
x5 = 0, x6 = 1, mem[101] = 1
i1: ld x5, x6(100) (x5 = mem[x6 + 100])
i2: add x4, x5, x6 (x4 = x5 + x6)
x4 should be 2
IF
ID
EX
MEM
WB
i1: ld x5, x6(100)
i2: add x4, x5, x6
IF
ID
EX
MEM
WB
How many bubbles?
How many cycles it needs for i1 to prepare the output before i2 uses it.
bubble
IF
ID
EX
MEM
WB
out
= 1
When i2 starts EX,
i1 has just finished MEM

## Slide 57: Bubble
x5 = 0
x6 = 1
x5 = 0, x6 = 1, mem[101] = 1
i1: ld x5, x6(100) (x5 = mem[x6 + 100])
i2: add x4, x5, x6 (x4 = x5 + x6)
x4 should be 2
IF
ID
EX
MEM
WB
i1: ld x5, x6(100)
i2: add x4, x5, x6
IF
ID
EX
MEM
WB
How many bubbles?
How many cycles it needs for i1 to prepare the output before i2 uses it.
out
= 1
When i2 starts EX,
i1 has just finished MEM

## Slide 58: Bubble
x5 = 0
x6 = 1
x5 = 0, x6 = 1, mem[101] = 1
i1: ld x5, x6(100) (x5 = mem[x6 + 100])
i2: add x4, x5, x6 (x4 = x5 + x6)
x4 should be 2
IF
ID
EX
MEM
WB
i1: ld x5, x6(100)
i2: add x4, x5, x6
IF
ID
EX
MEM
WB
How many bubbles?
How many cycles it needs for i1 to prepare the output before i2 uses it.
bubble
IF
ID
EX
MEM
WB
out
= 1

## Slide 59: Bubble
x5 = 0, x6 = 1, mem[101] = 1
i1: ld x5, x6(100) (x5 = mem[x6 + 100])
i2: add x4, x5, x6 (x4 = x5 + x6)
x4 should be 2
IF
EX
MEM
i1: ld x5, x6(100)
i2: add x4, x5, x6
IF
EX
MEM
How many bubbles?
How many cycles it needs for i1 to prepare the output before i2 uses it.
bubble
IF
EX
MEM
out
= 2
ID
ID
WB
ID
WB
WB

## Slide 60: Pipeline hazard
Structure Hazard
  Caused by limited hardware resources.
  Solution: add resources (e.g., separating inst. and data mem)
Data Hazard
  Solution: forwarding
    works for EX-hazard & MEM-hazard
  Load-use Hazard:
    Solution: stall and insert bubble
Control Hazard
  Solution: insert bubble
  Reduce branch delay: by predicting branch in ID stage

## Slide 61: Hazard Fix
There are two approaches to avoiding hazards
Forwarding
  Be able to send data to an earlier location in the pipeline before write back
  We do this by adding some multiplexers in the EX stage to choose between more recent values and the value from the register file
Stalling
  Add a “bubble” to the pipeline to give us time to resolve the hazard
  We do this by setting some of the controls to 0 and by preventing the PC from changing

## Slide 62: Q4.3 Instruction throughput
How does the new 4-stage design affect the instruction throughput?
instruction throughput for 4-stage pipelined CPU is lower than that in the 5-stage pipelined CPU, under ideal (no hazard) scenarios.
instruction throughput for 4-stage pipelined CPU is higher than that in the 5-stage pipelined CPU, under ideal (no hazard) scenarios.
instruction throughput for 4-stage pipelined CPU is the same as that in the 5-stage pipelined CPU, under ideal (no hazard) scenarios.
4-stage pipelined CPU tends to have fewer hazards than 5-stage pipelined CPU.
4-stage pipelined CPU tends to have more hazards than 5-stage pipelined CPU.
4-stage pipelined CPU has the same amount of hazards as 5-stage pipelined CPU.
throughput is still 1/200ps

## Slide 63: Q4.3 Instruction throughput
More stages, tend to have more hazards
  E.g. sequential model: 1 stage, no hazards
Why?
  Suppose i2 depends on the output of i1
  Intuitively, with more stages, there are more cases that i1 is still in process when i2 needs the input, and causes a hazard.

## Slide 64: Q4.3 Instruction throughput
i1: add x5, x6, x7
Nop
i2: add x4, x5, x6
IF
ID
EX
MEM
WB
i1: add x5, x6, x7
nop
IF
ID
EX
MEM
IF
ID
EX
MEM
i2: add x4, x5, x6
When i2 tries to read x5
i1 hasn’t written it back
=> hazard!
WB

## Slide 65: Q4.3 Instruction throughput
i1: add x5, x6, x7
Nop
i2: add x4, x5, x6
IF
ID
EX
WB
i1: add x5, x6, x7
nop
IF
EX
WB
IF
ID
EX
i2: add x4, x5, x6
When i2 tries to read x5
i1 has just written it back
=> No hazard
ID
ID

## Slide 66: Control hazard
assume x5 = 0 x6 = 0
beq x5, x6, 100
add x1, x2, x3
…
Should jump to here:
add x7, x8, x9
How many bubbles?
Note: jump instruction can decide the address of the next instruction in MEM stage

## Slide 67: Control hazard
assume x5 = 0 x6 = 0
i1: beq x5, x6, 100
add x1, x2, x3
…
Should jump to here:
i2: add x7, x8, x9
How many bubbles?
IF
ID
EX
i1: beq x5, x6, 100
ID
How many bubbles?
How many cycles it needs
for i1 to prepare the output
before next instruction uses it.
i2: add x7, x8, x9
IF
ID
EX
ID
Q1: what (the output of which stage of i1) does i2 need to correctly execute?
Q2: How many cycles does i1 need to finish that stage before i2 needs it?
MEM
WB
MEM
WB

## Slide 68: Control hazard
assume x5 = 0 x6 = 0
i1: beq x5, x6, 100
add x1, x2, x3
…
Should jump to here:
i2: add x7, x8, x9
How many bubbles?
IF
ID
EX
i1: beq x5, x6, 100
ID
How many bubbles?
How many cycles it needs
for i1 to prepare the output
before next instruction uses it.
i2: add x7, x8, x9
IF
ID
EX
ID
Q1: what (the output of which stage of i1) does i2 need to correctly execute?
i2 needs the instruction address
=> decided by MEM stage in i1
MEM
WB
MEM
WB

## Slide 69: Control hazard
MEM
assume x5 = 0 x6 = 0
i1: beq x5, x6, 100
add x1, x2, x3
…
Should jump to here:
i2: add x7, x8, x9
How many bubbles?
IF
ID
EX
i1: beq x5, x6, 100
ID
How many bubbles?
How many cycles it needs
for i1 to prepare the output
before next instruction uses it.
i2: add x7, x8, x9
IF
ID
EX
ID
i2 needs the instruction address
=> decided by MEM stage in i1
Q2: How many cycles does i1 need to finish that stage before i2 needs it?
i1 should finish MEM before i2 starts IF
i1 starts MEM at cycle k, i2 starts IF at cycle k+1
WB
MEM
WB

## Slide 70: Control hazard
assume x5 = 0 x6 = 0
i1: beq x5, x6, 100
add x1, x2, x3
…
Should jump to here:
i2: add x7, x8, x9
How many bubbles?
IF
ID
EX
i1: beq x5, x6, 100
ID
How many bubbles?
How many cycles it needs
for i1 to prepare the output
before next instruction uses it.
i2: add x7, x8, x9
IF
ID
EX
ID
i2 needs the instruction address
=> decided by MEM stage in i1
Q2: How many cycles does i1 need to finish that stage before i2 needs it?
MEM
WB
MEM
WB
Currently, i1 starts MEM at cycle k, i2 starts IF at cycle ?

## Slide 71: Control hazard
assume x5 = 0 x6 = 0
i1: beq x5, x6, 100
add x1, x2, x3
…
Should jump to here:
i2: add x7, x8, x9
How many bubbles?
IF
ID
EX
i1: beq x5, x6, 100
ID
How many bubbles?
How many cycles it needs
for i1 to prepare the output
before next instruction uses it.
i2: add x7, x8, x9
IF
ID
EX
ID
i2 needs the instruction address
=> decided by MEM stage in i1
Q2: How many cycles does i1 need to finish that stage before i2 needs it?
k
k - 1
MEM
WB
MEM
WB
k - 2

## Slide 72: Control hazard
assume x5 = 0 x6 = 0
i1: beq x5, x6, 100
add x1, x2, x3
…
Should jump to here:
i2: add x7, x8, x9
How many bubbles?
IF
ID
EX
i1: beq x5, x6, 100
ID
How many bubbles?
How many cycles it needs
for i1 to prepare the output
before next instruction uses it.
i2: add x7, x8, x9
IF
ID
EX
ID
i2 needs the instruction address
=> decided by MEM stage in i1
Q2: How many cycles does i1 need to finish that stage before i2 needs it?
Delay i2 for 3 cycles!
=> Insert 3 bubbles
k
k - 1
k - 2
MEM
WB
MEM
i1 should finish MEM before i2 starts IF
i1 starts MEM at cycle k, i2 starts IF at cycle k+1
WB

## Slide 73: Control hazard
MEM
i1: beq x5, x6, 100
How many bubbles?
How many cycles it needs
for i1 to prepare the output
before next instruction uses it.
i2: add x7, x8, x9
IF
Q2: How many cycles does i1 need to finish that stage before i2 needs it?
bubble
bubble
When i2 starts IF
i1 has just finished MEM
IF
EX
ID
WB
IF
EX
ID
MEM
IF
EX
ID
IF
WB
bubble
ID

## Slide 74: Control hazard
MEM
i1: beq x5, x6, 100
How many bubbles?
How many cycles it needs
for i1 to prepare the output
before next instruction uses it.
i2: add x7, x8, x9
IF
Q2: How many cycles does i1 need to finish that stage before i2 needs it?
bubble
bubble
When i2 starts IF
i1 has just finished MEM
IF
EX
ID
WB
IF
EX
ID
MEM
IF
EX
ID
IF
WB
bubble
ID

## Slide 75: Control hazard – current design
assume x5 = 0 x6 = 0
beq x5, x6, 100
i3: xxx
Should jump to here:
i2: xxx
How many bubbles?
IF
ID
EX
WB
i1: beq x5, x6, 100
i3: xxx
IF
EX
WB
ID
ID
What instruction to fetch??
PC+200 If x5==x6, otherwise PC+4
PC+200 in this case
However, result of x5==x6 is not available until EX
=> EX-IF dependency
Current design fetches i3 (PC+4)
Wrong instruction!!
How many bubbles?
How many cycles it needs for i1 to prepare the output before next instruction uses it.
2

## Slide 76: Control hazard – design #1
assume x5 = 0 x6 = 0
beq x5, x6, 100
xxx
Should jump to here:
i2: xxx
How many bubbles?
IF
ID
EX
WB
i1: beq x5, x6, 100
nop
IF
EX
WB
IF
ID
EX
nop
ID
ID
out: x5==x6
IF
ID
EX
i2: xxx
Idea: always insert 2 bubbles for branch
mux

## Slide 77: Control hazard – design #1’s problem
assume x5 = 0 x6 = 1
beq x5, x6, 100
i3: xxx // PC+4
…
i2: xxx // PC+200:
How many bubbles?
What if x5!=x6?
Actually no bubbles needed!
IF
ID
EX
WB
i1: beq x5, x6, 100
i3: xxx
IF
EX
WB
ID
ID
Fetch PC+4

## Slide 78: Control hazard – design #2
assume x5 = 0 x6 = 1
beq x5, x6, 100
i3: xxx // PC+4
…
i2: xxx // PC+200:
How many bubbles?
What if x5!=x6?
Actually no bubbles needed!
IF
ID
EX
WB
i1: beq x5, x6, 100
i2: xxx
IF
EX
WB
IF
ID
EX
xxx
ID
ID
IF
ID
EX
xxx
Nop Controler
out: x5==x6?
nops if x5==x6
mux

## Slide 79: Q4.4 others
How does the new 4-stage design affect the overall program performance?
Assuming no hazards, programs always execute faster under the 4-stage pipelined CPU than the original 5-stage pipeline.
Assuming no hazards, programs always execute slower under the 4-stage pipelined CPU than the original 5-stage pipeline.
Assuming no hazards, programs always execute at the same speed under the 4-stage pipelined CPU as the original 5-stage pipeline.
Assuming no hazards, programs can execute slower under the 4-stage pipelined CPU than the original 5-stage pipeline, because more instructions are needed (to calculate memory addresses for load/store).

## Slide 80: Common question for lab5
Incomplete problem: Some circuits will be tested together
  try to finish all circuits in one exercise, and check again
When implementing
  Don't change the contents above the dash line, and
  use Tunnels (not pins) as inputs and outputs
Building sub-circuits/sub-components and use Tunnels will help a lot
  especially for complex implementation, i.e. bonus exercise: Logical Shift Right

## Slide 81: Lab6
ALU & RegFile

## Slide 82: ALU
2 inputs, 1 ALU selector, 1 output(result)
You need to implement 14 instructions
  add, sub, and, or, xor, srl, divu,…
    allowed and encouraged to use built-in Logisim blocks to implement the arithmetic operations
  combinatorial circuits
    how to build any combinatorial circuits?
    think about srl(unsigned right shift), sra(signed right shift), sll(left shift)
How to select the result?
  “ALUSel”, MUX
Building sub-circuits and using Tunnels is helpful.

## Slide 83: Register File
Register file: a set of registers that can be read and written
  It’s a state element
Six inputs:
  clock, rs1, rs2, rd, write data, RegWEn
Two outputs:
  Read data 1, Read data 2
Step:
  build register
    Lab asks to implement 9 registers instead of 32
    Provide some outputs for testing and debugging purposes
  build register file

## Slide 84: Register File
Read:
Write:
Think about DEMUX

## Slide 85: Congrats to all
Great job!
Thanks for attending and supporting!
Good luck to all your final works~