## Slide 1: Pipelined CPU
Jinyang Li
Slides are based on Patterson and Hennessy

## Slide 2: What we’ve learnt so far
Single cycle RISC-V CPU design
5 stage pipelined RISC-V CPU
  Why pipelining? Faster (ideal throughput speedup: #-of-stages)
Pipelining challenges: hazards
  Structure (how to avoid stall? add resources)
  Data (how to minimize stall? forwarding)
  Control

## Slide 3: Today’s lesson
Handling control (branch) hazard
Handling exceptions
Briefly, more advanced topics:
  Multiple-issue
  Subword parallelism (SIMD)

## Slide 4: Recall our pipelined design so far
IF: instruction
fetch
ID: instruction
decode/reg read
EX: execute/
address calc
WB: write-back
MEM: memory access
Branch outcome determined in MEM stage

## Slide 5: Branch Hazard
If branch outcome is determined in MEM
PC
Flush 3 instructions (set controls to 0)
Instruction address
If x1==x0
Pc = pc+16*2

## Slide 6: Reducing Branch Delay
Add hardware to determine branch outcome earlier (e.g. ID instead of MEM)  fewer instructions to flush
36: sub x10, x4, x8 40: beq x1, x3, 16 // PC-relative branch // to 40+16*2=72 44: and x12, x2, x5 48: orr x13, x2, x6 52: add x14, x4, x2 56: sub x15, x6, x7 ... 72: ld x4, 50(x7)
How many instructions to flush
if branch outcome is known in ID?
clock-1
clock-2
clock-3
40: beq
44: and
IF
ID
EXE
MEM
WB
clock-4
clock-5
IF
ID
EXE
MEM
WB
IF
ID
EXE
MEM
WB
72: ld

## Slide 7: Branch determined in ID and is taken
Clock 2
Additional comparator
to determine branch outcome
Additional adder for
calculating target address
If branch is taken, set IF/ID.Flush
IF/ID.Flush

## Slide 8: Branch determined in ID and is taken
Clock 3
If IF/ID.Flush is set, zero out controls so
memory/register won’t be written in MEM and WB

## Slide 9: Dynamic Branch Prediction
Our simple 5-stage pipeline’s branch penalty is 1 bubble, but
  In deeper pipelines, branch penalty is more significant
Solution: dynamic prediction
  Branch prediction buffer (aka branch history table)
    Indexed by recent branch instruction addresses
    Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 10: 1-Bit Predictor: Shortcoming
Inner loop branches mispredicted twice!
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer
  Mispredict as taken on last iteration of inner loop
  Then mispredict as not taken on first iteration of inner loop next time around

## Slide 11: 2-Bit Predictor
Only change prediction on two successive mispredictions

## Slide 12: Calculating Branch Target (needed if branch is predicted taken)
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately

## Slide 13: Exceptions and Interrupts
“Unexpected” events requiring change in flow of control
Exception
  Arises within the CPU
    e.g., undefined opcode, syscall, memory permission error, divide by zero, …
Interrupt
  From an external I/O controller
Dealing with them without sacrificing performance is hard

## Slide 14: Handling Exceptions
Save PC of offending (or interrupted) instruction
  In RISC-V: Supervisor Exception Program Counter (SEPC)
Save indication of the problem
  In RISC-V: Supervisor Exception Cause Register (SCAUSE)
Jump to handler (aka code in OS kernel)
  Assume at 0000 0000 1C09 0000hex
OS’s handler does either of the following:
  Take corrective action; restart offending instruction
  Terminate program; report cause

## Slide 15: An Alternate Mechanism
Vectored Exception/Interrupts (x86)
Vector index (interrupt descriptor) specifies cause of exception
  E.g. in x86, 0 (divide by zero), 6 (invalid opcode), …
OS sets up the Interrupt Descriptor Table
  IDT[i] contains handler address, where I is vector index.

## Slide 16: Exceptions in a Pipeline
Another form of control hazard
Consider malfunction on add in EX stage
  add x1, x2, x1
  Prevent x1 from being clobbered
  Complete previous instructions
  Flush add and subsequent instructions
  Save PC (of offending instruction) in SEPC and set SCAUSE with cause
  Transfer control to handler
Similar to mispredicted branch
  Use much of the same hardware

## Slide 17: Exception Example
Exception on add in
  40 sub x11, x2, x4 44 and x12, x2, x5 48 orr x13, x2, x6 4c add x1, x2, x1 50 sub x15, x6, x7 54 ld x16, 100(x7) …
Handler
  1C090000 sd x26, 1000(x10) 1c090004 sd x27, 1008(x10) …

## Slide 18: Exception Example
These signals are set
if add malfunctioned
Handler address is used for IF in next cycle

## Slide 19: Exception Example
Offending instruction (add x1, x2, x1) becomes a bubble (so it won’t clobber registers)
Instructions in exception handler

## Slide 20: Instruction-Level Parallelism (ILP)
Pipelining: execute multiple instructions in parallel
To increase ILP
  Deeper pipeline
    Less work per stage  shorter clock cycle
  Multiple issue
    Replicate pipeline stages  multiple pipelines
    Start multiple instructions per clock cycle
      Finish multiple Instructions Per Cycle (IPC>1)
    E.g., 4GHz 4-way multiple-issue
      16 billion instructions/sec, peak IPC = 4 (CPI = 1/IPC = 0.25)
    Challenges: dependencies among multi-issued instructions
      reduce peak IPC this

## Slide 21: Multiple Issue
Static multiple issue (Very Long Instruction Word)
  Compiler groups instructions to be issued together
  Compiler detects and avoids hazards
Dynamic multiple issue (superscalar)
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 22: Static Multiple Issue
Compiler groups instructions into “issue packets”
  Group >1 instructions in an issue packet to be issued in a single cycle
  Instructions within a packet must have no dependencies
    Reorder
    Add nop
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations
   Very Long Instruction Word (VLIW)

## Slide 23: Dynamic Multiple Issue
“Superscalar” processors
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoids the need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 24: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
  ld x31,20(x21) add x1,x31,x2 sub x23,x23,x3 andi x5,x23,20
  Can start sub while add is waiting for ld

## Slide 25: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g., cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined
Different implementations of an ISA have different latencies and hazards

## Slide 26: Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g., pointer aliasing
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well

## Slide 27: Multiple-issue benefits from loop unrolling
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
  Avoid loop-carried dependency
    Store followed by a load of the same register
long x[100];
…
for (int i = 0; i < 100; i++) {
x[i] *= 2;
}
//suppose x1=&x[0]
//x2 = &x[100]
Loop:
ld x31, 0(x1)
add x31, x31, x30
sd x30, 0(x1)
addi x1, x1, 8
blt x1, x2, Loop
//suppose x20=&x[0]
//x22 = &x[100]
Loop:
ld x31, 0(x1)
add x31, x31, x30
sd x30, 0(x1)
ld x29, 8(x1)
add x29, x29, x28
sd x28, 8(x1)
addi x20, x20, 16
blt x20, x22, Loop

## Slide 28: Power Efficiency
Complexity of dynamic scheduling and speculations requires power
Multiple simpler cores may be better
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
Core | 2006 | 2930MHz | 14 | 4 | Yes | 2 | 75W
UltraSparc III | 2003 | 1950MHz | 14 | 4 | No | 1 | 90W
UltraSparc T1 | 2005 | 1200MHz | 6 | 1 | No | 8 | 70W

## Slide 29: ARM Cortex A53 and Intel i7
Processor | ARM A53 | Intel Core i7 920
Market | Personal Mobile Device | Server, cloud
Thermal design power | 100 milliWatts (1 core @ 1 GHz) | 130 Watts
Clock rate | 1.5 GHz | 2.66 GHz
Cores/Chip | 4 (configurable) | 4
Floating point? | Yes | Yes
Multiple issue? | Dynamic | Dynamic
Peak instructions/clock cycle | 2 | 4
Pipeline stages | 8 | 14
Pipeline schedule | Static in-order | Dynamic out-of-order with speculation
Branch prediction | Hybrid | 2-level
1st level caches/core | 16-64 KiB I, 16-64 KiB D | 32 KiB I, 32 KiB D
2nd level caches/core | 128-2048 KiB | 256 KiB (per core)
3rd level caches (shared) | (platform dependent) | 2-8 MB

## Slide 30: Real world processor performance
ARM Cortex-A53
Intel core i7
Ideal CPI=0.5 because of 2 issue
Ideal CPI=0.25 because of 4 issue

## Slide 31: Ways to improve performance: subword parallelism
ML/graphics applications perform same operations on vectors
  Partition a 128-bit adder into:
    Sixteen 8-bit adds
    Eight 16-bit adds
    Four 32-bit adds
Also called data-level parallelism, vector parallelism, or Single Instruction, Multiple Data (SIMD)
Intel’s AVX introduces 256-bit floating point registers
    8 single-precision ops
    4 double-precision ops

## Slide 32: Example: unoptimized matrix multiplication
1. void dgemm (int n, double* A, double* B, double* C)
2. {
3. for (int i = 0; i < n; ++i)
4. for (int j = 0; j < n; ++j)
5. {
6. double cij = C[i+j*n];
7. for(int k = 0; k < n; k++ )
8. cij += A[i+k*n] * B[k+j*n];
9. C[i+j*n] = cij;
10. }
11. }

## Slide 33: Matrix Multiply: optimized C
1. #include <x86intrin.h>
2. void dgemm (int n, double* A, double* B, double* C)
3. {
4. for ( int i = 0; i < n; i+=4 )
5. for ( int j = 0; j < n; j++ ) {
6. __m256d c0 = _mm256_load_pd(C+i+j*n); /* c0 = C[i][j] */
7. for( int k = 0; k < n; k++ )
8. c0 = _mm256_add_pd(c0, /* c0 += A[i][k]*B[k][j] */
9. _mm256_mul_pd(_mm256_load_pd(A+i+k*n),
10. _mm256_broadcast_sd(B+k+j*n)));
11. _mm256_store_pd(C+i+j*n, c0); /* C[i][j] = c0 */
12. }
13. }

## Slide 34: AVX Optimized Matrix multiply
1. vmovapd (%r11),%ymm0 # Load 4 elements of C into %ymm0
2. mov %rbx,%rcx # register %rcx = %rbx
3. xor %eax,%eax # register %eax = 0
4. vbroadcastsd (%rax,%r8,1),%ymm1 # Make 4 copies of B element
5. add $0x8,%rax # register %rax = %rax + 8
6. vmulpd (%rcx),%ymm1,%ymm1 # Parallel mul %ymm1,4 A elements
7. add %r9,%rcx # register %rcx = %rcx + %r9
8. cmp %r10,%rax # compare %r10 to %rax
9. vaddpd %ymm1,%ymm0,%ymm0 # Parallel add %ymm1, %ymm0
10. jne 50 <dgemm+0x50> # jump if not %r10 != %rax
11. add $0x1,%esi # register % esi = % esi + 1
12. vmovapd %ymm0,(%r11) # Store %ymm0 into 4 C elements
256-bit wide FP register

## Slide 35: Ways to improve performance: loop unrolling
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
  Avoid loop-carried dependency
    Store followed by a load of the same register

## Slide 36: Ways to improve performance: loop unrolling
Loop unrolling: replicate loop body
Unrolling exposes more parallelism for multi-issue pipelined CPU
  Reduces loop-control overhead
  Avoid loop-carried dependency
    Store followed by a load of the same register
long x[100];
…
for (int i = 0; i < 100; i++) {
x[i] *= 2;
}
//suppose x1=&x[0]
//x2 = &x[100]
Loop:
ld x31, 0(x1)
add x31, x31, x30
sd x30, 0(x1)
addi x1, x1, 8
blt x1, x2, Loop
//suppose x20=&x[0]
//x22 = &x[100]
Loop:
ld x31, 0(x1)
add x31, x31, x30
sd x30, 0(x1)
ld x29, 8(x1)
add x29, x29, x28
sd x28, 8(x1)
addi x20, x20, 16
blt x20, x22, Loop

## Slide 37: Performance Impact

## Slide 38: Summary on CPU design
ISA influences design of datapath and control
Datapath and control influence design of ISA
Pipelining improves instruction throughput using parallelism
  More instructions completed per second
  Latency for each instruction not reduced
Hazards: structural, data, control
Multiple issue and dynamic scheduling (ILP)
  Dependencies limit achievable parallelism
  Complexity leads to the power wall