## Slide 1: Basic Processor Implementation
Jinyang Li

## Slide 2: What we’ve learnt so far
Combinatorial logic
  Truth table
  ROM
ALU
Sequential logic
  Clocks
  Basic state elements (SR latch, D latch, flip-flop)
unclocked
Clocked (Level triggered)
Clocked (edge triggered)

## Slide 3: Today’s lesson plan
Implement a basic CPU

## Slide 4: Our CPU will be based on RISC-V instead of x86
3 popular ISAs now
ISA | Key advantage | Who builds the processors? | Where are the processors used?
x86 | Fast | Intel, AMD | Server (Cloud), Desktop, Laptop, Xbox console
ARM | Low power (everybody can license the design from ARM Holdings for $$$) | Samsung, NVIDIA, Qualcomm, Broadcom, Huawei/HiSilicon | Phones, Tablets, Nintendo console, Raspberry Pi
RISC-V | Open source, royalty-free | Western digital, Alibaba | Devices (e.g. SSD controllers)
RISC
Reduced
Instruction Set
CISC
Complex
Instruction Set

## Slide 5: RISC-V at a high level
 | RISC-V | X86-64
# of registers | 32 | 16
Memory | Byte-addressable, Little Endian | Byte-addressable, Little Endian
Fewer instructions | 50+ (200 manual pages) | 1000+ (2306 manual pages)
Simpler instruction encoding | 4-byte | Variable length
Simpler instructions | Ld/st instructions load/store memory to or from register Other instructions take only register operands | Instructions take either memory or register operands Complex memory addressing modes D(B, I, S) Prefixes modify instruction behavior
Why RISC-V is much simpler?
similarities

## Slide 6: Basic RISC-V instructions
Data transfer | load doubleword | ld x5, 40(x6) | x5=Memory[x6+40]
 | store doubleword | sd x5, 40(x6) | Memory[x6+40]=x5
Arithmetic Logical | addition | add x5, x6, x7 | x5 = x6 + x7
 | subtraction | sub x5, x6, x7 | x5 = x6 - x7
 | bitwise and | and x5, x6, x7 | x5 = x6 & x7
 | bitwise or | or x5, x6, x7 | x5 = x6 ¦ x7
Conditional Branch | Branch if equal | beq x5, x6, 100 | If (x5==x6) go to PC+100
Registers: x0, x1, x2,…, x31
64-bit

## Slide 7: RISC-V instruction formats
All instructions are 32-bit long
  Several formats encoding operation code (opcode), register numbers …
Opcode determines type of instruction

## Slide 8: R-type: arithmetic logic instructions
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
0
31
 | opcode | funct3 | funct7
add | 0110011 | 000 | 0000000
sub | 0110011 | 000 | 0100000
xor | 0110011 | 100 | 0000000
add x5, x6, x7 // x5=x6+x7
Example R-type instruction:
destination register
specifies which instruction
source register

## Slide 9: I-type: loads and immediate arithmetic
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits
 | opcode | funct3
ld | 0000011 | 011
addi (add immediate) | 0010011 | 000
Example I-type instruction:
ld x5, 40(x6) //x5=Memory[x6+40]
addi x5, x6, 100 // x5=x6+100
specifies which instruction
destination register
source register
Encodes the constant

## Slide 10: S-type: stores
rs2
rs1
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
imm[11:5]
imm[4:0]
 | opcode | funct3
sw (store word) | 0100011 | 010
sd (store doubleword) | 0100011 | 111
split s.t. rs1 and rs2 are always in the same place
Example S-type instruction:
sd x5, 40(x6) //Memory[x6+40]=x5
register storing base memory address
source register
Encodes the constant memory offset

## Slide 11: SB-type: conditional branch
rs2
rs1
funct3
opcode
7 bits
5 bits
5 bits
5 bits
3 bits
Imm[12]
Imm[10:5]
7 bits
Imm[11]
Imm[4:1]
 | opcode | funct3
beq | 1100111 | 000
bne | 1100111 | 001
Immediate encodes a 12-bit signed integer offset.
Branch address is PC+offset*2
Example SB-type instruction:
beq x5, x6, 100 // If (x5==x6) goto PC+2*100

## Slide 12: Instruction Execution
PC  fetch instruction from memory
Register numbers  which register to read/write in register file
Depending on instruction class, do the following:
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch comparison
  Access data memory for load/store
  PC  either target address (branch) or PC + 4

## Slide 13
ld x5, 40(x6)
Data memory
address
data
Instruction Memory
PC
data
address
4
add
x5 = Memory[x6+40]
64-bit register
Register file
ALU
Read-reg-1
Read
Data-1
Read-reg-2
Write-reg
Write-data
Read
data-2

## Slide 14
add x5, x6, x7
Data memory
address
data
Instruction memory
PC
data
address
Register file
ALU
Read-reg-1
Read
data-1
Read-reg-2
Write-reg
Write-data
4
add
x5 = x6 + x7
Read
data-2

## Slide 15
beq x5, x6, 100
Memory
address
data
Memory
PC
data
address
Register file
ALU
Read-reg-1
Read
data-1
Read-reg-2
Write-reg
Write-data
4
add
If (x5==x6) goto PC+2*100
Read
data-2
add

## Slide 16: Instruction Execution
Cannot just join wires together..
Use multiplexers!

## Slide 17: Data path vs. Control

## Slide 18: Building a Datapath
Datapath: elements that process data and addresses in the CPU
  Registers, ALUs, memories, …
We will refine our overview datapath design next…

## Slide 19: R-type Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result

## Slide 20: R-Type/Load/Store Datapath
Input: 32-bit instruction
It selects a 12-bit field in instruction and sign extends to 64-bit

## Slide 21: Full Datapath

## Slide 22: ALU Control
ALU used for
  Load/Store: F = add
  Branch: F = subtract (for comparison)
  R-type: F depends on opcode
ALU control lines | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract

## Slide 23: ALU Control
Assume a “Control” combinatorial logic that outputs 2-bit ALUOp derived from opcode
Build an “ALU Control” combinatorial logic to output ALU control
opcode | ALUOp | Operation | func7 | func3 | ALU function | ALU control
ld | 00 | load register | xxxxxxx | xxx | add | 0010
sd | 00 | store register | xxxxxxx | xxx | add | 0010
beq | 01 | branch on equal | xxxxxxx | xxx | subtract | 0110
R-type | 10 | add | 000000 | 000 | add | 0010
 |  | subtract | 010000 | 000 | subtract | 0110
 |  | AND | 000000 | 111 | AND | 0000
 |  | OR | 000000 | 110 | OR | 0001

## Slide 24: Datapath With Control
Control derived from instruction type

## Slide 25: R-Type Inst
add x5, x6, x7
funct7
rs2
rs1
rd
funct3
opcode

## Slide 26: Load Inst
ld x5, 40(x6)
immediate
rs1
rd
funct3
opcode

## Slide 27: BEQ Instruction
beq x5, x6, 100
rs2
rs1
funct3
opcode

## Slide 28: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary clock period for different instructions
Next lectures: We will improve performance by pipelining